## Slide 1: Trenching and Excavating Safety

## Slide 2
Asphyxiation
Each time a breath is exhaled the weight of the load restricts inhalation of the next breath. Slow suffocation usually follows unless rescue is immediate.
WHAT CAUSES DEATH?

## Slide 3
SOIL WEIGHT?
DEPENDING ON THE DENSITY AND WATER CONTENT:
One cubic yard weighs - 3000lbs or more
One cubic foot weighs - 100lbs or more
3000lbs or more
3 FEET
100lbs or more
1 FOOT

## Slide 4
DYNA
CAVE-INS RESULT FROM:
Vibrations
Adjacent Structures
Freezing and Thawing
The Weight of the Soil Itself
Addition or Removal of Water
Reduction in Frictional and Cohesive Capacities of Soil
THINGS THAT CAN CAUSE CAVE-INS

## Slide 5
HOW DO MOST DEATHS OCCUR?
Instantaneously
Trenches 5 to 15 deep
With absolutely no warning
In seemingly safe conditions
With workers in a bent or lying position

## Slide 6
EVALUATING THE SITE
BEFORE YOU BEGIN EXCAVATION:
The site must be assessed
Potential hazards must be determined
Known hazards reduced or eliminated
Emergency procedures established
Periodic inspection intervals determined
Utility locations must be staked or marked

## Slide 7
SAFETY REQUIREMENTS
Conduct inspections before each work shift
Do not work under elevated loads
Do not work over unprotected employees
Wear proper personal protective equipment
Provide walkways or bridges over trenches
Provide trench exits within 25 feet of workers in trenches more than four feet deep
Ensure spoilage is at least 2 ft. from trench edges

## Slide 8
WHAT TO DO IN AN EMERGENCY
Immediately call 911, or the Emergency Response Team
Report: - Exact Location
- Number of Victims
- Nature of Emergency
- Trench Measurements
- Special Hazards
Keep all life-support and dewatering systems operating
Clear workers away from the excavation
Shut down heavy equipment
Be prepared to meet and brief rescue personnel

## Slide 9
IN AN EMERGENCY
What not to do: - Don’t Panic!
- Control would-be rescuers
- Don’t sacrifice anyone else
- Never attempt to dig someone out
using motorized equipment
Remember - Your actions could save a life!

## Slide 10
PROTECTION METHODS
ACCIDENT PREVENTION METHODS:
Warn and reroute public traffic
Post signs, barricades and flagmen
Mandate use of reflective vests
Warn site traffic
Install protective supports systems

## Slide 11
UNDERGROUND HAZARDS
Utility lines must be located before excavating begins
Utility companies or owners must be contacted:
-- Response times must be considered
-- Advised of the proposed work
-- Questions concerning underground installations
need to be answered

## Slide 12
UNDERGROUND INSTALLATIONS
If no response is given within 24 hours* work can cautiously proceed *(local timeframes may vary ND 48 hours)
Underground installations must be determined by safe and acceptable means
Excavated underground installations must be protected
Never under estimate hazards associated with underground utilities!!!

## Slide 13
TRENCHES MORE THAN 5 FEET UNLESS MADE IN STABLE ROCK:
Require shoring
Or must have a stabilized slope
IN HAZARDOUS SOIL CONDITIONS:
Trenches under 5 feet need protection
TRENCH SAFETY

## Slide 14: CONTROLLING WATER
Adequate Precautions Must Be Taken When Working in Accumulated Water
Controlling Water and Water Removal Must Be Monitored by a Competent Person
Ditches, Dikes or Comparable Means Should Be Used to Prevent Surface Water From Entering Excavations

## Slide 15: SOIL TYPES
TYPE A SOILS
  - Clay
  - Silty Clay
  - Sandy Clay
  - Clay Loam
TYPE B SOILS
  - Granular Cohesionless Soils (Silt Loam)
TYPE C SOILS
  - Gravel
  - Sand
  - Loamy Sand

## Slide 16: HOW TO DETERMINE SOIL TYPES
SOIL CLASSIFICATION MUST BE DONE BY A
COMPETENT PERSON:
Continued
  VISUAL TEST
  Check entire worksite
  Fissured ground
  Layered soil
  Disturbed earth
  Seepage
  Vibration
  Poor drainage

## Slide 17: HOW TO DETERMINE SOIL TYPES
  Manual Test
  Plasticity
  Dry Strength
  Thumb penetration
  Pocket penetrameter
  Hand operated shear vane
  WARNING: One soil inspection and classification may not be enough. Outside disturbances during excavation may change even the best soil classification. Inspect the soil after any change in conditions.

## Slide 18
1926 Subpart P Appendix A – Soil Classification (c) (2)
The classification of the deposits shall be made based on the results of at least one visual and at least one manual analysis

## Slide 19: HOW TO PROTECT PEOPLE
Each employee must be protected from cave-ins by an adequately designed system. Exceptions are:
  Excavations made in stable rock
  Excavations less than 5 feet
Protective systems must have the capacity to resist all loads that are expected to be applied to the system

## Slide 20: BENCHING AND SLOPING
DESIGN OF BENCHING AND SLOPING SYSTEMS:
  OPTION 1 - Allowable configurations and slopes
  OPTION 2 - Determination of slopes and configurations using Appendices A and B
  OPTION 3 - Designs using other tabulated data
  OPTION 4 - Design by a registered professional engineer

## Slide 21: SPOIL PILES
2 FEET MINIMUM
Continued

## Slide 22: BENCHING AND SLOPING
20
FEET
MAX
3/4
1
TYPE A SOILS

## Slide 23: BENCHING AND SLOPING
20
FEET
MAX
1
1
TYPE B SOILS

## Slide 24: SHIELDING
  Shield systems must project at least 18 inches above the lowest point where the excavation face begins to slope

## Slide 25
Unsafe trench
Notes: No sloping or shoring. Previously disturbed soil

## Slide 26
Unsafe trench
Notes: No shoring, previously disturbed soil and the trench is starting to slough.

## Slide 27
Unsafe trench
Notes: Straight up and down sides. Not sloped. No visiable traffic control devices.

## Slide 28
Unsafe trench
Notes: Straight up and down sides.
Spoil pile too close.
Already caving in.
No egress or access points.
No hard hat.

## Slide 29
Unsafe trench
Notes: Improper angle of slope.
Water in trench.
Good example of supporting pipe.

## Slide 30
Unsafe trench
Notes: No sloping.
Not wearing hard hat.
Restricted access to ladder.

## Slide 31
Unsafe trench
Notes: Improper sloping.
Spoil pile too close.
What is with the ladder?
Overburden applied to pipe in background.

## Slide 32
Unsafe trench
Notes: Not properly sloped.
Water in trench bottom.

## Slide 33
Unsafe trench
Notes: Improper sloping.
Person outside trench box.
Trench box not effective.
Too close to excavator.

## Slide 34
Unsafe trench
Notes: Same location as previous slide.
No access.
Spoil piles too close.

## Slide 35
Notes: Good trench

## Slide 36
Notes: Good trench but needs to be engineered because of depth

## Slide 37
Notes: As we see here, a very important part of dumping is the ground itself. Will it hold what it’s going to be subjected to? These cracks are showing us that this ground is not solid. It will not support a heavy truck backing out on the edge. It will collapse.