## Slide 1: OSHA NOTICE & DISCLAIMER
“This material was produced under grant SH20866SH0 from the Occupational Safety and Health Administration, U.S. Department of Labor. It does not necessarily reflect the views or policies of the U.S. Department of Labor, nor does mention of trade names, commercial products, or organizations imply endorsement by the U.S. Government”

## Slide 2: CABLE HIGH LEAD SAFETY (Module #6)
Cable High Lead logging involves specialized equipment.
A skyline is used to support the operation of a carriage which drags logs from below to above.
The skyline is anchored to trees below, and the tower is anchored to trees above.
A mobile truck called a tower contains a winching system which drags the logs.
Specialized jobs called chokers, hook and unhook metal cables on the logs.

## Slide 3: YARDER & GUYLINE TAKEDOWN WHAT YOU NEED TO KNOW 1- the yarder tower is supported by guylines 2- there’s lots of traffic around the yarder 3- guylines are secured, footers are raised, and then the yarder moves

## Slide 4: YARDER & GUYLINE SET-UP WHAT YOU NEED TO KNOW 1- the number of guylines are reset according to each machine’s manufacturer’s requirements and secured with a shackle (sometimes called a clevis) 2- guylines are set as evenly as possible with the top of the tower 3 - 5/8 inch guide wires are used

## Slide 5: TOWER – ANCHOR WIRE SET-UP & SKYLINE RAISE WHAT YOU NEED TO KNOW 1- the tower is secured 2- the anchor wire is set down in the brush or hillside 3- yarders try to find a way to get “deflection” in the line and get it to lift 4- the skyline is attached into the carriage and accepted by signal

## Slide 6: HARDHAT USE
ALWAYS make sure YOUR hardhat is on at all times!
Just remember, HAZARDS are still present, even if a Skyline or high lead is temporarily down.
ALL Job classifications AND VISITORS need to wear hardhats when on a logging site.

## Slide 7: FALL PROTECTION USE FROM ROLLING STOCK – What Do You Need?
What are we talking about? Some DEFINITIONS:
ROLLING STOCK means any vehicle WITH WHEELS that can move around.
FALL PROTECTION means any method that prevents someone from falling from a height. Can include guardrails, or wearing a harness with a self-retracting lanyard.
MINIMUM HEIGHT for protection against falls is ANY distance GREATER or EQUAL TO 4 FEET.

## Slide 8: FALL PROTECTION FROM ROLLING STOCK – QUICK REVIEW
TIE-OFF POINT means any place ON the rolling stock that a person wearing a harness and lanyard can ATTACH TO and SECURE.
GUARD RAILS are Top rails (at 42 inches), Mid Rails (at 21 inches) to prevent falls from heights.
PREVENTION of GREATER HAZARD – means the controls might introduce a hazard that’s WORSE the original hazard.
OSHA “LETTER OF INTERPRETATION” – means the Federal OSHA agency document which interprets how General Industry fall protection requirements apply to rolling stock. This document may be updated at any time, so be sure to consult the latest document issue.

## Slide 9: FALL PROTECTION FROM ROLLING STOCK – QUICK REVIEW (Fed OSHA States)
WHERE can the latest OSHA “LETTER OF INTERPRETATION” on fall protection on rolling stock be found?
It can be found the Fed OSHA website, at:
www.osha.gov/pls/oshaweb/owadisp.show_document?p_table=INTERPRETATIONS&p_id=22278
The “Letter” used for this training was dated October 18, 1996. It was current as of June 1, 2011.

## Slide 10: FALL PROTECTION FROM ROLLING STOCK – QUICK REVIEW
BASICALLY, a lack of FALL PROTECTION might be cited in LOGGING OPERATIONS in 2 WAYS:
#1 – When a General Duty Clause 5(a)(1) citation is issued – for a recognized hazard with no standard. (OSHA’s “Catch-All clause”).
OR
#2 – If the person’s physical ability is not assessed and adequate training has not been received to perform the job safely.
(We’re referring to the Yarder Operator who is exposed to a fall hazard on rolling stock)

## Slide 11: FALL PROTECTION FROM ROLLING STOCK – What It Means for Loggers
YARDER MACHINES are a “Challenge”!
For Tower “Take Down” and “Set Up”, winch controls are AT the tower.
Control mechanism failure can cause the operator to be tangled and hoisted in the guide wires – a Greater hazard than the possible fall!
The YARDER OPERATOR must get to the tower, so the person MUST be able to do this physically demanding job requirement.

## Slide 12: FALL PROTECTION FROM ROLLING STOCK – CONTROL OPTIONS
CHECK YOUR YARDER MACHINE – Does it Have:
1 – A walking surface such as a catwalk, and equipped with Top & Mid Rails?
OR
2 – Several points of Attachment along with:
A Harness & Lanyard attached to an anchorage point OR
A Harness and a self retracting lifeline where the self-retracting lifeline is attached to the D ring on the harness (worn by the YARDER operator)
OR →

## Slide 13: FALL PROTECTION FROM ROLLING STOCK – CONTROL OPTIONS
WERE THE WORK CONDITIONS AND THE YARDER OPERATOR ASSESSED for the following conditions?
A – Are there mitigating conditions such that Yarder operations are conducted near areas where the fall is less than 4 feet, such as, but not limited to a sloped snow bank, or other soft materials that would cushion a fall?
OR
B – Was the Yarder Operator assessed for their physical ability to perform the job?
AND
C – Did the Yarder Operator receive adequate training to perform the job safely?

## Slide 14: AS WE CONTINUE…
The following VIDEO EXAMPLE(s) met the conditions of FALL PROTECTION based on Physical Ability, Received Training, & assessed conditions.
ALL other conditions are site specific and must be assessed on their own merits.
Bear in mind that you must check out and solve FALL PROTECTION issues based on YOUR CONDITIONS and EQUIPMENT…
Let’s get back to CABLE HIGH LEAD SAFETY →

## Slide 15: RAISING THE CARRIAGE & SKYLINE WHAT YOU NEED TO KNOW 1- the skyline is attached to the carriage 2- the Yarder must accept it and signal it 3- a hooker in the brush sets a short drag to test it

## Slide 16: QUICK TEST
Answer Question #1: Which of the following are important in cable high lead logging?
A – properly setting the guylines. B – properly setting the anchor line to get deflection so it lifts. C – checking and rechecking by the yarder operator.
D – all the above.

## Slide 17: QUICK TEST
Answer Question #2: To meet OSHA’s current fall protection requirements from rolling stock, WHAT ACCEPTABLE CONTROL METHODS need to be used ?
A – Catwalks with Top & Mid rails,
B – Several anchorage points on the yarder with:
A Harness & Lanyard attached to an anchorage point OR
A Harness and a self retracting lifeline where the self-retracting lifeline is attached to the D ring on the harness (worn by the YARDER operator)
C – Yarder physical ability gets assessed and the person receives adequate training to safely perform the job,
D – EITHER A, or B And C together.

## Slide 18: EVERY “CHOKER” CONTROLS the CARRIAGE OPERATION WHAT YOU NEED TO KNOW 1- chokers use a device called a bug, which is a radio control 2- communications is huge in high lead! 3- keep clear of MOVING logs!

## Slide 19: CHOKER CARRIAGE CONTROL IN THE BRUSH WHAT YOU NEED TO KNOW 1- the choker controls and uses communications 2- heads up all the time!

## Slide 20: TOWER DOWN FOR SLIPPERY OR SLOPING ROADS WHAT YOU NEED TO KNOW 1- the tower is lowered on slippery or sloping roads 2- guide wires are completely removed from their anchor points 3- stay clear of all guide wires

## Slide 21: TOWER SET-UP IN BAD WEATHER WHAT YOU NEED TO KNOW 1- the crew stays in view 2- stay out of the yarder’s way 3- good three point of contact driver exit 4- the levelers are set and the tower is raised.

## Slide 22: THE YARDER OPERATOR’S JOB WHAT YOU NEED TO KNOW 1- inspect the guide wire rigging 2- check the tower-don’t allow any crossed wires 3- the yarder communicates frequently with the chokers

## Slide 23: TOWER-CHOKER COMMUNICATION WHAT YOU NEED TO KNOW 1- the choker lines up the drag with the carriage and skyline 2- frequent communications by signal with the yarder

## Slide 24: QUICK TEST
Answer this question: What does the choker job involve?
A – controlling the carriage device with the radio operated “Bug”.
B – communicating with the yarder.
C – properly setting the chokers, AND watching for overhead hazards!
D – all the above.

## Slide 25: WRAP-UP
Cable high lead logging involves overhead wires under tension.
Overhead hazards exist due to movement of logs and the carriage.
Chokers and leads may be moving and may be present anywhere.
Communication and coordination of activity is extremely important!

## Slide 26: OSHA NOTICE & DISCLAIMER
“This material was produced under grant SH20866SH0 from the Occupational Safety and Health Administration, U.S. Department of Labor. It does not necessarily reflect the views or policies of the U.S. Department of Labor, nor does mention of trade names, commercial products, or organizations imply endorsement by the U.S. Government”