## Slide 1
This material was produced under grant number SH-22316-SH-1 from the Occupational Safety and Health Administration, U.S. Department of Labor. It does not necessarily reflect the views or policies of the U.S. Department of Labor, nor does mention of trade names, commercial products, or organizations imply endorsement by the U.S. Government.
Failure Mode Effects Analysis (FMEA)
Presented By The University of Texas-School of Public Health

## Slide 2: Learning Objectives
By the end of this module participants should be able to:
  Identify the definition of Failure Mode And Effects Analysis (FMEA)
  Describe how to apply FMEA in the procedure of design, process, and project.
  Identify the terminology of failure mode, effect and cause, severity, occurrence, detection, and current controls.
  Select the appropriate methods and strategies to apply Failure Mode And Effects Analysis (FMEA) in the hospital nurse unit.
  Develop a completed FMEA using Risk Priority Numbers (RPNs) in the hospital nurse unit.

## Slide 3: The DMAIC Process with Tools
Define
Measure
Analyze
Improve
Control
3&4
Phase
Tools:
FMEA
Quick Wins 5S
The 8 Wastes
DAY 2

## Slide 4: What Is an FMEA?
A structured approach to:
  Identify the ways in which a product or process can fail
  Estimate the risk associated with specific causes
  Prioritize the actions that should be taken to reduce the risk
A Process FMEA will:
  Capture the entire process and the key inputs (Xs)
  Identify ways the product or process can fail because of these Xs
  Facilitate the documentation of a plan to prevent those failures

## Slide 5: Applications For FMEA
  Design:
  Used to analyze product designs before they are released to production. A DFMEA should always be completed well in advance of a prototype build. Focuses on product function.
  Process:
  Used to analyze manufacturing, assembly, or any other processes. Focuses on process inputs. This is the topic for this module.
  Project:
  Documents and addresses failures that could happen during a major
  program

## Slide 6
PAPERWORK
TURN STEAM ON
TO DICY TANK
LOAD DMF
LOAD DICY
LOAD 2MI
1
BILL OF MATERIALS
ISO PROCEDURES
REWORK
SCALE ACCURACY
PREHEATING
LOAD ACCURACY
CLEANLINESS
RAW MATERIAL
LOAD ACCURACY
ENVIRONMENT
(HUMIDITY)
RAW MATERIAL
MIXER SPEED
LOAD ACCURACY
ENVIRONMENT
(HUMIDITY)
RAW MATERIAL
MIXER SPEED
Key Source Material For An FMEA
Process Map
FMEA

## Slide 7: The FMEA Form The Analysis Section
What is the Process Step
What can go wrong with the Process Step?
What is the Effect on the Outputs?
What are the Potential Causes?
How serious is such an Effect?
How often is the cause likely to occur and result in a Failure Mode?
How can this be found?
If risk is too high, what can be done?
How well can we detect a cause before it creates a Failure Mode and Effect?
Process
Step/
Input
Potential
Failure
Mode
Potential
Failure
Effects
Potential
Causes
Current
Controls
S
E
V
D
E
T
O
C
C
R
P
N
Estimated risk is “Sev” x “Occ” x “Det”
Current
Controls
Action
Section

The FMEA Form - The Analysis Section

## Slide 8: Definition Of Terms – Failure Mode
Failure Mode: The way in which a specific process input fails
  If it is not detected and either corrected or removed, it may cause a negative “Effect” to occur
  Can be associated with a defect (in discrete manufacturing) or a process input variable that goes outside of specification
    Anything that an operator can see that’s wrong is considered a Failure Mode
    Note 1: Just because a dimension is out of spec (a Failure Mode), it does not imply with 100% certainty that the product will not function (an effect)
    Note 2: Just because the process is improperly setup (a failure cause), it does not imply with 100% certainty that the dimension will be out of spec (a Failure Mode)

## Slide 9: Definition Of Terms – Effect And Cause
Effect: The adverse impact on customer requirements. Generally has an external customer focus, but can also include downstream processes.
  A product or process that does not perform satisfactorily to design
Cause: Whatever causes the Failure Mode to occur. How a specific part of the process (operation or component) can cause a Failure Mode.
  A worn spindle (cause) may cause a dimension to be out of tolerance (mode) which may cause the part to not fit (effect)

## Slide 10: Definition Of Terms – Severity, Occurrence, And Detection
Severity: An assessment of how serious the Failure Effect (due to the Failure Mode) is to the customer
Occurrence: An assessment of the likelihood that a particular Cause will happen and result in the Failure Mode
Detection: An assessment of the likelihood that the current controls will detect the Cause of the Failure Mode or the Failure Mode itself, should it occur, thus preventing the Failure Effect from reaching your customer. The customer in this case could be the next operation, subsequent operations, or the end user

## Slide 11: Definition Of Terms – Current Controls
Current Controls: Systematized methods/devices in place to prevent or detect failure Modes or Causes (before causing effects)
  Prevention-based controls may include Mistake Proofing, automated controls, setup verifications, Preventive Maintenance, and Control Charts
  Detection-based controls may include audits, checklists, inspection, laboratory testing, and Control Charts

## Slide 12: Rating Definitions Typical Scales
High 10
Low 1
Rating
Severity | Occurrence | Detection
Hazardous without warning | Very high and almost inevitable | Cannot detect
Loss of primary function | High repeated failures | Low chance of detection
Loss of secondary function | Moderate failures | Moderate chance of detection
Minor effect | Occasional failures | Good chance of detection
No effect | Failure unlikely | Almost certain detection
Note : Determine if your company has rating scales and rules. In some companies, rating a “10” on severity may have legal consequences.
Severity
Occurrence
Detection

## Slide 13: Risk Priority Number (RPN)
A key output of an FMEA is the “Risk Priority Number”
The RPN is a calculated number based on information you provide regarding:
  The likelihood of potential causes of Failure Modes
  The seriousness of the resulting effects
  The current ability of the process to detect the causes of the Failure Modes before they cause an effect to reach a customer
It is calculated as the product of three (3) ratings, each one related to the severity, frequency, and detect ability
RPN = Severity x Occurrence x Detection Regardless of RPN, high severity scores should be given special attention.

## Slide 14: Risk Priority Numbers (2)
The Risk Priority Number need not be limited to Severity, Occurrence, and Detection.
Some examples:
  Add an “Impact” score to estimate the overall impact of the Failure Mode on the process (10 = high, 1 = low)
  Add an “EHS” rating to a project FMEA to incorporate possible environmental impact (10 = high, 1 = low)
  Add an “EOC” or Ease Of Completion (10 = easy, 1= hard) to help prioritize/focus projects

## Slide 15: Comments On Detection Scores
Cause
Failure Mode
(Defect)
Effect
High detection scores imply that we will not easily catch the existence of a Failure Cause until after the resulting Failure Mode creates a Failure Effect. Usually, this means that we detect the effect at the end of the line or, even worse, our customer finds it.
A very low detection score generally implies that you catch the cause before it creates the Failure Mode.
Low Det Score
Virtually certain Prevention
High Det Score
Virtually no Prevention

## Slide 16
FMEA Model
Cause
Faculty inverter
High particle count
Temp controller out
Drill not properly
Part not clamped
Drill not properly sharpened
Mode
Agitator too slow
Pits
Temp too high of calibration
Hole not drilled sharpened
Hole not drilled square in fixture
Hole not drilled
Effect
Extractable too high
Internal opens on printed circuit in clean room
Conversion rate too low
Part will not assemble straight
Part will not assemble straight
Part will not assemble to proper diameter
Cause
Mode
Effect
Notes: Lets come up with some Healthcare examples here…

## Slide 17
Failure Mode 1
Failure Mode 2
Effect 1
Failure Mode 1
Effect 1
Effect 2
Failure Mode 1
Failure Mode 2
Effect 1
Linking Failure Modes To Effects Note: The Last Three (3) Examples On Prior Slide
Effect 2
Note that the relationship between the Failure Mode and the Effect is not always 1-to-1.

## Slide 18
A Second Look At The Analysis Section File: FMEA_Form.XLS
Process or
Product
Name:
Prepared by:
Page ____ of ____
Responsible:
Process Step
Key
Process
Input
Potential Failure
Mode
Potential Failure
Effects
S
E
V
Potential Causes
O
C
C
Current Controls
D
E
T
R
P
N
What is the
process step
What is the
Key
Process
Input?
In what ways
does the Key
Input go wrong?
What is the impact
on the Key Output
Variables (Customer
Requirements) or
internal
requirements?
How Severe is the effect
to the customer?
What causes the
Key Input to go
wrong?
How often does cause or
FM occur?
What are the existing
controls and procedures
(inspection and test) that
prevent either the cause
or the Failure Mode?
Should include an SOP
number.
How well can you detect
cause or FM?
Sev x Occ x Det
0
0
FMEA Date (Orig) ______________ (Rev) _____________
Process/Product - FMEA
Failure Modes and Effects Analysis

## Slide 19
The FMEA Form The Action Section
Actions
Taken
Actions
Recommended
Responsibility
S
E
V
D
E
T
O
C
C
R
P
N
Analysis
Section

R
P
N

## Slide 20: 9 Strategies To Complete An FMEA
  For each Process Input, determine the ways in which the Process Step can go wrong (Failure Modes)
  For each Failure Mode associated with the inputs, determine Effects
  Identify potential Causes of each Failure Mode
  List the Current Controls for each Cause
  Assign Severity, Occurrence, and Detection ratings to each Cause
  Calculate RPN
  Determine Recommended Actions to reduce High RPNs
  Take appropriate actions and document
  Recalculate RPNs
Notes: SK: Changed the title

## Slide 21
Getting Started
Utilize Process Maps, C&E Diagrams, C&E Matrices, data collection, warranty analysis, testing, and other pertinent information
Select people from functions both upstream and downstream from the process under analysis
  Engineering
  Manufacturing
  Maintenance
  Tooling
  Quality Assurance
  Marketing
  Suppliers
  Health, Safety, and Environment (HSE)

## Slide 22: Exercise # 1: The FMEA Analysis
Notes: Provide FMEA Excel files to exercise

## Slide 23
Practical Tips for FMEA
Do not try FMEA alone, it is a group activity
FMEA, done right, may be a time consuming process
Activities are required for completion, it is not just a paperwork
activity
The team will likely need training and coaching
Prepare properly for meetings
Summarize often
Make sure voting is independent (suggest anonymous ballots)
Negotiate issues
Notes: SK: Changed the title

## Slide 24: Summary
Failure modes and effects analysis (FMEA) is a step-by-step approach for identifying all possible failures in a design, a manufacturing or assembly process, or a product or service.
A key output of an FMEA is the “Risk Priority Number.”

## Slide 25: Thank You