## Slide 1: Introduction to the Global Harmonization System, GHS
Institute of Occupational Safety and Health

## Slide 2: FY-13 OSHA Susan Harwood Grant Program
This material was produced under grant number SH-23563-12-60-F-12 from OSHA. It does not necessarily reflect the views or policies of the U.S. Department of Labor, nor does mention of trade names, commercial products, or organizations imply endorsement by the U.S. Government.
Notes: What does OSHA do?
OSHA employs the following strategies to help employers and employees reduce injuries, illnesses, and deaths on the job:
Enforcement – making sure OSHA Regulations are followed
Assistance – outreach & training to employers and employees
Cooperation – partnerships and alliances through voluntary programs
OSHA promotes workplace safety and health by:
Implementing new (or improved) safety and health management systems.
Completing worksite inspections. Companies failing to OSHA Regulations may be cited and/or fined.
Promoting cooperative programs including Voluntary Protection Programs, OSHA Strategic Partnerships, and other industry Alliances.
Establishing specific rights and responsibilities of employees and employers.
Supporting innovation in dealing with workplace hazards.
Establishing recordkeeping and reporting requirements for employers.
Developing training programs for occupational safety and health personnel.
Partnering with states that operate their own occupational safety and health programs.
Supporting the OSHA Consultation Program.

## Slide 3: OSHA Cares

## Slide 4: Objectives: Participants will:
  Define the background of the Global Harmonization System, GHS
  Explain how the GHS will be applied
  Describe OSHA’s modifications to the Hazard Communication Standard, HCS
  Identify OSHA’s timeline for GHS implementation
  Compare, Contrast & Identify OSHA GHS Labeling and Warning systems
  Distinguish the differences between the MSDS & the GHS Safety Data Sheet, SDS

## Slide 5: What is the GHS?
"Globally Harmonized System of Classification and Labeling of Chemicals," commonly referred to as The Purple Book.
Notes: The Globally Harmonized System (GHS) is an international approach to hazard communication, providing agreed criteria for classification of chemical hazards, and a standardized approach to label elements and safety data sheets. The GHS was negotiated in a multi-year process by hazard communication experts from many different countries, international organizations, and stakeholder groups. It is based on major existing systems around the world, including OSHA's Hazard Communication Standard and the chemical classification and labeling systems of other US agencies.
The result of this negotiation process is the United Nations' document entitled "Globally Harmonized System of Classification and Labeling of Chemicals," commonly referred to as The Purple Book. This document provides harmonized classification criteria for health, physical, and environmental hazards of chemicals. It also includes standardized label elements that are assigned to these hazard classes and categories, and provide the appropriate signal words, pictograms, and hazard and precautionary statements to convey the hazards to users. A standardized order of information for safety data sheets is also provided. These recommendations can be used by regulatory authorities such as OSHA to establish mandatory requirements for hazard communication, but do not constitute a model regulation.

## Slide 6: What is the GHS?
Based on major existing worldwide systems, including the OSHA HAZCOM
  Harmonized classification criteria for health, physical, and environmental hazards of chemicals
  Standardized labelling
  Signal words, pictograms, precautionary statements
  A standardized order of information for safety data sheets, SDS
Notes: A standardized order of information for safety data sheets is also provided. These recommendations can be used by regulatory authorities such as OSHA to establish mandatory requirements for hazard communication, but do not constitute a model regulation.

## Slide 7: How is the GHS to be applied?
Are all chemical covered under the GHS?
Notes: The GHS Classification and Communication elements are the foundation of programs to ensure the safe use of chemicals, as shown in Figure 2.1. The first two steps in any program to ensure the safe use of chemicals are to identify intrinsic hazard(s) (i.e., classification) and then to communicate that information. The design of the GHS communication elements reflect the different needs of various target audiences, such as workers and consumers. To proceed further up the pyramid, some existing national programs also include risk management systems as part of an overall program on the sound management of chemicals. The general goal of these systems is to minimize exposure, resulting in reduced risk. The systems vary in focus and include activities such as establishing exposure limits, recommending exposure monitoring methods and creating engineering controls. However, the target audiences of such systems are generally limited to workplace settings. With or without formal risk management systems, the GHS is designed to promote the safe use of chemicals.
2.1 Are all chemicals covered by the GHS? The GHS covers all hazardous chemicals. There are no complete exemptions from the scope of the GHS for a particular type of chemical or product. The term "chemical" is used broadly to include substances, products, mixtures, preparations, or any other terms that may be used by existing systems. The goal of the GHS is to identify the intrinsic hazards of chemical substances and mixtures and to convey hazard information about these hazards. The GHS is not intended to harmonize risk assessment procedures or risk management decisions, as described above. "Articles" as defined in the OSHA Hazard Communication Standard (HCS) (29 CFR 1910.1200), or by similar definitions, are outside the scope of the GHS. Chemical inventory (e.g., TSCA, EINECS, etc.) and chemical control requirements in various countries are not harmonized by the GHS.Classification in the GHS is criteria-based, not limiting coverage to a list that can become outdated. It is not anticipated that the GHS will develop or maintain an international classification authority or international classification list. Several countries currently maintain regulatory lists. GHS classification criteria can be used to reclassify chemicals on lists, if desired. Existing lists, such as those provide by organizations that evaluate cancer hazards, could be used in conjunction with the GHS to promote harmonization.

## Slide 8: How is the GHS to be applied?
  Will all hazardous chemicals require a GHS label and Safety Data Sheet?
Now called a
Safety Data Sheet
Notes: The need for GHS labels and/or Safety Data Sheets is expected to vary by product category or stage in the chemical's lifecycle from research/production to end use. The sequence of lifecycle events is shown in Figure 2.2. For example, pharmaceuticals, food additives, cosmetics and pesticide residues in food will not be covered by the GHS at the point of consumption, but will be covered where workers may be exposed (workplaces), and in transport. Also, the medical use of human or veterinary pharmaceuticals is generally addressed in package inserts and is not part of existing hazard communication systems. Similarly, foods are generally not labeled under existing hazard communication systems. The exact requirements for labels and Safety Data Sheets will continue to be defined in national regulations. However, national requirements are expected to be consistent with the detailed discussion of scope provided in Chapter 1.1 of the GHS document.

## Slide 9: How is the GHS to be applied?
  How will the GHS impact existing regulations?
  GHS building blocks
Notes: 2.3 How will the GHS impact existing regulations? The GHS is a voluntary international system that imposes no binding treaty obligations on countries. To the extent that countries adopt the GHS into their systems, the regulatory changes would be binding for covered industries. For countries with existing systems, it is expected that the GHS components will be applied within the framework/infrastructure of existing hazard communication regulatory schemes. For example, exceptions and exemptions found in existing regulations would not be expected to change (e.g., transportation of limited quantities). However, the specific hazard criteria, classification processes, label elements and SDS requirements within an existing regulation will need to be modified to be consistent with the harmonized elements of the GHS. It is anticipated that ALL existing hazard communication systems will need to be changed in order to apply the GHS. For example, in the U.S. EPA and OSHA would be expected to require hazard pictograms/symbols on labels. Canada and the EU would be expected to adopt the GHS pictograms/symbols instead of those currently in use. The transport sector is expected to adopt the changed criteria (LD50/LC50) for the GHS Acute Toxicity Categories 1 - 3. OSHA HCS, WHMIS and the EU would all need to change their acute toxicity criteria. Test data already generated for the classification of chemicals under existing systems should be accepted when classifying these chemicals under the GHS, thereby avoiding duplicative testing and the unnecessary use of test animals.
2.4 What is meant by GHS Building Blocks? The GHS classification and communication requirements can be thought of as a collection of building blocks. In regulatory schemes, coverage and communication of hazards vary by the needs of target audiences/sectors. Accordingly, the GHS was designed to contain the hazard endpoints and communication tools necessary for application to known regulatory schemes. The GHS is structured so that the appropriate elements for classification and communication, which address the target audiences, can be selected. The full range of harmonized elements is available to everyone, and should be used if a country or organization chooses to cover a certain effect when it adopts the GHS. The full range of these elements does not have to be adopted. Countries can determine which of the building blocks will be applied in different parts of their systems (consumer, workplace, transport, pesticides, etc.). For example, some options for implementing the GHS include: Not using a GHS class (e.g., cancer, hazardous to the aquatic environment, etc.);
Not using a GHS category (normally at the beginning or end of a class, e.g., Acute Toxicity Cat. 5);
Combining categories (e.g., Acute Toxicity Cat.# 1 and Cat.# 2; Skin Corrosion Cat.1A, 1B and 1C).
2.5 How should the GHS Building Blocks by applied? Appropriate implementation of the GHS means that the hazards covered by a Competent Authority (CA) are covered consistently with the GHS criteria and requirements. The EPA, Health Canada and OSHA are examples of Competent Authorities. Competent Authorities will decide how to apply the various elements of the GHS based on the CA needs and the needs of target audiences. When a regulatory scheme covers something that is in the GHS, and implements the GHS, that coverage should be consistent. Once an endpoint and subclasses are selected, as needed, the GHS classification criteria, assigned label elements and SDS provisions should be followed as specified in the GHS. If a regulatory system covers carcinogenicity, for example, it should follow the harmonized classification scheme, the harmonized label elements and, where appropriate, the SDS. Figure 2.3 shows some of the hazard endpoint/subcategory and hazard communication building block choices for the transport, workplace, consumer and pesticide sectors.

## Slide 10: How is the GHS to be applied?
  To gain a better understanding of the building block approach, it is helpful to look at the specific sectors/target audiences
    Transport
    Workplace
    Consumer
    Pesticides
Notes: 2.5.1 Transport For transport, it is expected that application of the GHS will be similar to application of current transport requirements. GHS physical, acute and environmental hazard criteria are expected to be adopted in the transport sector.
Containers of dangerous goods will have pictograms that address acute toxicity, physical hazards, and environmental hazards.
GHS hazard communication elements such as signal words, hazard statements and SDS are not expected to be adopted in the transport sector.
2.5.2 Workplace In the workplace, it is expected that most of the GHS elements will be adopted, including;·GHS physical and health hazard criteria, as appropriate;
Labels that have the harmonized core information under the GHS (signal words, hazard statements and symbols, etc.);
Safety Data Sheets;
Employee training to help ensure effective communication is also anticipated;
All workplace systems may not have the jurisdiction to adopt environmental hazards. 2.5.3 Consumer For the consumer sector, it is expected that labels will be the primary focus of GHS application.·The appropriate GHS hazard criteria are expected to be adopted;
These labels will include the core elements of the GHS (signal words, hazard statements and symbols, etc.), subject to some sector-specific considerations in certain systems (e.g., risk-based labelling).
2.5.4 Pesticides For pesticides, it is expected that the GHS will be adopted.The appropriate GHS hazard criteria are expected to be adopted;
Pesticide labels will include the core elements of the GHS (signal words, hazard statements and symbols, etc.), subject to some sector-specific considerations in certain systems.

## Slide 11: Phase-in period in the revised Hazard Communication Standard
Effective Completion Date | Requirement(s) | Who
December 1, 2013 | Train employees on the new label elements and safety data sheet (SDS) format. | Employers
June 1, 2015* December 1, 2015 | Compliance with all modified provisions of this final rule, except: The Distributor shall not ship containers labeled by the chemical manufacturer or importer unless it is a GHS label | Chemical manufacturers, importers, distributors and employers
June 1, 2016 | Update alternative workplace labeling and hazard communication program as necessary, and provide additional employee training for newly identified physical or health hazards. | Employers
Transition Period to the effective completion dates noted above | May comply with either 29 CFR 1910.1200 (the final standard), or the current standard, or both | Chemical manufacturers, importers, distributors, and employers
Notes: *This date coincides with the EU implementation date for classification of mixtures
During the phase-in period, employers would be required to be in compliance with either the existing HCS or the revised HCS, or both. OSHA recognizes that hazard communication programs will go through a period of time where labels and SDSs under both standards will be present in the workplace. This will be considered acceptable, and employers are not required to maintain two sets of labels and SDSs for compliance purposes.
OSHA is requiring that employees are trained on the new label elements (i.e., pictograms, hazard statements, precautionary statements, and signal words) and SDS format by December 1, 2013, while full compliance with the final rule will begin in 2015. OSHA believes that American workplaces will soon begin to receive labels and SDSs that are consistent with the GHS, since many American and foreign chemical manufacturers have already begun to produce HazCom 2012/GHS-compliant labels and SDSs. It is important to ensure that when employees begin to see the new labels and SDSs in their workplaces, they will be familiar with them, understand how to use them, and access the information effectively. For more information,http://www.osha.gov/dsg/hazcom/effectivedates.html.

## Slide 12: Revised OSHA HAZCOM Standard, HCS
  Why did OSHA decide to modify the Hazard Communication Standard to adopt the GHS
    Improve safety and health of workers through effective communications on chemical hazards
      Reduce confusion by enforcing a standardized approach to include:
        Global classification
        Measures to determine of chemical hazards
        SDS
        Labels and
Notes: OSHA has modified the Hazard Communication Standard (HCS) to adopt the GHS to improve safety and health of workers through more effective communications on chemical hazards. Since it was first promulgated in 1983, the HCS has provided employers and employees extensive information about the chemicals in their workplaces. The original standard is performance-oriented, allowing chemical manufacturers and importers to convey information on labels and material safety data sheets in whatever format they choose. While the available information has been helpful in improving employee safety and health, a more standardized approach to classifying the hazards and conveying the information will be more effective, and provide further improvements in American workplaces. The GHS provides such a standardized approach, including detailed criteria for determining what hazardous effects a chemical poses, as well as standardized label elements assigned by hazard class and category. This will enhance both employer and worker comprehension of the hazards, which will help to ensure appropriate handling and safe use of workplace chemicals. In addition, the safety data sheet requirements establish an order of information that is standardized. The harmonized format of the safety data sheets will enable employers, workers, health professionals, and emergency responders to access the information more efficiently and effectively, thus increasing their utility.
Adoption of the GHS in the US and around the world will also help to improve information received from other countries—since the US is both a major importer and exporter of chemicals, American workers often see labels and safety data sheets from other countries. The diverse and sometimes conflicting national and international requirements can create confusion among those who seek to use hazard information effectively. For example, labels and safety data sheets may include symbols and hazard statements that are unfamiliar to readers or not well understood. Containers may be labeled with such a large volume of information that important statements are not easily recognized. Given the differences in hazard classification criteria, labels may also be incorrect when used in other countries. If countries around the world adopt the GHS, these problems will be minimized, and chemicals crossing borders will have consistent information, thus improving communication globally.

## Slide 13: Major changes to the Hazard Communication Standard
Three major change are:
  Hazard classification:
    Definitions of hazards will provide criteria for:
      Health & physical hazards
      Classification of mixtures
  2. Labels:
    Manufacturers & importers will provide labels to include signal word, pictogram, and hazard statement for hazard class & category.
    Precautionary statements
  3. Safety Data Sheets: Specified 16-section format
Notes: A. The three major areas of change are in hazard classification, labels, and safety data sheets.
Hazard classification: The definitions of hazard have been changed to provide specific criteria for classification of health and physical hazards, as well as classification of mixtures. These specific criteria will help to ensure that evaluations of hazardous effects are consistent across manufacturers, and that labels and safety data sheets are more accurate as a result.
Labels: Chemical manufacturers and importers will be required to provide a label that includes a harmonized signal word, pictogram, and hazard statement for each hazard class and category. Precautionary statements must also be provided.
Safety Data Sheets: Will now have a specified 16-section format.
The GHS does not include harmonized training provisions, but recognizes that training is essential to an effective hazard communication approach. The revised Hazard Communication Standard (HCS) requires that workers be re- trained within two years of the publication of the final rule to facilitate recognition and understanding of the new labels and safety data sheets.
For a side-by-side comparison of the current HCS and the final revised HCS please see OSHA's hazard communication safety and health topics webpage at:http://www.osha.gov/dsg/hazcom/index.html

## Slide 14: HCS Pictograms and Hazards
Pictogram: symbol & other graphics, such as a border, pattern, or color that should convey facts about the hazard
Signal words: indicate the relative level of severity of the hazard and alert the reader to a potential hazard on the label
Hazard Statement: describes the nature of the hazard of a chemical, including, where appropriate, the degree of hazard.
Precautionary Statement: recommended measures to be taken to minimize or prevent adverse effects
Notes: Under the current Hazard Communication Standard (HCS), the label preparer must provide the identity of the chemical, and the appropriate hazard warnings. This may be done in a variety of ways, and the method to convey the information is left to the preparer. Under the revised HCS, once the hazard classification is completed, the standard specifies what information is to be provided for each hazard class and category. Labels will require the following elements:
Pictogram: a symbol plus other graphic elements, such as a border, background pattern, or color that is intended to convey specific information about the hazards of a chemical. Each pictogram consists of a different symbol on a white background within a red square frame set on a point (i.e. a red diamond). There are nine pictograms under the GHS. However, only eight pictograms are required under the HCS.
Signal words: a single word used to indicate the relative level of severity of hazard and alert the reader to a potential hazard on the label. The signal words used are "danger" and "warning." "Danger" is used for the more severe hazards, while "warning" is used for less severe hazards.
Hazard Statement: a statement assigned to a hazard class and category that describes the nature of the hazard(s) of a chemical, including, where appropriate, the degree of hazard.
Precautionary Statement: a phrase that describes recommended measures to be taken to minimize or prevent adverse effects resulting from exposure to a hazardous chemical, or improper storage or handling of a hazardous chemical.

## Slide 15: HCS Pictograms and Hazards
Health Hazard | Flame | Exclamation Mark
• Carcinogen • Mutagenicity • Reproductive Toxicity • Respiratory Sensitizer • Target Organ Toxicity • Aspiration Toxicity | • Flammables • Pyrophorics • Self-Heating • Emits Flammable Gas • Self-Reactives • Organic Peroxides | • Irritant (skin and eye) • Skin Sensitizer • Acute Toxicity (harmful) • Narcotic Effects • Respiratory Tract Irritant • Hazardous to Ozone Layer (Non Mandatory)
Gas Cylinder | Corrosion | Exploding Bomb
• Gases under Pressure | • Skin Corrosion/ burns • Eye Damage • Corrosive to Metals | • Explosives • Self-Reactives • Organic Peroxides
Flame over Circle | Environment (Non Mandatory) | Skull and Crossbones
• Oxidizers | • Aquatic Toxicity | • Acute Toxicity (fatal or toxic)
Notes: Instructor Notes:
There are nine pictograms under the GHS to convey the health, physical and environmental hazards. The final Hazard Communication Standard (HCS) requires eight of these pictograms, the exception being the environmental pictogram, as environmental hazards are not within OSHA's jurisdiction. The hazard pictograms and their corresponding hazards are shown on this slide.
Pont out the red borders and explain the reasoning.
Under the revised Hazard Communication Standard (HCS), pictograms must have red borders. OSHA believes that the use of the red frame will increase recognition and comprehensibility. Therefore, the red frame is required regardless of whether the shipment is domestic or international.
Will OSHA allow blank red borders?
A. The revised Hazard Communication Standard (HCS) requires that all red borders printed on the label have a symbol printed inside it. If OSHA were to allow blank red borders, workers may be confused about what they mean and concerned that some information is missing. OSHA has determined that prohibiting the use of blank red borders on labels is necessary to provide the maximum recognition and impact of warning labels and to ensure that users do not get desensitized to the warnings placed on labels.

## Slide 16: Updating Label Information
Chemical manufacturers, importers, distributors, or employers who become newly aware of hazard information shall revise the labels for the chemical within six months
If the chemical is not currently produced or imported, the same group shall add the data to the label before the chemical is shipped or taken to into the workplace
Notes: How will workplace labeling provisions be changing under the revised Hazard Communication Standard?
A. The current standard provides employers with flexibility regarding the type of system to be used in their workplaces and OSHA has retained that flexibility in the revised Hazard Communication Standard (HCS). Employers may choose to label workplace containers either with the same label that would be on shipped containers for the chemical under the revised rule, or with label alternatives that meet the requirements for the standard. Alternative labeling systems such as the National Fire Protection Association (NFPA) 704 Hazard Rating and the Hazardous Material Identification System (HMIS) are permitted for workplace containers. However, the information supplied on these labels must be consistent with the revised HCS, e.g., no conflicting hazard warnings or pictograms.

## Slide 17: Safety Data Sheet (SDS) changes under the revised Hazard Communication Standard
Section 1 Section 2 Section 3 Section 4 Section 5 Section 6 Section 7 Section 8 | Identification Hazard(s) identification Composition/information on ingredients First-Aid measures Fire-fighting measures Accidental release measures Handling and storage Exposure controls/personal protection | Section 9 Section 10 Section 11 Section 12 Section 13 Section 14 Section 15 Section 16 | Physical and chemical properties Stability and reactivity Toxicological information Ecological information Disposal considerations Transport information Regulatory information Other information
Notes: The information required on the safety data sheet (SDS) will remain essentially the same as that in the current standard (HazCom 1994). HazCom 1994 indicates what information has to be included on an SDS, but does not specify a format for presentation or order of information. The revised Hazard Communication Standard (HazCom 2012) requires that the information on the SDS be presented using specific headings in a specified sequence.
Paragraph (g) of the final rule provides the headings of information to be included on the SDS and the order in which they are to be provided. In addition, Appendix D provides the information to be included under each heading. The SDS format is the same as the ANSI standard format which is widely used in the U.S. and is already familiar to many employees.
The SDS must also contain Sections 12-15, to be consistent with the United Nations' Globally Harmonized System of Classification and Labeling of Chemicals (GHS). Although the headings for Sections 12-15 are mandatory, OSHA will not enforce the content of these four sections because these sections are within other agencies' jurisdictions.

## Slide 18: HCS Pictograms and Hazards Quiz
1. What does this stand for? | 2. What does this stand for? | 3. What does this stand for?
Name a hazard | Name a hazard | Name a hazard
4. What does this stand for? | 5. What does this stand for? | 6. What does this stand for?
Name a hazard | Name a hazard | Name a hazard
7. What does this stand for? | 8. What does this stand for? | 9. What does this stand for?
Name a hazard | Name a hazard | Name a hazard
Notes: Instructor Notes:
There are nine pictograms under the GHS to convey the health, physical and environmental hazards. The final Hazard Communication Standard (HCS) requires eight of these pictograms, the exception being the environmental pictogram, as environmental hazards are not within OSHA's jurisdiction. The hazard pictograms and their corresponding hazards are shown on this slide.
Pont out the red borders and explain the reasoning.
Under the revised Hazard Communication Standard (HCS), pictograms must have red borders. OSHA believes that the use of the red frame will increase recognition and comprehensibility. Therefore, the red frame is required regardless of whether the shipment is domestic or international.
Will OSHA allow blank red borders?
A. The revised Hazard Communication Standard (HCS) requires that all red borders printed on the label have a symbol printed inside it. If OSHA were to allow blank red borders, workers may be confused about what they mean and concerned that some information is missing. OSHA has determined that prohibiting the use of blank red borders on labels is necessary to provide the maximum recognition and impact of warning labels and to ensure that users do not get desensitized to the warnings placed on labels.

## Slide 19: Estimated Impact by the Revised HCS
OSHA estimates over 5 million workplaces in the United States would be affected
The revised Hazard Communications Standard's (HCS) total cost, an estimated $201 million a year for the entire United States
  Classifying chemical hazards: $22 million
  Training: $94 million
  Management familiarization: $59 million
  Printing packaging & labels: #24 million
Notes: OSHA estimates that over 5 million workplaces in the United States would be affected by the revised Hazard Communication Standard (HCS). These are all those workplaces where employees—a total of approximately 43 million of them—could be exposed to hazardous chemicals. Included among these 5 million workplaces are an estimated 90,000 establishments that create hazardous chemicals; these chemical producers employ almost 3 million workers.
Q: What are the estimated overall costs for industry to comply with the revised Hazard Communication Standard?
A: The revised Hazard Communications Standard's (HCS) total cost, an estimated $201 million a year on an annualized basis for the entire United States, is the sum of four major cost elements. (1) OSHA estimates that the cost of classifying chemical hazards in accordance with the GHS criteria and revising safety data sheets and labels to meet new format and content requirements would be $22.5 million a year on an annualized basis. (2) OSHA estimates that training for employees to become familiar with new warning symbols and the revised safety data sheet format under GHS would cost $95.4 million a year on an annualized basis. (3) OSHA estimated annualized costs of $59 million a year for management to become familiar with the new GHS system and to engage in other management-related activities as may be necessary for industry's adoption of GHS. (4) OSHA estimated annualized costs of $24.1 million for printing packaging and labels for hazardous chemicals in color.

## Slide 20: Estimated benefits attributable to the revised Hazard Communication Standard
Increased safety and health:
  OSHA estimates that the revised HCS will result in the prevention of 43 fatalities and 585 injuries and illnesses
How?
  Enable employees exposed to workplace chemicals to more quickly obtain and understand information about chemical hazards
  Expected to improve the use of correct exposure controls and work practices
Notes: OSHA expects that the modifications to the Hazard Communication Standard (HCS) will result in increased safety and health for the affected employees and reduce the numbers of accidents, fatalities, injuries, and illnesses associated with exposures to hazardous chemicals. The GHS revisions to the HCS standard for labeling and safety data sheets would enable employees exposed to workplace chemicals to more quickly obtain and to more easily understand information about the hazards associated with those chemicals. In addition, the revisions to HCS are expected to improve the use of appropriate exposure controls and work practices that can reduce the safety and health risks associated with exposure to hazardous chemicals.
OSHA estimates that the revised HCS will result in the prevention of 43 fatalities and 585 injuries and illnesses (318 non-lost-workday injuries and illnesses, 203 lost-workday injuries and illnesses, and 64 chronic illnesses) annually. The monetized value of this reduction in occupational risks is an estimated $250 million a year on an annualized basis.
OSHA estimates that the revised HCS will result in savings of $475.2 million from productivity improvements for health and safety managers and logistics personnel, $32.2 million during periodic updating of SDSs and labels, and $285.3 million from simplified hazard communication training.
OSHA anticipates that, in addition to safety and health benefits, the revised HCS will result in four types of productivity benefits: (1) for chemical manufacturers, because they will need to produce fewer SDSs in future years; (2) for employers, in providing training to new employees as required by the existing OSHA HCS through the improved consistency of the labels and SDSs. (3) for firms engaging in, or considering engaging in, international trade.

## Slide 21: Team Activity
Instructor will divide the class into teams
Each team will receive an easel & a marker
Team members will brainstorm and list GHS bullets reviewed in the video
Team will also list any topics not covered in the video that was covered in class
Each team will present their conclusions

## Slide 22: Summary
  Define the background of the Global Harmonization System, GHS
  Explain how the GHS will be applied
  Describe OSHA’s modifications to the Hazard Communication Standard, HCS
  Identify OSHA’s timeline for GHS implementation
  Compare, Contrast & Identify OSHA GHS Labeling and Warning systems
  Distinguish the differences between the MSDS & the GHS Safety Data Sheet, SDS

## Slide 23: OSHA Contact Numbers
To report Unsafe Working Conditions, Safety and Health Violations Contact OSHA @:
1-800-321-OSHA (6742) / TTY1-877-889-5627
To File a Complaint Form:
To file an OSHA-7 report online, see how to file a complaint with OSHA (www.osha.gov)
For more information regarding your rights, see Worker Rights
Notes: OSHA is here to assist you in preventing injuries by providing training and assistance to ALL individuals. For more in formation please contact OSHA.

## Slide 24: Reference List
GHS: The Purple Book, Retrieved from:
  https://www.osha.gov/dsg/hazcom/ghs.html
Modification of the Hazard Communication Standard (HCS) to conform with the United Nations' (UN) Globally Harmonized System of Classification and Labeling of Chemicals (GHS), Retrieved from:
  https://www.osha.gov/dsg/hazcom/hazcom-faq.html

## Slide 25: Institute of Occupational Safety and Health
Questions & Answers
Let’s not meet again . . . by accident!
IOSH
IOSH