## Slide 1: Class 3 - Risk Assessment and Accident Investigation
This material was produced under grant number SH-22224-SH1 from the Occupational Safety and Health Administration, U.S. Department of Labor. It does not necessarily reflect the views or policies of the U.S. Department of Labor, nor does mention trade names, commercial products, or organizations imply endorsement by the U.S. Government.
Notes: Risk Management class presented during the Construction Advancement Foundation Site Safety Supervisor Course.

## Slide 2: Construction Site Safety Program
Unit 1-
Investigating Workplace Injuries
Notes: Risk Management class presented during the Construction Advancement Foundation Site Safety Supervisor Course.

## Slide 3: DEFINITIONS
ACCIDENT - The National Safety Council defines an accident as an undesired event that results in personal injury or property damage. INCIDENT - An incident is an unplanned, undesired event that adversely affects completion of a task. NEAR MISS - Near misses describe incidents where no property was damaged and no personal injury sustained, but where, given a slight shift in time or position, damage and/or injury easily could have occurred.
Notes: Instructor should use this slide to establish industry used terminology as a preface to this course.

## Slide 4: When do you conduct an investigation?
All incidents, whether a near miss or an actual injury-related event, should be investigated.
Near miss reporting and investigation allow you to identify and control hazards before they cause a more serious incident.
Accident/incident investigations are a tool for uncovering hazards that either were missed earlier or have managed to slip out of the controls planned for them. It is useful only when done with the aim of discovering every contributing factor to the accident/incident to "foolproof" the condition and/or activity and prevent future occurrences.
The objective is to identify root causes.
Notes: Instructor should use this slide to facilitate a discussion on what type of injury should be investigated.

## Slide 5: Who Should Investigate?
Management - The usual investigator for all incidents is the supervisor in charge of the involved area and/or activity.
Employees- Accident investigations represent a good way to involve employees in safety and health. Employee involvement will not only give you additional expertise and insight, but in the eyes of the workers, will lend credibility to the results. Employee involvement also benefits the involved employees by educating them on potential hazards, and the experience usually makes them believers in the importance of safety, thus strengthening the safety culture of the organization.
Safety Representative- The safety department or the person in charge of safety and health should participate in the investigation or review the investigative findings and recommendations.
Safety Committee- Many companies use a team or a subcommittee or the joint employee-management committee to investigate incidents involving serious injury or extensive property damage.
Notes: Numerous employees are affected by workplace injuries or damaged property. This slide is intended to help course participants discuss how many people may need to be involved in a complet investigation.

## Slide 6: Training accident investigators
Investigators need basic training; No one should investigate incidents without appropriate accident investigation training.
  Field Supervisors
  Office Personnel
  Newly appointed or assigned Safety Representatives
Ability to recognize “Root Cause”; A good investigation is likely to reveal several contributing factors, and it probably will recommend several preventive actions.
Technical Skills;
  Understanding of task being performed at the time of the accident.
  Understanding of environmental influences on the accident.
  Investigator answers the six basic questions; who, what, when, where, why, and how
Notes: Not everyone in an organization is a prepared to conduct investigations. This slide is intended to have course participants discuss training potential investigators should have.

## Slide 7: Investigation Traps
Blame without proof; The error made by the employee may not be the most important contributing cause. The employee who has not followed prescribed procedures may have been encouraged directly or indirectly by a supervisor or production quotas to "cut corners."
Policies that miss the mark; The prescribed procedures may not be practical, or even safe. Sometimes where elaborate and difficult procedures are required, engineering redesign might be a better answer. Lack of Accountability; Supervisors and others who investigate incidents should be held accountable for describing causes carefully and clearly. When reviewing accident investigation reports, the safety professional should be on the lookout for catch-phrases, for example, "Employee did not plan job properly." While such a statement may suggest an underlying problem with this worker, it is not conducive to identifying all possible causes, preventions, and controls. Certainly, it is too late to plan a job when the employee is about to do it. Further, it is unlikely that safe work will always result when each employee is expected to plan procedures alone.
Notes: Investigations should result in meaningful results. This slides provides some of the more common “traps’ untrained investigators could fall in to.

## Slide 8: Results of an accident investigation
The primary purpose of accident investigations is to prevent future occurrences. For example, the “Job Hazard Analysis” should be revised and employees retrained to the extent that it fully reflects the recommendations made by an incident report. Implications from the root causes of the accident need to be analyzed for their impact on all other operations and procedures.
Recommended preventive actions should make it very difficult, if not impossible, for the incident to recur.
The investigative report should list the ways to "foolproof" the condition or activity.
Notes: How are the results of investigation incorporated into a meaningful corrective action? This slide is intended to help course participants learn hoe to take investigation results and turn them into injury preventing actions.

## Slide 9: The Interview
Take Notes!
Ask open-ended questions
  “What did you see?”
  “What happened?”
Do not make suggestions
  If the person is stumbling over a word or concept, do not help them out
  Use closed-ended questions later to gain more detail.
  After the person has provided their explanation, these type of questions can be used to clarify
    “Where were you standing?”
    “What time did it happen?”
Notes: This slide is intended to help potential investigators conduct a better documented investigations.

## Slide 10: The Interview
Don’t ask leading questions
  Bad: “Why was the forklift operator driving recklessly?”
  Good: “How was the forklift operator driving?”
If the witness begins to offer reasons, excuses, or explanations, politely decline that knowledge and remind them to stick with the facts
Summarize what you have been told.
  Correct misunderstandings of the events between you and the witness
Ask the witness for recommendations to prevent recurrence
  These people will often have the best solutions to the problem
Notes: Course participants should learn techniques to better questions persons involved. The result of any interview is to develop accurate documentation leading to a meaningful corrective action

## Slide 11: Record the Facts
Interview witnesses as soon as possible.
If Possible - Document the accident scene before changes are made.
  Take photos
  Draw scaled sketches
  Record measurements
Collect support documents
Keep all notes and remarks in a bound notebook or three ring binder.
Record:
  Pre-accident conditions
  Accident sequence
  Post-accident conditions
Document victim location, witnesses, machinery, energy sources and other contributing factors.
Even the most insignificant detail may be useful!
Notes: Instructor should facilitate a group discussion about documenting facts not unverified opinion. Information recorded will become part of the permanent record of the occurrence and should be as accurate as possible.

## Slide 12: Investigation Report
An accident investigation is not complete until a report is prepared and submitted.
Background Information
  Where and when the accident occurred
  Who and what were involved
  Operating personnel and other witnesses
Account of the Accident (What happened?)
  Sequence of events
  Extent of damage
  Accident type
  Agency or source (of energy or hazardous material)
Recommendations (to prevent a recurrence) for immediate and long-range action remedy
  Basic causes
  Indirect causes
  Direct causes
Notes: Course Instructor should insure attendees have a clear understanding of the importance of accurate documentation.

## Slide 13: Accident Investigation Exercise
Break into teams
Read the scenario handout
Complete the investigation report
Identify the unsafe acts or conditions that caused the injury
Notes: Class activity: This activity can be broken into several segments including with the trainees broken into small groups or 2-4.
1.) Have small groups indentify any OSHA rules that may have been violated resulting in the injury.
2.) Groups could discuss training that may have prevented the injury
3.) Groups could think of meaningful corrective actions that would have prevented the injury

## Slide 14: Accident #1
Accident Type:
Explosion
Weather Conditions:
Clear
Type of Company:
Removal/Installation/Junking of Gasoline Pumps and Underground Tanks
Size of Work Crew:
2
Union or Non-union:
Non-union
Worksite Inspection Conducted (1926.20(b)(2)):
No
Designated Competent Person on Site (1926.20(b)(2)):
No
Employer Safety Health Program:
No
Training and Education for Employees Designated (1926.21(b)):
No
Craft of Deceased Employee(s):
Laborer
Age & Sex
27; Male
Time on the Job:
2 years
Time on Task:
1 hour
A laborer was killed when a gasoline storage tank he was cutting with a portable power saw exploded. The worker's company was involved in installing, removing and junking gasoline pumps and underground tanks. Although he had experienced working with the saw and scrap materials, the worker did not adequately purge the tank and test for vapors before beginning to cut. The 18 x 6 foot, 3000 gallon tank had been used recently for underground storage at a service station. At the time of the explosion, the mechanic was cutting on the tank with a gasoline powered portable saw equipped with an abrasive epoxy disk for cutting metal. The explosion propelled the worker 10 to 15 feet from the tank into another tank.
Notes: Accident #1 for the group activity

## Slide 15: Accident #2
Accident Type:
Fall, Different Level
Weather Conditions:
Clear, Warm
Type of Operation:
Painting Contractor
Size of Work Crew:
2
Collective Bargaining
No
Competent Safety Monitor on Site:
No
Safety and Health Program in Effect:
No
Was the Worksite Inspected Regularly:
No
Training and Education Provided:
Inadequate
Employee Job Title:
Painter
Age & Sex:
29-Male
Experience at this Type of Work:
Unknown
Time on Project:
1 month
Two employees were painting the exterior of a three-story building when one of the two outriggers on their two-point suspension scaffold failed. One painter safely climbed back onto the roof while the other fell approximately 35 feet to his death. The outriggers were inadequately counterweighted with three 5-gallon buckets containing sand and were not secured to a structurally sound portion of the building. Neither painter was wearing an approved safety belt and lanyard attached to an independent lifeline.
Notes: Accident #2 for the group activity

## Slide 16: Accident #3
Accident Type:
Electrocution
Weather Conditions:
Indoor Work
Type of Operation:
Installing and Trouble-shooting overhead lamps
Size of Work Crew:
15
Competent Safety Monitor on Site:
Yes
Safety and Health Program in Effect:
Inadequate
Was the Worksite Inspected Regularly:
Yes
Training and Education Provided:
No
Employee Job Title:
Electrician
Age & Sex:
53-Male
Experience at this Type of Work:
Journeyman
Time on Project:
1 Month
The employee was attempting to correct an electrical problem involving two non-operational lamps. He proceeded to the area where he thought the problem was. He had not shut off the power at the circuit breaker panel nor had he tested the wires to see if they were live. He was electrocuted when he grabbed the two live wires with his left hand and then fell from the ladder.
Notes: Accident #3 for the group activity

## Slide 17: Construction Site Safety Program
Unit 2-
Root Cause Analysis
Notes: Transition Slide from investigation to Root Cause Analysis

## Slide 18: Root Cause Analysis
Root Cause Analysis seeks to identify the origin of a problem. It uses a specific set of steps, with associated tools, to find the primary cause of the problem, so that you can:
  Determine what happened
  Determine why it happened
  Figure out what to do to ensure it will not happen again
Notes: This slide is intended to help help course atendees understand how to conduct and Root Cause Analysis and implement meaningful corrective actions.

## Slide 19: 3 Main Root Causes
Physical causes (Work Factors) - Tangible, material items failed in some way (for example, a car's brakes stopped working).
Human causes (Unsafe Acts) - People did something wrong. or did not doing something that was needed. Human causes typically lead to physical causes (for example, no one filled the brake fluid, which led to the brakes failing).
Organizational causes (Unsafe Conditions) - A system, process, or policy that people use to make decisions or do their work is faulty (for example, no one person was responsible for vehicle maintenance, and everyone assumed someone else checks the brake fluid level in the service trucks).
Notes: Instructor should facilitate course discussion that would encourage attendees to think about all the various contributing factors and identify the most accurate remedial action.

## Slide 20: Root Cause Analysis
Define the Problem
What is the negative result?
What are the specific symptoms?
Collect Data
How long has the problem existed?
What is the impact of the problem?
Identify Possible Causal Factors
What sequence of events leads to the problem?
What conditions allow the problem to occur?
Identify the Root Cause(s)
Ask “Why”
What is the real reason the problem occurred?
Recommend and Implement Solutions
What can you do to prevent the problem from happening again?
How will the solution be implemented?
Notes: Root Cause is different from accident reporting. In some cases employers or those conducting investigations may look to report what happened but not focus on prevention of a reoccurrence. Instructors should facilitate group discussion regarding prevention.

## Slide 21: The “5 Whys”
By repeatedly asking the question "Why" (five is a good rule of thumb), you can peel away the layers of symptoms which can lead to the root cause of a problem.
Very often the reason for a problem will lead you to another question. Although this technique is called "5 Whys," you may find that you will need to ask the question fewer or more times than five before you find the issue related to a problem.
Notes: This root cause technique could be discussed in small groups or by the larger group as a whole. The purpose is to get participants to look past initial findings and get to the single action that, if prevented, would not resulted in the injury.

## Slide 22: “5 Why” Scenario #1
1.) Why is the monument disintegrating? Use of harsh chemicals
2.) Why are harsh chemicals used?
To clean pigeon droppings
3.) Why so many pigeons?
They eat spiders and there are a lot of spiders at monument
4.) Why so many spiders? They eat gnats and lots of gnats at monument
5.) Why so many gnats?
They are attracted to the light at dusk.
Root Cause Solution:
Turn on the lights at a later time.
Problem: The Washington Monument was disintegrating
Notes: Demonstration #1 of the “5 Why” technique

## Slide 23: “5 Why” Scenario #2
1. Why did the employee fall from the ladder? Employee reached beyond the ladders balance point and the ladder tipped over.
2. Why did the employee reach out and not reposition the ladder? Because there were several pallets of material in the way and he couldn’t move the ladder into the correct position.
3. Why were pallets stored in an area being painted? The materials being stored on the pallets were not scheduled to installation for several weeks but due to weather conditions the materials had been moved inside.
4. Why where the pallets not moved so the painter could appropriately access the work are? The controlling and creating contractor was not contacted and the painting work was not rescheduled. The hazard was not identified during the JHA and the employee proceeded with his assigned tasks in a manner he thought was expected.
5. Why was the JHA not completed?
Supervisor was not appropriately trained and did not conduct a JHA as required by site and employer requirement.
Root Cause Solution: Insure all supervision are appropriately trained to conduct JHA and action plans communicated to affected personnel.
Problem Statement: Employee fell from a 6’ folding step ladder while painting.
Notes: Demonstration #2 of the “5 Why” technique

## Slide 24: Root Cause Exercise
Get original teams
Identify the Root Cause of the injury in your accident investigation
Will your Root Cause Analysis change your original corrective actions?
Notes: Get participants back into small groups and have them define a root cause for the incident scenarios previously presented. The information documented during the first part of the exercise resulted in gathering of information. In this phase participants should being using collected documentation to find the root cause.

## Slide 25: Construction Site Safety Program
Unit 3-
Job Hazard Analysis
Notes: Transition Slide to unit 3

## Slide 26: Purpose of a Job Hazard Analysis
A means of systematically identifying workplace hazards as they occur is needed so that hazards can be eliminated before accidents occur. The greater the number of ways that problems are brought to management's attention, the less likely is it that an accident will occur when one of the protective systems fail.
Notes: JHA are known by many names. Instructor should discuss how and why this type of information is important to affect workers

## Slide 27: JHA 5 Step Process
Step 1 - Watch the work being done
    What are some effective methods to watch the work being done?
    Is it important to involve the employee performing the task?
Step 2 - Break the job down into steps
Step 3 - Describe the hazards in each step of the task
    The primary purposes of the JHA is to make the job safer. The information gathered in this step will be valuable in helping to eliminate and/or reduce hazards associated with the job, and improve the system weaknesses that produced them.
Step 4 - Control Measures
Step 5 – Documentation, Write it up
Notes: This slide begins the explanation of how to conduct or develop a JHA. The purpose is to bring the students to a common understanding of how to begin.
The “fix-the-system” culture is one that makes every effort to address the hazards in the workplace by first identifying the hazardous condition or practice, analyzing the hazard to determine the root cause and then eliminate those hazards by correcting the deficiencies in the system. (could include supervisor training, improved accountability system, establishment of standards of performance at all levels, to name a few.)
What are some effective methods to watch the work being done?
Video, observation, photos, sketches.

## Slide 28: Identify the Type Hazard
Mechanical -
Caught in
Caught between
Falls
Electrical
Temperature
Environmental Hazards
Flammability/Fire
Confined Space
Ergonomic -
  High Frequency
  High Duration
  High Force
  Posture
  Point of Operation
  Mechanical Pressure
  Vibration
  Environmental Exposure
Notes: Instructor should insure participants are looking at all types of injury factors. This slide is intended to indentify non-personnel factors.

## Slide 29: Special Hazards
Explosives
  Explosions result in large amounts of gas, heat, noise, light and over-pressure.
Electrical Contact
  Inadequate insulation, broken electrical lines or equipment, lightning strike, static discharge etc.
Chemical Reactions
  Chemical reactions can be violent, can cause explosions, dispersion of materials and emission of heat.
Notes: Special hazards, while not always routine must be understood by investigators and documented.

## Slide 30: The Hierarchy of Controls
Engineering controls
Administrative Controls - Work Practice
Personal Protective Equipment (PPE).
Notes: Instructor should insure participants understand that PPE is the LAST line of defense. Engineering Controls is the most desire able as it provides the highest level of protection for workers.

## Slide 31: Engineering Controls
The first and best strategy is to control the hazard at its source. Engineering controls do this, unlike other controls that generally focus on the employee exposed to the hazard. The basic concept behind engineering controls is that, to the extent feasible, the work environment and the job itself should be designed to eliminate hazards or reduce exposure to hazards.
Engineering controls can be simple in some cases. They are based on the following principles:
  If feasible, design the facility, equipment, or process to remove the hazard or substitute something that is not hazardous.
  If removal is not feasible, enclose the hazard to prevent exposure in normal operations.
  Where complete enclosure is not feasible, establish barriers or local ventilation to reduce exposure to the hazard in normal operations.
Notes: Instructor should provide examples of Engineering Controls
1.) Handrails
2.) Sloping
3.) Lock Out

## Slide 32: Administrative Controls – Work Practices
While safe work practices can be considered forms of administrative controls, OSHA uses the term administrative controls to mean other measures aimed at reducing employee exposure to hazards. These measures include:
  Additional relief workers
  Exercise breaks
  Rotation of workers
These types of controls are normally used in conjunction with other controls that more directly prevent or control exposure to the hazard.
Notes: Unlike engineering control Administrative and PPE control do not remove the hazard from the environment. Admin and PPE seek to limit the effect the hazard has on the worker but does not eliminate it.

## Slide 33: Personal Protective Equipment
When exposure to hazards cannot be engineered completely out of normal operations or maintenance work, and when safe work practices and management controls cannot provide sufficient additional protection from exposure, personal protective clothing and/or equipment may be required.
A supplementary method of control is the use of protective clothing or equipment. This is collectively called personal protective equipment, or PPE. PPE may also be appropriate for controlling hazards while engineering and work practice controls are being installed. For specific OSHA requirements on personal protective equipment, see OSHA’s standard, 1910 Subpart I.
Notes: Personnel Protective Controls assume the hazard will occur and the device will prevent injury to the worker.

## Slide 34: JHA Exercise
Get back in your original groups
Use your completed accident investigation form and Root Cause Analysis to create a Job Hazard Analysis for the task being conducted in your assigned injury scenario
Notes: This group activity builds on previous group tasks and asked participants to pull together all previous collected information and develop a Job Hazard Analysis that would prevent the injury from occurring.

## Slide 35: Construction Site Safety Program
Unit 4-
Near Miss &
Hazard Reporting
Notes: Transition slide

## Slide 36: Near Miss Incident
An unplanned event that did not result in injury, illness, or damage - but had the potential to do so.
Only a fortunate break in the chain of events prevented an injury, fatality or damage.
Although human error is commonly an initiating event, a faulty process or system invariably permits or compounds the harm, and should be the focus of improvement
Notes: Instructor should facilitate a group conversation about getting workers to better report near miss incidents. Workers and Supervisors tend to not report near miss incident if they believe it will have a negative outcome for them.

## Slide 37: Near Miss Reporting
Near Miss is a Zero Cost Learning Tool.
A near miss reporting system includes both mandatory (for incidents with high loss potential) and voluntary, non-punitive reporting by witnesses. A key to any near miss report is the "lesson learned". Near miss reporters are in a position to describe what they observed about genesis of the event, and the factors that prevented loss from occurring.
A Root Cause Analysis should be used to identify the defect in the system that resulted in the error and factors that may help eliminate a reoccurrence.
Near misses are smaller in scale, relatively simpler to analyze and easier to resolve.
Notes: The importance of near miss reporting as a means of preventing a reoccurrence of injuries should be discussed.

## Slide 38: Incident Pyramid
Notes: While the actual incident numbers may very the concept of the pyramid is that preventing low level preventable occurrences will lead to lower serious injuries and longer time between undesired events.

## Slide 39: Construction Site Safety Program
Unit 5-
Risk Management & Cost Control
Notes: Transition Slide

## Slide 40: Experience Modification Rate
While the formula may appear complex, it
If you are at the industry average, your Experience Mod is a 1.0. If your experience is 20% better then average your Experience Mod would be a .80 or 20% worse would be 1.20.
It makes sense to reward companies that practice effective safety and claims management techniques over those who do not. In effect, the Experience Mod does just that.
Notes: Experience Modification Rate or EMR effects a companies ability to obtain work by increase the cost of doing business.

## Slide 41: How do claims affect your EMR?
Medical-only claims Claims that require medical treatment only are usually less severe so employers should not be penalized when they occur. Consequently, any medical only claims are reduced by 70% before they enter the formula. You can take advantage of this by ensuring that injured employees remain at work when possible or return to work within the waiting period. This is where an effective claims management and return to work program can have a dramatic effect.
Lost time claims In most cases, the first $5,000 of a lost time claim is counted at full value. The dollar amounts after $5,000 is discounted. There is also a large claim cap limit to protect you from a catastrophic loss. Because the first $5,000 of each loss goes into the formula dollar-for-dollar, severity is a factor. A single claim valued at $20,000 has less effect on your Experience Mod then 10 claims valued at $2,000.
Notes: While not a topic related to OSHA this topic should be addressed so that attendees understand the full impact of work related injuries.

## Slide 42: Tips for Managing Claims
To minimize claims:
Investigate incident immediately to avoid second occurrence
Develop a Return to Work program. Have light duty jobs available if possible
Get the injured worker back to work ASAP, retrain if necessary
Manage the claims process; be proactive
Develop a Kept-On-Salary policy
Key business decisions to better manage your EMR:
Report all employee hours worked
Track incidents from office personnel, field personnel, and subsidiary divisions independently
Do not lump subsidiary companies under one EMR rate
Take a proactive approach to training, avoidance, and claim management
Designate a Safety Director and give that person the proper authority to affect policy, decisions, and personnel
Work with Washington State Labor and Industries and OSHA representatives when they visit the jobsite
Realize that the money spent now on safety can save you much more later on.
Notes: While not OSHA related. Course participants should have a working knowledge of the post injury side of this a Safety Supervisors role. A review of claim management functions will help participants understand the total process.

## Slide 43: Why Safety Programs Fail
Safety is a priority, not a value!
Safety is not managed in the same manner as production, quality, and cost issues!
Safety is not driven through continuous improvement!
Notes: This slide is intended to help participants understand that Safety is not a one time event, Safety functions should be driven throughout the organization

## Slide 44: Risk Management Terms
Hazard
A Condition With the Potential for Causing Injury or Damage
Risk
An Expression of possible loss in terms of severity and probability
Risk Assessment
Using sound concepts to Detect, Hazards and Estimate the Risk they Pose.
Gambling
Making risk decisions without reasonable or prudent assessment or management of the risk involved
Notes: 3
Standard Risk Management Terminology.

## Slide 45: Risk Management Benefits
Reduction in Material and Property Damage.
Effective Project Accomplishment.
Reduction in Serious Injuries and Fatalities.
Notes: 3
Good Risk Management practice can help owners better realize the value of an affective safety program.

## Slide 46: Experience Modification Rates
The base premium is calculated by dividing a company's payroll in a given job classification by 100, and then by a 'class rate' determined by the National Council on Compensation Insurance (NCCI) that reflects the inherent risk in that job classification. For example, structural ironworkers have an inherently higher risk of injury than receptionists, so their class rate is significantly higher.
A comparison is made of past claims history to those of similar companies in your industry. If you've had a higher-than-normal rate of injuries in the past, it is reasonable to assume that your rate will continue to be higher in the future. Insurers examine your history for the three full years ending one year before your current policy expires. For example, if you're getting a quote for coverage that expires on January 5, 2008, the retro plan will look at 2004, 2005 and 2006.
NCCI has developed a complicated formula that considers the ratio between expected losses in your industry and what your company actually incurred, as well as both the frequency of losses and the severity of those losses. A company with one big loss is going to be 'penalized' less severely than a company with many smaller losses, because having many small losses is seen as a sign that you'll face larger ones in the future.
The result of that formula is your EMR, which is then multiplied against the manual premium rate to determine your actual premium (before any special discounts or credits from your insurer). Essentially, if your EMR is higher than 1.00, your premium will be higher than average; if it's 0.99 or lower, your premium will be less.
Notes: Experience Modification Rates AND OSHA incidents are used by construction purchaser to eliminate potential bidders. Participants need to understand how their companies EMR affect the ability to competitively bid work.

## Slide 47: EMR Affects
How does a high EMR affect costs? An EMR of 1.2 would mean that insurance premiums could be as high as 20% more than a company with an EMR of 1.0. That 20% difference must be passed on to clients in the form of increased bids for work. A company with a lower EMR has a competitive advantage because they pay less for insurance.
How do I lower EMR? The good news is that EMR can be lowered. An effective safety program that eliminates hazards and prevents injuries is the starting point. No injuries equal no claims.
Notes: Explanation of the EMR calculation

## Slide 48: Controlling Accident Costs
Proactive Approach
  Establish medical provider(s)
  Conduct detail investigation and accompany injured employee to Doctor
  Establish modified duty tasks
  Insure Nurse/Case Manager is working with injured employee
Reactive Approach
  Delayed injury reporting
  Investigations are delayed or incomplete
  Employee is left to find own medical provider and work with insurance
  Return to full work status is delayed by others – employee left without income
Notes: Proactive vs. Reactive Safety program difference explanation

## Slide 49: What Rights Do You Have Under OSHA? You have the right to:
  A safe and healthful workplace
  Know about hazardous chemicals
  Information about injuries and illnesses in your workplace
  Complain or request hazard correction from employer
  Training
  Hazard exposure and medical records
  File a complaint with OSHA
  Participate in an OSHA inspection
  Be free from retaliation for exercising safety and health rights
  Whistleblower and Section 11c
  Employer rights and Responsibilities
Notes: Review worker rights under OSHA