## Slide 1: Title Page
HAZARD COMMUNICATION STANDARD 2012 (HCS/GHS)
BY
WAYNE STATE UNIVERSITY
FOR
SUSAN HARWOOD TRAINING GRANT
2014-2015

## Slide 2: MAIN MODULE HAZARD COMMUNICATION STANDARD WITH GLOBALLY HARMONIZED SYSTEM OF CLASSIFICATION AND LABELING OF CHEMICALS (HCS/GHS)

## Slide 3: ACKNOWLEDGEMENT
UNITED STATES DEPARTMENT OF LABOR Occupational Health and Safety Administration (OSHA) Susan Harwood Training Follow-On Grant
SH-27686-SH5
This material was produced under a grant (SH-26321-SH4) from the Occupational Health Administration, U.S. Department of Labor. It does not necessarily reflect the views or policies of the U.S. Department of Labor, nor does the mention of trade names, commercial products, or organization imply endorsement by the U.S. Government.
Notes: This material was produced under Susan Harwood grant number SH-26321-SH4 Occupational Safety and Health Administration, U.S. Department of Labor, and used for training purposes under the Susan Harwood Training Follow-On Grant SH-27686-SH5

## Slide 4: Worker Rights
Workers are entitled to safe and healthful conditions. The OSH ACT provides workers with the right to:
    Ask OSHA to inspect their workplace;
    Review employers’ records of work-related injuries and illnesses
    Get copies of their medical records; and
    Receive information and training about hazards and their prevention, using applicable OSHA standards.
WORKER RIGHTS
UNDER OSH ACT
Notes: Workers are entitled to working conditions that do not pose a risk of serious harm to them. To help ensure a safe and healthful workplace, the OSH Act provides workers with the right to ask OSHA to inspect their workplace; use their rights under the law without retaliation and discrimination; receive information and training about hazards, and the methods for prevention. Under the OSH Act, workers also have the right to ask for the OSHA standards that apply to their workplace, get copies of test results regarding the hazards in the workplace, review records of work-related injuries and illnesses, and get copies of their medical records.

## Slide 5: Whistleblower rights
Workers may file a complaint with OSHA if the employer retaliates by taking unfavorable personnel action against them for whistleblowing.
  for more information Whistleblowers’ Rights
Whistleblower laws require that complaints be filed with OSHA within certain time limits following the alleged retaliation.
RIGHTS AS A WHISTLEBLOWER
Notes: Workers may file a complaint with OSHA if the employer retaliates by taking unfavorable personnel action because workers engaged in protected activity relating to workplace safety or health, asbestos in schools, cargo containers, airline, commercial motor carrier, consumer product, environmental, financial reform, food safety, health insurance reform, nuclear, pipeline, public transportation agency, railroad, maritime, motor vehicle safety, and securities laws. If it is believed that the employer retaliated against the worker because of exercising legal rights as an employee, workers must contact OSHA as soon as possible; the complaints must be filed within the legal time limits. An employee can file a complaint with OSHA by visiting or calling the local OSHA office or sending a written complaint to the closest OSHA regional or area office. Written complaints may be filed by facsimile, electronic communication, hand delivery during business hours, U.S. mail (confirmation services recommended), or other third-party commercial carrier.

## Slide 6: Right to know
Federal Hazard Communication Standard, Title 29, Part 1910.1200 of the Code of Federal Regulations (29 CFR 1910.1200) mandates that “Workers have the right to know and understand the hazardous chemicals they use and how to work with them safely.”
This regulation is designed to make information about hazardous chemicals that are present in work places available to exposed employees.
The hazard communication standard applies to any business, including manufacturers that use hazardous chemicals, regardless of the number of individuals employed.
RIGHT-TO-KNOW
Notes: Federal Hazard Communication Standard, Title 29, Part 1910.1200 of the Code of Federal Regulations (29 CFR 1910.1200) mandates that “Workers have the right to know and understand the hazardous chemicals they use and how to work with them safely.” This regulation is designed to make information about hazardous chemicals that are present in work places available to exposed employees. The hazard communication standard applies to any business, including manufacturers that use hazardous chemicals, regardless of the number of individuals employed.

## Slide 7: PREMISE
This training is for
  people who are working with chemicals
    either have never taken any training on Hazard Communication Standard (HCS), or
    need a refresher training on HCS
This presentation
  can be used in its entirety, or
  can be selectively used by a trainer as he/she sees fit in accordance with the training objectives.
Notes: This training is based on the premise that trainees will be people who are working with chemicals, and they either have never taken any training on Hazard Communication Standard (HCS), or they need refresher training on HCS, with updates including GHS. The trainer using this presentation is free to use it in its entirety, or select any parts of it as the trainer sees fit in accordance with the training objectives.

## Slide 8: Learning objectives
This training module aims to
  help workers to understand and identify the purpose of
    Right-to-Know
    Hazard Communication
    Globally Harmonized System (GHS) and
    Hazard Communication Standard (HCS)
  cover the 10 sections of HCS
  present information on effective dates to implement the new standard
LEARNING OBJECTIVES
Notes: The aim of this training material is to give information about right-to-know, hazard communication, the globally harmonized system of classification and labeling of chemicals (GHS), and hazard communication standard (HCS) by identifying their purposes. Another objective of this training module is to explain each section of the hazard communication standard and present information on effective dates for implementation of the new standard.

## Slide 9: HAZARD COMMUNICATION
Applies to chemical hazards, such as
  health hazards (e.g., irritation, and carcinogenicity)
  physical hazards (e.g., flammability, and corrosion)
  environmental hazards (e.g. aquatic toxicity)
Notes: Chemicals cause a wide range of health hazards, such as irritation, and carcinogenicity; physical hazards such as flammability and corrosion; and environmental hazards which are chronic aquatic toxicity and acute aquatic toxicity.

## Slide 10: HAZARD COMMUNICATION
Main objective of hazard communication is to provide information to employees on how to protect themselves against chemical hazards in the workplace
Notes: Hazard Communication provides information to employees so they can protect themselves against the mentioned chemical hazards in the workplace.

## Slide 11: GLOBALLY HARMONIZED SYSTEM
Globally Harmonized System of Classification and Labeling of Chemicals (GHS) is
  applicable internationally
  a new system for classification and labeling of chemicals
GHS
  covers chemical hazards
  aims to improve safety and health of workers through effective hazard communication
Notes: GHS which stands for “The Globally Harmonized System of Classification and Labeling of Chemicals” is an international approach to hazard communication, providing agreed upon criteria for the classification of chemical hazards; and a standardized approach to labels and safety data sheets. It is a new system for the classification and labeling of chemicals, covering their health, physical and environmental hazards. It aims at improving safety and health of workers through more effective communication on the chemicals and their hazards.

## Slide 12: Hazard Communication Standard
Hazard Communication Standard (HCS) - 29 CFR 1910.1200
  a.k.a. the “Right-to-Know” standard
  requires employers to inform and train workers about hazardous chemicals
    focusing on possible health and physical hazards in the workplace
HAZARD COMMUNICATION STANDARD
Notes: Hazard Communication Standard (HCS) or 29 CFR 1910.1200 protects employee’s right to be informed about hazardous chemicals in the workplace. It is also known as the “Right-to-Know” standard. Hazard communication standard covers Physical, Health and Environmental Hazards and requires employers to inform and train workers on hazardous chemicals and their possible hazards in the workplace.

## Slide 13: Haz Com Slide 13
HCS
  first enacted on November 25, 1983
  became applicable to construction in 1994
  was revised to align with GHS in 2012
  will be fully implemented by June 2016
HAZARD COMMUNICATION STANDARD
Notes: HCS was first enacted on November 25, 1983, becoming applicable to the construction industry in 1994. It was revised in 2012 to align with GHS which is supported by the United Nations. The new system will be fully implemented by June 2016.

## Slide 14: Haz Com Slide 14
The new standard (HCS/GHS) will help to
  improve understanding of hazards and safety in the use of chemicals
  reduce injuries and illnesses
  decrease costs for American businesses
It will eliminate
    updating of labels
    revisions of SDS’s
    additional tests for classification
HAZARD COMMUNICATION STANDARD
Notes: HCS/GHS is expected to improve understanding of hazards and of safety in using chemicals.The new standard will help to reduce injuries and illnesses, and decrease costs for American businesses by eliminating the need to periodically update labels, revise safety data sheets, and run tests for classification.

## Slide 15: Haz Com Slide 15
Hazard Communication Standard has 10 sections:
  Purpose
  Scope and Application
  Definitions
  Hazard Classification
  Written Hazard Communication Program
  Labels and Other Forms of Warning
  Safety Data Sheets
  Employee Information and Training
  Trade Secret
  Effective Dates
HAZARD COMMUNICATION STANDARD
Notes: The Hazard Communication Standard has 10 sections, which are: purpose, scope and application, definitions, hazard classification, written hazard communication program, labels and other forms of warning, safety data sheets, employee information and training, trade secret and effective dates. These sections are explained in detail in the next slides.

## Slide 16: PURPOSE
Main objective of the Hazard Communication Standard is to
  ensure that
    all imported or produced chemicals are classified with respect to their hazards
    information about the hazards are transmitted to both employers and employees
Notes: The main purpose of the standard is to ensure that all imported or produced chemicals are classified with respect to their hazards, and information about the hazards are transmitted to both employers and employees.

## Slide 17: PURPOSE
HCS aims to
  give information to workers, who may be exposed to hazardous chemicals, on protective measures, such as
    labeling of chemicals
    developing training programs
    using safety data sheets (SDS), and
    maintaining a written hazard communication program.
Notes: HCS also aims to give information to people who may be exposed to hazardous chemicals, on protective measures, such as labeling of chemicals, developing training programs, using safety data sheets (SDS), and maintaining a written hazard communication program.

## Slide 18: SCOPE AND APPLICATION
HCS mandates that
  employers must inform their employees about hazardous chemicals in the workplace through
      labels or other forms or warning
      safety data sheets (SDS)
      training
Notes: Under HCS, employers must inform their employees about existing hazardous chemicals in the workplace, through labels or other forms of warning such as tags, placards and markings, safety data sheets which are the documents containing details of specific hazardous chemicals, and training about the standard, existing hazardous chemicals in the work place, and the usage of these chemicals.
Figure Source : Susan Harwood grant number 22315-11-60-F-72, UNIVERSITY OF PUERTO RICO Río Piedras Campus Division of Continued Education and Professional Studies (DECEP)

## Slide 19: SCOPE AND APPLICATION
HCS also requires that
  employers in laboratories and workplaces where employees only handle chemicals in sealed containers should
    check labels on containers to ensure they are not defaced or removed
    maintain safety data sheets and make them accessible to employees
    make sure that all employees are trained in accordance with the information and training section of the standard.
Notes:     Employers in laboratories and workplaces where employees only handle hazardous chemicals in sealed containers should check the labels on the containers to ensure they are not defaced or removed; maintain safety data sheets and make them accessible to employees; and make sure that all employees are trained in accordance with the information and training section of the standard.

## Slide 20: SCOPE AND APPLICATION
Under HCS
  manufacturers and distributors are required to provide all necessary information (SDS and container labels) to employers prior to shipment
Notes: Manufacturers and distributors are also required to provide the safety data sheets and label the containers prior to shipment. If the safety data sheet is not provided with a shipment that has been labeled as a hazardous chemical, the distributor or employer shall obtain one from the chemical manufacturer or importer as soon as possible. The chemical manufacturer or importer shall also provide distributors or employers with a safety data sheet upon request.
Figure Source: Susan Harwood grant number 22315-11-60-F-72, UNIVERSITY OF PUERTO RICO Río Piedras Campus Division of Continued Education and Professional Studies (DECEP)

## Slide 21: DEFINITIONS
HCS defines a variety of terms; these are
  Article
  Assistant secretary
  Chemical
  Chemical manufacturer
  Chemical name
  Classification
  Commercial account,
  Common name
  Container
  Designated representative
Director
Distributor
Employee
Employer
Exposure or exposed
Foreseeable emergency
Hazard category
Hazard class
Hazard not otherwise
classified (HNOC)
Notes: Both employees and employers should know the meanings of the words that are used in HCS for better understanding them. There are a lot of terms which are defined in the Definitions section of HCS, such as chemical, chemical manufacturer, chemical name, employee, employer, hazard class, and so on.

## Slide 22: DEFINITIONS
Hazard statement
Hazardous chemical
Health Hazard
Immediate use
Importer
Label
Label elements
Mixture
Physical hazard
Pictogram
Precautionary statement
Product identifier
Produce
Pyrophoric gas
Responsible party
Safety data sheet (SDS)
Signal word
Simple asphxyiant
Specific chemical identity
Substance
Trade secret
Use
Work area
Workplace
Additional definitions for
Notes: There are other definitions given in HCS, as well, such as label, pictogram, work area, workplace, etc.

## Slide 23: DEFINITIONS
Examples of terms and definitions
  "Chemical" means any substance, or mixture of substances.
  "Employer" means a person engaged in a business where chemicals are either used, distributed, or are produced for use or distribution, including a contractor or subcontractor.
  "Hazard class" means the nature of the physical or health hazards, e.g., flammable solid, carcinogen, oral acute toxicity.
For a complete listing of definitions, refer to
  https://www.osha.gov/dsg/hazcom/HCSFinalRegTxt.html
Notes: Chemical, employer and hazard class terms are 3 of the definitions given in the hazard communication standard. "Chemical" means any substance, or mixture of substances. "Employer" means a person engaged in a business where chemicals are either used, distributed, or are produced for use or distribution, including a contractor or subcontractor. "Hazard class" means the nature of the physical or health hazards, e.g., flammable solid, carcinogen, oral acute toxicity. For complete listing of terms and their definitions, definitions section of hazard communication standard can be used.

## Slide 24: HAZARD CLASSIFICATION
Under HCS importers and manufacturers are required to classify chemicals with respect to their hazards by using a full range of available scientific literature or other evidences concerning potential hazards.
GHS divides hazards into three groups
HAZARDS
Physical Hazards
Health Hazards
Environmental Hazards
Notes: Under HCS, importers and manufacturers are required to classify the chemicals with respect to their hazards by using a full range of available scientific literature or other evidences concerning potential hazards. Hazards are classified under three headings in HCS: Physical Hazards, Health Hazards; and Environmental Hazards. Physical hazards are those which threaten employees’ physical safety, such as explosives. Health Hazards are associated with chemicals which pose hazardous effects, such as skin irritation, carcinogenicity and acute toxicity. Environmental Hazards may pose a risk of damage to the aquatic environment such as acute aquatic toxicity and chronic aquatic toxicity. OSHA does not mandate the use of environmental hazards in HCS/GHS.

## Slide 25: HAZARD CLASSIFICATION
Physical, Health and Environmental hazards are further classified based on hazard severity expressed by numbers and letters (as needed)
Hazard Groups (Physical, Health and Environmental)
Hazard Class (Explosives,Acute Toxicity,…)
Hazard Categories (1,2 or Type A,B…)
Hazard Subcategories (1A,1B, 2A…)
Notes: Physical, Health and Environmental hazards are further classified based on hazard severity expressed by numbers and/or letters. Under each hazard class there are different hazard categories and subcategories. These categories show the severity of hazard. As the hazard category number increases the severity of hazard decreases. The signal words and hazard statements are assigned to the hazards according to their hazard categories.

## Slide 26: PHYSICAL HAZARD CLASSIFICATION
Classification of Physical Hazards
    Explosives
    Flammable Gases
    Flammable Aerosols
    Oxidizing Gases
    Gases Under Pressure
    Flammable Liquids
    Flammable Solids
    Self-Reactive Substances
    Pyrophoric Liquids
    Pyrophoric Solids
    Self-Heating Substances
    Substances which, in contact with water emit flammable gases
    Oxidizing Liquids
    Oxidizing Solids
    Organic Peroxides
    Corrosive to Metals
Notes:   There are 16 physical hazards which are explosives, flammable gases, flammable aerosols, oxidizing gases which may, generally by providing oxygen, cause or contribute to the combustion of other material more than air does, gases under pressure which is a substance compressed, liquefied, or dissolved at 29 psi or more, flammable liquids, flammable solids, self-reactive substances which are thermally unstable liquid or solid substances or mixtures liable to undergo a strongly exothermic decomposition even without participation of oxygen, pyrophoric liquids, pyrophoric solids which are capable of igniting spontaneously in air, self-heating substances which generate heat by reaction with air without energy supply, substances which emit flammable gases in contact with water, oxidizing liquids and oxidizing solids which are the substances that release oxygen to another material for purpose of combustion, organic peroxides which are found in many products such as accelerators, activators, cross-linking agents and curing agents and corrosive to metals.
  Figure : Substances which, in contact with water emit flammable gases
Figure Source: Susan Harwood grant number 22315-11-60-F-72, UNIVERSITY OF PUERTO RICO Río Piedras Campus Division of Continued Education and Professional Studies (DECEP)

## Slide 27: PHYSICAL HAZARD CATEGORIES
Hazard Class | Hazard Categories |  |  |  |  |  | 
Explosives | Unstable Explosives | Div. 1.1 | Div. 1.2 | Div. 1.3 | Div. 1.4 | Div 1.5 | Div 1.6
Flammable Gases | 1 | 2 |  |  |  |  | 
Flammable Aerosols | 1 | 2 |  |  |  |  | 
Oxidizing Gases | 1 |  |  |  |  |  | 
Gases Under Pressure | 1 |  |  |  |  |  | 
Flammable Liquids | 1 | 2 | 3 | 4 |  |  | 
Flammable Solids | 1 | 2 |  |  |  |  | 
Self Reactive Substances | Type A | Type B | Type C | Type D | Type E | Type F | Type G
Pyrophoric Liquids | 1 |  |  |  |  |  | 
Pyrophoric Solids | 1 |  |  |  |  |  | 
Self Heating Substances | 1 | 2 |  |  |  |  | 
Substances which in contact with water emit flammable gases | 1 | 2 | 3 |  |  |  | 
Oxidizing Liquids | 1 | 2 | 3 |  |  |  | 
Oxidizing Solids | 1 | 2 | 3 |  |  |  | 
Organic Peroxides | Type A | Type B | Type C | Type D | Type E | Type F | Type G
Corrosive to Metals | 1 |  |  |  |  |  | 
Notes: the physical hazard classes and their categories are listed above. There are different category numbers for different hazards. For example hazard category for oxidizing liquids can be 1, 2 or 3. On the other hand, organic peroxides can be Type A through G, where the hazard category is designated by a letter. Further information on the classification and categorization of physical hazards can be found in APPENDIX B OF CFR 1910.1200 - PHYSICAL HAZARD CRITERIA

## Slide 28: PHYSICAL HAZARD CLASSIFICATION
The flammable liquids class has 4 categories (1, 2,3 and 4), with a hazard statement, signal word and pictogram
Categories | Hazard Statement | Signal Word | Symbol (Pictogram)
Category 1 | Extremely flammable liquid and vapor (Flash point < 23°C and initial boiling point ≤ 35°C) (95°F) | “Danger” | Flame
Category 2 | Highly flammable liquid and vapor ( Flash point < 23°C and initial boiling point > 35°C) (95°F) | “Danger” | Flame
Category 3 | Flammable liquid and vapor (Flash point ≥ 23°C and ≤ 60°C) (140°F) | “Warning” | Flame
Category 4 | Combustible liquid Flash point ≥ 60°C (140°F) and ≤ 93°C (200°F) | “Warning” | No symbol
Notes: Flammable liquid means a liquid having a flash point of not more than 93°C (199.4°F). Flash point means the minimum temperature at which a liquid gives off vapor in sufficient concentration to form an ignitable mixture with air near the surface of the liquid. A flammable liquid is classified in one of four categories. Hazard statements, signal word and pictograms may change for different categories. For category 1 and 2 the “Danger” signal word is used, while for category 3 and 4 the “Warning” signal word is used. The flame pictogram is used for categories 1, 2 and 3, but there is no pictogram for category 4.

## Slide 29: HEALTH HAZARD CLASSIFICATION
Classification of Health Hazards
    Acute Toxicity
    Skin Corrosion/Irritation
    Serious Eye Damage/Eye Irritation
    Respiratory or Skin Sensitization
    Germ Cell Mutagenicity
    Carcinogenicity
    Reproductive Toxicology
    Target Organ Systemic Toxicity - Single Exposure
    Target Organ Systemic Toxicity - Repeated Exposure
    Aspiration Toxicity
Notes: There are 10 health hazard classes; namely, acute toxicity which may harm the organs and cause organ damage,; skin corrosion and irritation which are chemicals that cause irreversible damage and destruction of the skin; serious eye damage and eye irritation, respiratory or skin sensitization, germ cell mutagens which may induce heritable mutations in human germ cells; carcinogenicity, reproductive toxicology which affect the ability of men and women to have healthy children; target organ systemic toxicity which is caused by either single or repeated exposure and can damage or affect the function of a certain organ; and aspiration toxicity which can cause chemical pneumonia, and varying degrees of pulmonary injury, or death.
Figures: Upper - Skin corrosion Lower - Serious eye damage
Source: Susan Harwood grant number 22315-11-60-F-72, UNIVERSITY OF PUERTO RICO Río Piedras Campus Division of Continued Education and Professional Studies (DECEP)

## Slide 30: HEALTH HAZARD CATEGORIES
Hazard Class | Hazard Categories |  |  | 
Acute Toxicity | 1 | 2 | 3 | 4
Skin Corrosion/Irritation | 1A | 1B | 1C | 2
Serious Eye Damage/ Eye Irritation | 1 | 2A | 2B | 
Respiratory or Skin Sensitization | 1 |  |  | 
Germ Cell Mutagenicity | 1A | 1B | 2 | 
Carcinogenicity | 1A | 1B | 2 | 
Reproductive Toxicology | 1A | 1B | 2 | Effects on or via lactation
Target Organ Systematic Toxicity (Single Exposure) | 1 | 2 | 3 | 
Target Organ Systematic Toxicity (Repeated Exposure) | 1 | 2 |  | 
Aspiration Toxicity | 1 |  |  | 
Notes: Health hazard classes and their categories are listed above. There are different categories for different hazard classes, . Further information about classification and categorization of health hazards can be found in APPENDIX A of CFR 1910.1200– HEALTH HAZARD CRITERIA

## Slide 31: SERIOUS EYE DAMAGE/IRRITATION
Categories | Hazard Statement | Signal Word | Symbol (Pictogram)
Category 1 (Eye Damage) | Causes serious eye damage | “Danger” | Corrosion
Category 2A (Eye Irritation) | Causes serious eye irritation | “Warning” | Exclamation mark
Category 2B (Eye Irritation) | Causes eye irritation | “Warning” | No pictogram
Notes: Serious eye damage is the production of tissue damage in the eye, or serious physical decay of vision, following application of a test substance to the anterior surface of the eye, which is not fully reversible within 21 days of application. Eye irritation is the production of changes in the eye following the application of test substance to the anterior surface of the eye, which are fully reversible within 21 days of application. There are 3 categories of serious eye damage and irritation. Category 1 is for eye damage; category 2A and 2B are for eye irritation hazard. Hazard Statement of “Causes serious eye damage” is used for Category 1; “Causes serious eye irritation” is used for category 2A; and “Causes eye irritation” is used for Category 2B. The signal word of “Danger” is used for Category 1 and “Warning is used for Categories 2A and 2B. Corrosion pictogram is used for Category 1, and the exclamation mark pictogram is used for Category 2A. There is no pictogram for Category 2B.

## Slide 32: ENVIRONMENTAL HAZARDS
Classification of Environmental Hazards is non-mandatory
Hazardous to the aquatic environment
Acute aquatic toxicity
Chronic aquatic toxicity
Category 1
Category 1
Category 2
Category 2
Category 3
Category 4
Category 3
Notes: Environmental hazard classes and their categories are shown above. Environmental hazards are the hazards that affect aquatic life. There are two different hazard classes for environmental hazard which are acute aquatic toxicity and chronic aquatic toxicity. OSHA does not mandate environmental hazards in labels and SDS.

## Slide 33: CHRONIC AQUATIC TOXICITY
Chronic Aquatic Toxicity hazard class has 4 categories (1,2,3 and 4)
Categories | Hazard Statement | Signal Word | Symbol (Pictogram)
Category 1 | Very toxic to aquatic life with long lasting effects | “Warning” | Fish and tree
Category 2 | Toxic to aquatic life with long lasting effects | No signal word | Fish and tree
Category 3 | Harmful to aquatic life with long lasting effects | No signal word | No symbol
Category 4 | May cause long lasting harmful effects to aquatic life | No signal word | No symbol
Notes: Chronic aquatic toxicity means potential or actual properties of a substance that can cause adverse effects to aquatic organisms. There are 4 categories (1,2,3 and 4) for the Chronic Aquatic Toxicity hazard class. The severity of hazard changes according to categories, and the “Warning” signal word is used for Category 1, chronic aquatic toxicity hazard. There is no signal word for other categories. The environment pictogram is used for Category 1 and 2, and there is no pictogram for Category 3 and 4.

## Slide 34: WRITTEN HAZARD COMMUNICATION PROGRAM
Employers are required to maintain a written hazard communication program in the workplace that must include
  safety data sheets (SDSs), labels and other forms of warning about the chemicals present
  a list of existing chemicals using a product identifier (unique name or number) referenced on SDS
  training information about hazards of non-routine works (e.g., the cleaning of reactor vessels)
Notes: Employers are required to maintain a written hazard communication program in the workplace. In each workplace, there should be safety data sheets, labels and other forms of warning about the chemicals present; a list of existing chemicals using a product identifier, which can be a unique name or number referenced on the appropriate safety data sheet; and training information about hazards of non-routine works, such as a manual about how to clean the reactor vessels.

## Slide 35: WRITTEN HAZARD COMMUNICATION PROGRAM – MULTIEMPLOYER CASES
For multi employer workplaces, each employer should individually prepare a hazard communication program that
  includes access to safety data sheets by other employers’ employees
  provides precautionary measures taken to protect other employers’ workers from possible hazards
  has methods to inform the employees of the other employers about the existing labeling system
Notes: For multi employer workplaces where all employees can be exposed to hazardous chemicals, all employers should prepare a hazard communication program that includes access to safety data sheets by other employers’ employees; provides precautionary measures taken to protect other employers’ workers from possible hazards; and has methods to inform the employees of the other employers about the existing labeling system.

## Slide 36: PRIMARY WORKPLACE FOR WRITTEN HAZARD COMMUNICATION PROGRAM – MULTIPLE WORKPLACES
If the employer has more than one workplace, the hazard communication program materials may be kept in the primary workplace
  from where it can be immediately obtained in an emergency
Notes: If the employer has more than one workplace, the hazard communication program materials may be kept in the primary workplace. Employer must ensure that employees can immediately obtain required information in an emergency.
Figure Source: Susan Harwood grant number 22315-11-60-F-72, UNIVERSITY OF PUERTO RICO Río Piedras Campus Division of Continued Education and Professional Studies (DECEP)

## Slide 37: LABELS AND OTHER FORMS OF WARNING
Labels are
  written, printed or graphical information elements concerning a hazardous chemical
  affixed to, printed on, or attached to the immediate container or package of a hazardous chemical
Notes: Labels are written, printed or graphical information elements concerning a hazardous chemical that are affixed to, printed on, or attached to the immediate container or package of a hazardous chemical.
Figure Source: Susan Harwood grant number 22315-11-60-F-72, UNIVERSITY OF PUERTO RICO Río Piedras Campus Division of Continued Education and Professional Studies (DECEP)

## Slide 38: LABELS AND OTHER FORMS OF WARNING
Employer can use any labeling system as long as the labels contain the mandatory sections and information.
Labels must be
  legible
  clearly displayed
  in English (othere languages can be added if needed)
Notes: Employer can use any labeling system as long as they contain the above mentioned sections and information. Labels must be legible, and clearly displayed. They must be in English but other languages can be added if needed.

## Slide 39: LABELS AND OTHER FORMS OF WARNING
Labels must be revised within 6 months of when new information becomes available
Notes: Chemical manufacturers, distributors or importers, who become aware of new information about a chemical product, must revise the label within 6 months.

## Slide 40: LABELS AND OTHER FORMS OF WARNING
Manufacturers, importers and distributors are required to label, mark or tag their chemicals before the chemicals leave the workplace.
Notes: Manufacturers, importers and distributors are required to label, mark or tag their chemicals before the chemicals leave the workplace.
Figure source: Susan Harwood grant number 22315-11-60-F-72, UNIVERSITY OF PUERTO RICO Río Piedras Campus Division of Continued Education and Professional Studies (DECEP)

## Slide 41: LABELS AND OTHER FORMS OF WARNING
Labels must contain
  Product identifier
  Symbols (Hazard pictograms)
  Signal word
  Hazard statement(s)
  Precautionary Statement(s)
  Name, Address, Phone Number of manufacturer, importer or responsible party.
Notes: Labels must follow a specific format under GHS. It is required that a label include a product identifier, which shows how the hazardous chemical is identified, such as chemical name, code number or batch number; pictograms, signal words, precautionary statements, and name, address, phone number of manufacturer, importer or responsible party.

## Slide 42: LABELS AND OTHER FORMS OF WARNING
Sample label
LABELS AND OTHER FORMS OF WARNING
Notes:   A sample label is shown above, which has a product identifier, Toxiflam; a flame and a skull and crossbones pictograms;
  the signal word “Danger”; hazard statement “Toxic If Swallowed, Flammable Liquid and Vapor”;
  precautionary statement “Do not eat, drink or use tobacco when using this product. Wash hands thoroughly after handling. Keep container tightly closed. Keep away from heat/spark/open flame. No smoking. Wear protective gloves and eye/face protection. Ground container and receiving equipment. Use explosion-proof electrical equipment. Take precautionary measures against static discharge. Use only non-sparking tools. Store in cool/well-ventilated place. IF SWALLOWED: Immediately call a POISON CONTROL CENTER or doctor/physician. Rinse mouth.”; and
  name, address, phone number of manufacturer, importer or responsible party, which is My Company, Mysteryt, My Town NJ 00000, Tel: 444 999 9999”.

## Slide 43: Pictograms
HCS/GHS
Health Hazard
Flame over a Circle
Skull and Crossbones
Environment
Flame
Exclamation Mark
Gas Cylinder
Corrosion
Exploding Bomb
PICTOGRAMS
Notes: Pictograms are standardized symbols that alert workers to the various hazards. Each pictogram consists of a symbol on a white background framed within a red border and represents a distinct hazard(s). There are 9 pictograms used in the new labeling system to convey the health, physical and environmental hazards. OSHA does not mandate the use of environment pictogram. Each pictogram shows the health and safety hazards related to the chemical itself. There can be one or more pictograms on a given label. These pictograms can also be found in Safety Data Sheets containing more information about the chemical product.

## Slide 44: Health Hazard Pictogram
HEALTH HAZARD PICTOGRAM
Carcinogen
Mutagen
Reproductive Toxicity
Respiratory Sensitizer
Target Organ Toxicity
Aspiration Toxicity
Notes: The first pictogram is a symbol of Health Hazard associated with chemicals that can cause health problems over a long period of time. These are carcinogens which can lead to cancer; mutagens which can cause alterations in DNA; reproductive toxicity which affects the ability of men and women to have healthy children; respiratory sensitizers which can cause allergic reactions after exposure; target organ toxicity hazards which can damage or affect the function of a certain organ; and aspiration toxicity hazards which could lead to chemical pneumonia, and varying degrees of pulmonary problems.

## Slide 45: Flame Pictogram
FLAME PICTOGRAM
  Flammables
  Pyrophorics
  Self-Heating
  Emits Flammable Gas
  Self-Reactives
  Organic Peroxides
Notes: This pictogram is a symbol of a flame. It is associated with flammable liquids, solids and aerosols. Also indicated by this pictogram are pyrophorics which are capable of igniting spontaneously in air; self heating chemicals which generate heat by reaction with air without any energy supply. It will also appear on chemical products that emits flammable gases, self reactive products** (Type B, C, D, E, F) which are thermally unstable liquid or solid substances or mixtures liable to undergo a strongly exothermic decomposition even without participation of oxygen; and organic peroxides*** (types B, C, D, E, F) which are found in many products such as accelerators, activators, cross-linking agents and curing agents.
**Self reactive types;
Type B- as packaged, does not detonate or deflagrate rapidly but is capable of undergoing a thermal explosion. (Heating causes fire)
Type C – as packaged, possesses explosive properties but will not detonate, deflagrate or thermally explode;
Types D, E, F – have shown hazards such as partial detonation, etc. when tested in a laboratory but do not possess these hazards as packaged.
***Organic peroxide types:
Type B- Any organic peroxide possessing explosive properties and which, as packaged, neither detonates nor deflagrates rapidly, but is liable to undergo a thermal explosion in that package
Type C-Any organic peroxide possessing explosive properties when the chemical as packaged cannot detonate or deflagrate rapidly or undergo a thermal explosion
Type D-
(i)Detonates partially, does not deflagrate rapidly and shows no violent effect when heated under confinement; or
(ii) Does not detonate at all, deflagrates slowly and shows no violent effect when heated under confinement; or
(iii) Does not detonate or deflagrate at all and shows a medium effect when heated under confinement;
Type E-Any organic peroxide which, in laboratory testing, neither detonates nor deflagrates at all and shows low or no effect when heated under confinement
Type F- Any organic peroxide which, in laboratory testing, neither detonates in the cavitated state nor deflagrates at all and shows only a low or no effect when heated under confinement as well as low or no explosive power

## Slide 46: Exclamation Mark Pictogram
EXCLAMATION MARK PICTOGRAM
  Irritant (skin and eye)
  Skin Sensitizer
  Acute Toxicity (harmful)
  Narcotic Effects
  Respiratory Tract Irritant
  Hazardous to Ozone Layer (Non-mandatory)
Notes: Exclamation mark pictogram is used on a labels for substances which are: Irritant to skin and eye; skin sensitizer which can cause allergic response following skin contact; acute toxicity which may harm the organs and cause organ damage; chemicals that have narcotic effects, respiratory tract irritant when they are inhaled; and chemicals that are Hazardous to the Ozone layer. OSHA does not mandate to use this pictogram for ozone damage, because it does not directly affect the health of workers.

## Slide 47: Gas Cylinder Pictogram
GAS CYLINDER PICTOGRAM
Gases under Pressure
  Substance is compressed, liquefied, or dissolved at 29 psi or more
Notes: The gas cylinder pictogram will appear on labels of cylinder of compressed gases under pressure. This pictogram on a chemical label means that the substance is a compressed, liquefied, or dissolved gas at 29 pounds per square inches or more.

## Slide 48: Sorrosion pictogram
CORROSION PICTOGRAM
Skin Corrosion/Burns
Eye Damage
Corrosive to Metals
Notes: The corrosion pictogram appears on containers of chemicals which cause skin corrosion or burns, and eye damage. It is also used for materials which are corrosive to metals.

## Slide 49: Exploding Bomb Pictogram
EXPLODING BOMB PICTOGRAM
Explosives
Self-Reactives
Organic Peroxides
Notes: The exploding bomb pictogram is used for explosives which are capable (by chemical reaction) of producing gas at such a temperature and pressure, and at such a speed as to cause damage to the surroundings; self reactives (types A, B)** which are tthermally unstable liquid or solid substances or mixtures liable to undergo a strongly exothermic decomposition even without the participation of oxygen; and organic peroxides (types A, B)*** which are found in many products such as accelerators, activators, cross-linking agents and curing agents.
**Self reactive substance types:
Type A – as packaged, will detonate or deflagrate rapidly;
Type B – as packaged, does not detonate or deflagrate rapidly but is capable of undergoing a thermal explosion. (Heating causes explosion)
***Organic peroxide types:
Type A -Any organic peroxide which, as packaged, can detonate or deflagrate rapidly
Type B - Any organic peroxide possessing explosive properties and which, as packaged, neither detonates nor deflagrates rapidly, but is liable to undergo a thermal explosion in that package

## Slide 50: Flame over circle pictogram
FLAME OVER CIRCLE PICTOGRAM
Oxidizers
  substances that release oxygen to another material for purpose of combustion
Notes: This pictogram of a flame over circle associated with materials that are classified as oxidizers. Oxidizers are substances that release oxygen to the another material for the purpose of combustion. They help the materials burn much more rapidly than they normally would. Therefore, they should not be stored close to flammable materials.

## Slide 51: Skull and Crossbones pictogram
SKULL AND CROSSBONES PICTOGRAM
Acute Toxicity (severe)
  overexposure may be toxic or fatal
Notes: The skull and cross bones pictogram is used to identify the chemicals which cause acute toxicity hazards. Depending on the toxicity of the chemical, this pictogram indicates that the overexposure of this chemical may be toxic or fatal.

## Slide 52: Environment pictogram
ENVIRONMENT PICTOGRAM
(NON - MANDATORY)
Aquatic Toxicity
  toxic to plants and aquatic life
Notes: The last pictogram, which is environment, appears on chemicals that are considered as toxic to plants and aquatic life. OSHA does not enforce the use this pictogram because it does not directly affect the health of exposed workers.

## Slide 53: Signal words
Signal words show the severity of the possible hazard and lead people to taking precautions.
Signal Words
Warning
Danger
SIGNAL WORDS
Notes: Signal words emphasize hazards and indicate the relative level of severity of the hazard as assigned to a GHS hazard class and category. Signal words are used to indicate the severity of the possible hazard and lead people to taking precautions. “Warning” and “Danger” are the two signal words used in HCS/GHS.

## Slide 54: Signal Words
Warning - used for less severe hazards
Danger - used for more severe hazards
Environmental Hazard Classes | Hazard Categories |  |  | 
Acute Aquatic Toxicity | 1 | 2 | 3 | 
Chronic Aquatic Toxicity | 1 | 2 | 3 | 4
Danger | 
Warning | 
No Signal Word | 
Signal words for different categories of hazard classes are shown with different colors
SIGNAL WORDS
Notes: “Warning” is used for less severe hazards, while “danger” is used for more severe hazards. Since the signal words are assigned according to hazard categories, there can be more than one signal word for each hazard class. However, there will only be one signal word on the label no matter how many hazards a chemical may have. If one of the hazards warrants “Danger” as the signal word and another warrants the signal word “Warning,” then only “Danger” should appear on the label. The signal words are colored in the tables above. Red is used to show “Danger” and yellow is used to show “Warning”. There is no color if there is not a signal word for the hazard category. For the environmental hazards, acute aquatic toxicity and chronic aquatic toxicity, the “Warning” signal word is used for Hazard Category 1.

## Slide 55: SIGNAL WORDS COLOR CODED FOR PHYSICAL HAZARDS
Physical Hazard Classes | Hazard Categories |  |  |  |  |  | 
Explosives | Unstable Explosives | Div. 1.1 | Div. 1.2 | Div. 1.3 | Div. 1.4 | Div 1.5 | Div 1.6
Flammable Gases | 1 | 2 |  |  |  |  | 
Flammable Aerosols | 1 | 2 |  |  |  |  | 
Oxidizing Gases | 1 |  |  |  |  |  | 
Gases Under Pressure | 1 |  |  |  |  |  | 
Flammable Liquids | 1 | 2 | 3 | 4 |  |  | 
Flammable Solids | 1 | 2 |  |  |  |  | 
Self Reactive Substances | Type A | Type B | Type C | Type D | Type E | Type F | Type G
Pyrophoric Liquids | 1 |  |  |  |  |  | 
Pyrophoric Solids | 1 |  |  |  |  |  | 
Self Heating Substances | 1 | 2 |  |  |  |  | 
Substances which in contact with water emit flammable gases | 1 | 2 | 3 |  |  |  | 
Oxidizing Liquids | 1 | 2 | 3 |  |  |  | 
Oxidizing Solids | 1 | 2 | 3 |  |  |  | 
Organic Peroxides | Type A | Type B | Type C | Type D | Type E | Type F | Type G
Corrosive to Metals | 1 |  |  |  |  |  | 
SIGNAL WORDS COLOR CODED FOR PHYSICAL HAZARDS
Notes: There are different signal words for different hazard categories of each physical hazard class. For example, for flammable gases “Danger” is used for Category 1 (in red) and “Warning” is used for Category 2 (in yellow). For organic peroxides, Types A, B, C and D warrant the “danger” signal word (in red), while Types E and F call for the “Warning” signal word (in yellow). Type G has no signal word, so it is colorless.

## Slide 56: SIGNAL WORDS COLOR CODED FOR HEALTH HAZARDS
Health Hazard Classes | Hazard Categories |  |  | 
Acute Toxicity | 1 | 2 | 3 | 4
Skin Corrosion/Irritation | 1A | 1B | 1C | 2
Serious Eye Damage/ Eye Irritation | 1 | 2A | 2B | 
Respiratory Sensitization | 1 |  |  | 
Skin Sensitization | 1 |  |  | 
Germ Cell Mutagenicity | 1A | 1B | 2 | 
Carcinogenicity | 1A | 1B | 2 | 
Reproductive Toxicology | 1A | 1B | 2 | Effects on or via lactation
Target Organ Systematic Toxicity (Single Exposure) | 1 | 2 | 3 | 
Target Organ Systematic Toxicity (Repeated Exposure) | 1 | 2 |  | 
Aspiration Toxicity | 1 |  |  | 
SIGNAL WORDS COLOR CODED FOR HEALTH HAZARDS
Notes: Signal words are also assigned to different hazard categories of each hazard class for health hazards. For example, for serious eye damage and eye irritation there are three different categories, and “Danger” is used for Category 1 (in red) and “Warning” is used for Category 2A and 2B (in yellow).

## Slide 57: Hazard Statement
Hazard statement describes the nature of the hazard(s) of a chemical for each hazard class (i.e., physical, health, environmental)
Examples
    “Causes serious eye damage through prolonged or repeated exposure.”
    “Toxic if inhaled.”
HAZARD STATEMENT
Notes: Hazard statements are standardized and are assigned phrases that describe the hazard(s) of a chemical for each category of hazard class . Examples are “Causes serious eye damage through prolonged or repeated exposure” and “Toxic if inhaled”.

## Slide 58: Precautionary Statement
Precautionary statement helps prevent or minimize adverse effects of hazardous chemical products during handling, transportation or storage
There are four types of precautionary statements
    Prevention (to minimize exposure)
    Response (what to do in case of exposure, e.g., first aid)
    Storage (requirements for storage)
    Disposal (consistent with regulations)
PRECAUTIONARY STATEMENT
Notes: Precautionary statements are recommended measures to be taken to prevent or minimize adverse effects of hazardous chemical products during handling, transportation or storage. Examples are “keep away from heat, sparks and open flames and store in a cool, well-ventilated place”, or “do not eat, drink or smoke when using this product”. (First aid is included in the precautionary information.) The GHS label should include all appropriate precautionary information. There are four types of precautionary statement: prevention which is used to minimize exposure; response is used to explain what to do in case of exposure; storage shows the requirements for storage and disposal; disposal shows how to dispose the chemical according to regulations.

## Slide 59: Supplementary Statements
Producer, importer or employer can add some helpful information and instructions to labels in the form of supplementary statements (optional)
Examples are
    Recommended Personal Protective Equipment (PPE)
    Ingredients in chemical products, etc.
SUPPLEMENTARY STATEMENTS
Notes: Supplementary statements are an optional section for labels. The label producer may provide additional instructions or information that it is deemed helpful. An example of an item that may be considered supplementary is the recommendation for using a certain type of personal protective equipment (PPE) by workers handling the chemical may need to wear to protect themselves. Another example may be information on the percentage of ingredients in chemical products.

## Slide 60: SAFETY DATA SHEET (SDS)
SDS is a document containing details of specific hazardous chemicals and their usage
HCS requires chemical manufacturers, distributors, or importers to provide SDS to communicate hazards of chemical products
Notes:   Safety Data Sheets (SDSs) are the complete resource for details regarding hazardous chemicals and how the product can be safely used. The HCS requires chemical manufacturers, distributors, or importers to provide SDS to communicate the hazards of hazardous chemical products.

## Slide 61: SAFETY DATA SHEETS
Updated SDSs should be
  shipped with the first shipment of the hazardous product
  made available to workers at all times in the workplace
If the employer notices that the SDS is not available,
  it is required that the manufacturer be informed immediately and the SDS be obtained as soon as possible.
  The manufacturer must send any SDS requested by a customer as soon as possible
Notes: The SDS should be shipped with the first shipment of the hazardous product after it is developed or updated. If the employer notices that SDS is not available, it is required that the manufacturer be informed immediately and the SDS be obtained as soon as possible. The manufacturer must send any SDS requested by a customer as soon as possible. Employers are required to make SDS(s) available to workers at all times in the workplace.

## Slide 62: SAFETY DATA SHEETS
Employers shall have a SDS in the workplace for each hazardous chemical used
SDS must be
  in English
  based on scientific evidence
  revised within 3 months when new information becomes available
Chemical manufacturers and importers shall obtain or develop a SDS for each hazardous chemical they produce or import.
Notes: Chemical manufacturers and importers shall obtain or develop a safety data sheet for each hazardous chemical they produce or import. Employers shall have a safety data sheet in the workplace for each hazardous chemical which they use. Safety data sheets must be in English, and they should be based on scientific evidence. If a manufacturer, importer or distributor becomes aware of a new hazard or information, it is required that the safety data sheet be updated within 3 months.

## Slide 63: SAFETY DATA SHEETS
There are 16 sections in HCS/GHS (12 are mandatory), which are as follows:
  Identification
  Hazard(s) identification
  Composition/information on ingredients
  First-Aid measures
  Fire-fighting measures
  Accidental release measures
  Handling and storage
Notes: The SDS should contain 16 headings, and 12 of these headings are mandatory. First, there should be information about identification of the substance or mixture and of the supplier, with emergency phone number, etc. Second, is the hazard(s) identification section which identifies the hazards of the chemical and the appropriate warning information associated with those hazards such as the hazard classification of the chemical (e.g., flammable liquid, category), signal word, hazard statement, pictogram and precautionary statement. The third section which is Composition/information on ingredients identifies the ingredient(s) contained in the product, including impurities and stabilizing additives such as chemical name, common name and synonym. In the following sections, the first aid measures section describes the initial care that should be given by untrained responders to an individual who has been exposed to the chemical. Fire fighting measures section gives recommendations about suitable extinguishing equipment and special protective equipment or precautions for firefighters, advice on specific hazards that develop from the chemical during the fire. Accidental release measures provides recommendations on the appropriate response to spills, leaks, or releases, including containment and cleanup practices to prevent or minimize exposure to people, properties, or the environment. Handling and storage section provides guidance on the safe handling practices and conditions for safe storage of chemicals.

## Slide 64: SAFETY DATA SHEETS
  Exposure controls/personal protection
  Physical and chemical properties
  Stability and reactivity
  Toxicological information
  Ecological information
  Disposal considerations
  Transport information
  Regulatory information
  Other information, including date of preparation or last revision
Non-mandatory
Notes: Exposure controls/personal protection section is about exposure limits recommended by OSHA, Permissible Exposure Limits (PELs), American Conference of Governmental Industrial Hygienists (ACGIH) Threshold Limit Values (TLVs) and manufacturers, engineering controls, and personal protective measures that can be used to minimize worker exposure. Physical and chemical properties section identifies physical and chemical properties associated with the substance or mixture such as appearance, odor, vapor pressure, pH, relative density, etc. Stability and reactivity section describes the reactivity hazards of the chemical and the chemical stability information such as description of the specific test data for the chemical, any stabilizers that may be needed to maintain chemical stability, etc. Toxicological information identifies toxicological and health effects information or indicates that such data are not available, such as information on the likely routes of exposure (inhalation, ingestion, skin and eye contact, description of the delayed, immediate, or chronic effects from short- and long-term exposure, etc). Ecological information, disposal considerations, transport information and regulatory information sections are non-mandatory and thus not enforced by OSHA. Ecological information section gives an idea about the ecological impact of the chemical if it is released to the environment, such as the potential for a substance to move from the soil to the groundwater, ozone layer depletion potential etc. Disposal considerations section provides guidance on proper disposal practices, recycling or reclamation of the chemical(s) or its container, etc. Transport information section includes information about classification for shipping and transporting of hazardous chemical(s) by road, air, rail, or sea, such as UN number (four-figure identification number of the substance), UN proper shipping name, etc. Regulatory information section identifies the safety, health, and environmental regulations specific for the product that is not indicated anywhere else on the SDS, such as any national and/or regional regulatory information of the chemical or mixtures (including any OSHA, Department of Transportation, Environmental Protection Agency, or Consumer Product Safety Commission regulations). Other information section is another mandatory section and it indicates when the SDS was prepared or when the last known revision was made. The SDS may also state where the changes have been made to the previous version. You may wish to contact the supplier for an explanation of the changes. Other useful information also may be included in this section

## Slide 65: SAFETY DATA SHEETS
Sample SDS (first two sections)
Notes: The sample shown above presents the first two sections of a typical safety data sheet.

## Slide 66: SAFETY DATA SHEETS
Every worker should study the pertinent SDSs before working with chemicals
If workers must travel between workplaces during a work shift, employer must ensure that employees can immediately obtain required SDS information in an emergency
If workers need additional information or have questions, they should ask their employers or supervisors
Notes: Every worker should study the SDS before working with chemicals. If workers must travel between workplaces during a work shift, the safety data sheets may be kept at the primary workplace. However, the employer must ensure that employees can immediately obtain the required information in an emergency. If worker needs additional information or have questions, they should ask their employers or supervisors.

## Slide 67: EMPLOYEE INFORMATION AND TRAINING
Employees should be informed about
  training requirements and information on chemicals they will work with
  operations in the workplace where hazardous chemicals are located and used
  location and availability of the written hazard communication program, safety data sheets, and list(s) of hazardous chemicals
Notes: Employees should be informed about employee information and training requirements, operations in the workplace where hazardous chemicals are located and used, as well as the location and availability of the written hazard communication program, safety data sheets, and list(s) of hazardous chemicals.

## Slide 68: EMPLOYEE INFORMATION AND TRAINING
Employees should be trained on
  methods and observations used to detect presence or release of hazardous chemicals in the workplace
  measures that employees can take to protect themselves from possible hazards
  details of the hazard communication program developed by employer, including
    labels on received containers
    labeling system of the employer
    safety data sheets, where to find them, and how to use the information in SDS.
Notes: Employees should be trained on methods and observations used to detect the presence or release of hazardous chemicals in the workplace, measures that employees can take to protect themselves from possible hazards, and the details of the hazard communication program developed by the employer, including labels on the received containers; labeling system of the employer; safety data sheets; where to find and how to use specific information in SDS, etc.

## Slide 69: TRADE SECRETS
Manufacturers, importers, or employers may withhold specific chemical identity including
  name of chemical
  exact percentage of ingredients
  other information about hazardous chemicals
Notes: Manufacturers, importers, or employers may withhold the specific chemical identity, including name of the chemical, exact percentage of ingredients, and other information about hazardous chemicals.
Figure Source: Susan Harwood grant number 22315-11-60-F-72, UNIVERSITY OF PUERTO RICO Río Piedras Campus Division of Continued Education and Professional Studies (DECEP)

## Slide 70: TRADE SECRETS
In case of emergency, for first aid treatment, manufacturer, importer or employer must immediately disclose
  chemical identity, and
  percentages of ingredients
  to treating physician or nurse without any confidentiality agreement
Notes: In case of emergency, for first aid treatment, manufacturer, importer or employer must immediately disclose the chemical identity and percentage of ingredients to the treating physician or nurse without any confidentiality agreement.

## Slide 71: TRADE SECRETS
In non-emergency situations; importer, manufacturer or employer may disclose information about chemical to health professional (providing medical or other health services to exposed workers), if the request
  is in writing
  has reasonable details
  includes a description of procedures to maintain confidentiality
If there is a dispute between parties regarding trade secrets, they can go to OSHA for resolution.
Notes: In non-emergency situations, the importer, manufacturer or employer may disclose the information about the chemical to the health professional providing medical or other health services to exposed workers, if the request is in writing, has reasonable details and includes a description of procedures to be used to maintain the confidentiality of the disclosed information. If there is a dispute between parties regarding trade secrets, they can go to OSHA for resolution.

## Slide 72: Effective dateas
Effective Completion Date | Requirement(s) | Who
December 1, 2013 | Train employees on the new label elements and safety data sheet (SDS) format. | Employers
June 1, 2015* December 1, 2015 | Compliance with all modified provisions of this final rule, except: The Distributor shall not ship containers labeled by the chemical manufacturer or importer unless it is a GHS label | Chemical manufacturers, importers, distributors and employers
June 1, 2016 | Update alternative workplace labeling and hazard communication program as necessary, and provide additional employee training for newly identified physical or health hazards. | Employers
Transition Period to the effective completion dates noted above | May comply with either 29 CFR 1910.1200 (the final standard), or the current standard, or both | Chemical manufacturers, importers, distributors, and employers
EFFECTIVE DATES
Notes: According to the revised hazard communication standard published on March 24, 2012, employers had to train their employees on the new label elements and safety data sheet format until December 1, 2013. Chemical manufacturers and distributors must reclassify their chemicals according to GHS guidelines and produce GHS formatted safety data sheets and labels until June 1, 2015 and after that they have six months to distribute the old inventory. After December 1, 2015, distributors shall not ship containers labeled by the chemical manufacturer or importer unless it is a GHS label. Workplace labeling and hazard communication program must be updated according to GHS, and additional employee training for newly identified physical or health hazards must be provided by the employers until June 1, 2016.
During the transition period, employers would be required to be in compliance with either the existing hazard communication standard or the revised standard with GHS, or both. OSHA recognizes that hazard communication programs will go through a period of time where labels and SDSs under both standards will be present in the workplace. This will be considered acceptable, and employers are not required to maintain two sets of labels and SDSs for compliance purposes.

## Slide 73: Summary
HCS classifies hazard as physical, health and environmental hazards
  Hazards are further classified based on severity
Employers are required to maintain a written hazard communication program in the workplace, and
  safety data sheets (SDS), labels and other forms of warning about the chemicals
  a list of existing chemicals using a product identifier
  training information about hazards of non-routine works (e.g., the cleaning of reactor vessels)
SUMMARY
Notes: Hazard communication standard classifies hazards as physical, health and environmental. Environmental hazards are not mandated by OSHA. These hazard classes are further classified based on their severity expressed by numbers and letters. In each workplace, employers are required to maintain a written hazard communication program which includes safety data sheets, labels or other forms of warning about the chemicals, a list of existing chemicals using a product identifier referenced on SDS, and training information on hazards of non-routine works, such as cleaning of reactor vessels.

## Slide 74: Summary 2
SDS must be
  available in the workplace
  in English
  based on scientific evidence
  revised within 3 months of when new information becomes available
Labels must be
  legible
  clearly displayed
  in English
  revised within 6 months of when new information becomes available
SUMMARY
Notes: The safety data sheets should always be available to workers in the workplace. SDS should be written in English; however, other languages can be added if needed. Information given should be based on scientific evidence. If new information becomes available, SDS should be updated by manufacturer, importer or distributor within three months. Labels on the containers should be legible and clearly displayed. Labels should be written in English; however, other languages can be added as additional information. It should be revised within six months when new information becomes available.

## Slide 75: end
THANK YOU!