## Slide 1: USF OTI Education Center Respirable Silica in the Construction Industry
Module 1

## Slide 2: Module 1: Introduction
This material was produced under grant number SH-29661-SH6 from OSHA. It does not necessarily reflect the views or policies of the U.S. Department of Labor, nor does mention of trade names, commercial products, or organizations imply endorsement by the U.S. Government.

## Slide 3: Module 1: Introduction
Course Opening
Objectives
Introductions
Housekeeping
Pre-test
Notes: The instructor will open with the description of the course:
This is a one day training session intended to educate frontline employees and foreman about OSHA’s new silica standard for the construction industry. This course will offer and overview of the new silica standard, as well as information on how to recognize, avoid and abate silica dust hazards. Participants will also learn allowable housekeeping techniques, as well as participating in a hands on workshop regarding respiratory protection use. Participant’s level of knowledge will be tested by administering a pretest and posttest.
Objectives are:
Trainees will be able to describe the requirements of the new silica standard for construction
Enabling Objective:
Identify general differences between the old and new silica standard
Identify general the areas of the new standard that trainees should be concerned
Enabling objectives:
Identify basic health risks, both short and long-term, associated with silica exposure
Identify basic activities likely to expose workers to silica exposure
Identify general differences between engineering and administrative controls and PPE Enabling Objectives:
Identify basic types of PPE used to reduce health hazards associated with silica exposure
Identify importance of respiratory protection
Identify proper use of respiratory protection
Identify when to perform and how to perform a user seal check
Identify how to maintain and care for respiratory protection
Identify when it is time to replace/change a respirator
Upon successful completion of this course the participant will receive a course certificate of attendance. Instructor is to provide a basic background and history on themselves. This should include experience in construction working around silica based materials.
Inform the students that they will take the pretest at the end of this section.
Advance to next slide to discuss housekeeping issues for the classroom.

## Slide 4: Module 1: Introduction (continued)
Instructor Contact Information
Attendance Requirements
Personal Expectations
Emergency Exits
Notes: Instructor shall provide contact information incase of emergencies.
Instructor shall inform the students of the attendance requirements. Students can not miss more than 10% of the class to receive credit.
Students shall provide a short introduction to include their name, company, personal expectations for the class, and how they work with Silica Based material.
Instructor shall go over the emergency procedures and exits.
Advance to the next slide.

## Slide 5: Module 1: Introduction (continued)
The nearest restroom is………
Course management requests that you switch all cell phones to “silent mode” so everyone may enjoy the educational sessions without interruption.
This is a non-smoking facility.
You may go outside if you wish to smoke.
Notes: Instructor shall identify the restrooms for the students.
Ensure that all cellular devices are turned off or placed into the silent mode to prevent from disturbing the class. Inform the students that if they need to take a call or answer text, they should leave the room.
USF is a non-smoking facility and students are not permitted to use any tobacco products or vapor smoking devices in the classroom. They must also follow the facility rules on smoking locations.
Advance to the next slide.

## Slide 6: Module 1: Introduction (continued)
NO Tape Recording
Use of computers during presentations
Breaks and Course Matrix
Standard of Conduct
Notes: Instructor shall inform students of the general rules and expectations:
There is NO use of any recording devices either for sound or video while in the classroom. All materials are the property of USF OTI and may not be reproduced without the exclusive written authority of the USF OTI.
Computers are not required in this course and should not be used during class.
Regular breaks will be provided throughout the course including a lunch.
All students are reminded that all class discussions and comments must keep diversity in mind and refrain from making comments that maybe offensive to any student or the instructor. Please maintain a professional attitude.
Advance to the next slide.

## Slide 7: Schedule
Notes: The instructor shall go over the course matrix schedule.
Advance to the next slide.

## Slide 8: Module 1: Introduction (continued)
Pre-test
Notes: Instructor will have the students take the Silica Pretest and review the answer after all student have completed the test.
Begin tab 2

## Slide 9: USF OTI Education Center Respirable Silica in the Construction Industry
Module 2

## Slide 10: Module 2
This material was produced under grant number SH-29661-SH6 from OSHA. It does not necessarily reflect the views or policies of the U.S. Department of Labor, nor does mention of trade names, commercial products, or organizations imply endorsement by the U.S. Government.
OSH ACT, Silica Standard, Table 1, and Overview
Notes: Instructor shall review the Susan Harwood Training Grant Program.
Advance to next slide

## Slide 11: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
OSHA awards grants to nonprofit organizations on a competitive basis through its Susan Harwood Training Grant Program.
Grants are awarded to provide training and education programs for employers and workers on the recognition, avoidance, and prevention of safety and health hazards in their workplaces and to inform workers of their rights and employers of their responsibilities under the Occupational Safety and Health (OSH) Act.
Notes: Instructor shall review the Susan Harwood Training Grant Program.
OSHA awards grants to nonprofit organizations on a competitive basis through its Susan Harwood Training Grant Program. Grants are awarded to provide training and education programs for employers and workers on the recognition, avoidance, and prevention of safety and health hazards in their workplaces and to inform workers of their rights and employers of their responsibilities under the Occupational Safety and Health (OSH) Act.
Advance to the next slide.

## Slide 12: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
Solicitation for the Susan Harwood Grant Program is a function of Congressional budgetary approval and appropriation by the Department of Labor.
In 1997, the program was re-named in honor of the late Susan Harwood, a former director of the Office of Risk Assessment in OSHA's Health Standards Directorate, who died in 1996. During her 17-year tenure with the agency, Harwood helped develop OSHA standards to protect workers exposed to bloodborne pathogens, cotton dust, benzene, formaldehyde, asbestos and lead in construction.
Notes: Instructor shall continue to review the Susan Harwood Training Grant Program.
Solicitation for the Susan Harwood Grant Program is a function of Congressional budgetary approval and appropriation by the Department of Labor. In 1997, the program was re-named in honor of the late Susan Harwood, a former director of the Office of Risk Assessment in OSHA's Health Standards Directorate, who died in 1996. During her 17-year tenure with the agency, Harwood helped develop OSHA standards to protect workers exposed to bloodborne pathogens, cotton dust, benzene, formaldehyde, asbestos and lead in construction.
USF OTI was awarded this grant to provide educational materials and classes to the public and companies that are interested in understanding Respirable Silica Standard and protecting themselves and their employees from this harmful substance.
Advance to the next slide.

## Slide 13: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
Terminal Objective:
  Students will be able to describe the purpose of the Susan Harwood Training Grant Program.
Enabling Objective:
  Identify basic Workers Rights and Employer Responsibilities under the OSH Act.
  Recognize that employees have a right to voice safety and health concerns free from retaliation.
  Describe how to file a complaint.
Notes: Instructor to review the Objectives with the students.
Terminal Objective:
  Students will be able to describe the purpose of the Susan Harwood Training Grant Program
Enabling Objective:
  Identify basic Workers Rights and Employer Responsibilities under the OSH Act
  Recognize that employees have a right to voice safety and health concerns free from retaliation
  Describe how to file a complaint
  Advance to the next slide.

## Slide 14: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
Objective:
  Define respirable crystalline silica;
  Describe how to use Table 1.
Notes: Instructor to review the Objectives with the students.
Objective:
  Define respirable crystalline silica.
  Describe how to use table 1.
Advance to the next slide.

## Slide 15: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
OSHA’s Mission is to assure safe and healthful working conditions for working men and women by setting and enforcing standards and by providing training, outreach, education and assistance.
Some of the things OSHA does to carry out its mission are:
  Developing job safety and health standards and enforcing them through worksite inspections
  Providing training programs to increase knowledge about occupational safety and health
Notes: Instructor shall discuss The Mission of OSHA with students. OSHA was first signed into law in 1970 and became effective in April of 1971 by President Richard Nixon. OSHA has been working to fulfil it mission to:
It is to assure safe and healthful working conditions for working men and women by setting and enforcing standards and by providing training, outreach, education and assistance.
Some of the things OSHA does to carry out its mission are:
  Developing job safety and health standards and enforcing them through worksite inspections. This is the congressional and enforcement sides of OSHA.
  Providing training programs to increase knowledge about occupational safety and health. This is part of the role of USF OTI along with providing consultation services to help small employer meet the requirements of the OSH Act.
Advance to the next slide.

## Slide 16: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
Employers have the responsibility to:
Provide a workplace free from recognized hazards and comply with OSHA standards;
Provide training required by OSHA standards;
Keep records of injuries and illnesses;
Provide medical exams when required by OSHA standards and provide workers access to their exposure and medical records;
Not discriminate against workers who exercise their rights under the Act (Section 11(c));
Post OSHA citations and hazard correction notices and;
Provide and pay for most PPE.
Notes: Instructor shall review the Employer Responsibilities with the students.
Every employer is responsible for the following:
Provide a workplace free from recognized hazards and comply with OSHA standards,
Provide training required by OSHA standards, employees are to be trained in any activity and about the hazards of that activity or chemicals use.
Keep records of injuries and illnesses, that happen at work.
Provide medical exams when required by OSHA standards and provide workers access to their exposure and medical records, things like silica, lead, hexavalent, hearing, and others require medical testing on a regular basis.
Not discriminate against workers who exercise their rights under the Act (Section 11(c)), employees have the right to report employers that do not address hazards in the workplace once identified.
Post OSHA citations and hazard correction notices,
Provide and pay for most PPE that is required for the task.
Advance to the next slide.

## Slide 17: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
Employees have the right to:
  A safe and healthful workplace;
  Know about hazardous chemicals;
  Report injury to employer;
  Complain or request hazard correction from employer;
  Training;
  Hazard exposure and medical records;
  File a complaint with OSHA;
  Participate in an OSHA inspection, and;
  Employees are supposed to adhere to employers’ safety and health polices and procedures, and;
  Be free from retaliation for exercising safety and health right.
Notes: Instructor shall discuss the Employee Rights:
  A safe and healthful workplace
  Know about hazardous chemicals, Hazardous Communication on the chemicals that employees work with and are exposed to.
  Report injury to employer, employees are responsible to report their injuries to the employer.
  Complain or request hazard correction from employer, if there is a hazard employees have the responsibility to report hazards and expect correction. If the employer refuse to correct the condition the employee has the right to report the condition to OSHA without fear of retaliation.
  Training, every employee has the right to be trained by the employer on all task and hazards.
  Hazard exposure and medical records, employees have the right to review and have copies of all of their own medical records related to work.
  File a complaint with OSHA.
  Participate in an OSHA inspection, employee have the right to speak to and walk with OSHA during inspections.
  Be free from retaliation for exercising safety and health right, each employee has the responsibility and right to report hazards with out fear of being fired, change of duty, or any other retaliation.
Advance to the next slide.

## Slide 18: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
Health and Safety:
Workers may ask about safety and health concerns in the workplace to their employers without fear of discharge or discrimination.
OSHA rules protect workers who raise concerns to their employer or OSHA about unsafe or unhealthful conditions in the workplace.
Notes: Instructor will discuss the OSHA 11(c) and how it protects the employees from retribution for reporting unsafe or unhealthy conditions.
The 11(c) of the OSHA Act provides protection for employees to report unsafe or unhealthy conditions.
Advance to the next slide.

## Slide 19: What are OSHA Standards?
OSHA standards are:
Rules that describe the methods employers must use to protect employees from hazards.
Designed to protect workers from a wide range of hazards.
Where there are no specific standards, employers must comply with the General Duty Clause of the OSH Act.
Notes: Instructor shall discuss how OSHA standards are: Rules that describe the how employers must protect employees from hazards. They are designed to protect workers from a wide range of hazards. Focus on the Construction, General, maritime, and agriculture Industries. In cases where there are no specific rules to protect workers, the OSHA 5(a)(1) gives a General Duty for employers to protect the workers from all know hazards.
Advance to the next slide.

## Slide 20: Module 2: OSHA Standards
These standards also:
Limit the amount of hazardous chemicals, substances, or noise that workers can be exposed to;
Require the use of certain safe work practices and equipment, and;
Require employers to monitor certain hazards and keep records of workplace injuries and illnesses.
Notes: These OSHA standards also:
Limit the amount of hazardous chemicals, substances, or noise that workers can be exposed to based on data that shows negative or harmful effects.
Require the use of certain safe work practices and equipment and employers are required to monitor certain hazards and keep records of workplace injuries and illnesses.
Employees have the right to review these records and the records of medical exams.
Advance to the next slide.

## Slide 21: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
How to file a complaint
Download the OSHA complaint form from OSHA’s website.
File the complaint online:
  Workers can file a complaint
  A worker representative can file a complaint
Telephone or visit local regional or area offices to discuss your concerns.
Complete the form – be specific and include appropriate details.
OSHA determines if an inspection is necessary.
Workers do not have to reveal their name.
Notes: Instructor is to discuss how to file a complaint with OSHA when there is a hazardous situation that the employer has not addressed adequately or corrected. Employees can call or go on the website to file a complaint about their employer after bringing it to the attention of the employer. The employee does not have to provide their name when making the complaint. They do need to be as specific as possible to ensure that the hazard is clearly identified and OSHA can address the issue based on a rule or OSHA 5(a) general duty clause if there is not specific standard.
Advance to the next slide.

## Slide 22: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
The final Silica rule took effect on June 23, 2016 after which industries have to comply with most requirements, based on the following schedule:
Construction – June 23, 2017
General Industry and Maritime – June 23, 2018;
Hydraulic Fracturing – June 2018 for all provisions except engineering controls which have a compliance date of June 23, 2021.
Notes: Instructor is to discuss when the new Silica rule took effect and when each industry will need to be in compliance.
The final Silica rule took effect on June 23, 2016 after which industries have one to five years to comply with most requirements, based on the following schedule:
Construction – June 23, 2017, This is the first part of the updated standard that will go into effect and the focus of this course.
General Industry and Maritime – June 23, 2018
Hydraulic Fracturing – June 2018 for all provisions except engineering controls which have a compliance date of June 23, 2021.
Advance to the next slide.

## Slide 23: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
What is Respirable Crystalline Silica?
Crystalline silica is a common mineral found in many naturally occurring and man-made materials used at construction sites.
Materials like sand, concrete, brick, block, stone and mortar contain crystalline silica.
Notes: Instructor will discuss What is Respirable Crystalline Silica?
Crystalline silica is a common mineral found in many naturally occurring and man-made materials used at construction sites. Materials like sand, concrete, brick, block, stone and mortar contain crystalline silica. Amorphous silica, such as silica gel, is not crystalline silica. Sand or soil is not a harmful form of silica either in its natural state. These particles are far to large to breathe in.
Advance to the next slide.

## Slide 24: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
Respirable crystalline silica is a very small particle typically at least 100 times smaller than ordinary sand found on beaches or playgrounds.
It is generated by operations like:
- cutting sawing
- grinding
- drilling and crushing stone, rock, concrete, brick, block and mortar, or when abrasive blasting with sand.
Notes: Instructor shall cover the size and where respirable silica comes from.
The problem lies with Respirable crystalline silica which is a very small particles, typically at least 100 times smaller than ordinary sand found on beaches or playgrounds – it is generated by high-energy operations like cutting, sawing, grinding, drilling and crushing stone, rock, concrete, brick, block and mortar, or when abrasive blasting with sand. Basically, when we break down larger sand or quarts grains. These particles become small enough to be able to float in the air, then were able to breathe them into our lungs, where many of the problems begin.
Advance to the next slide.

## Slide 25: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
The standard applies to all occupational exposures to respirable crystalline silica in construction work, except where employee exposure will remain below 25 μg/m3 as an 8-hour TWA under any foreseeable conditions.
Exposures to respirable crystalline silica occur when the following tools are used on:
- concrete
- brick
- block, stone, mortar, and other materials that contain crystalline silica
Notes: Instructor shall discuss the exposures:
Over the next few slides some of the exposures are discussed.
The standard applies to all occupational exposures to respirable crystalline silica in construction work, except where employee exposure will remain below 25 μg/m3 as an 8-hour TWA under any foreseeable conditions.
Exposures to respirable crystalline silica occur when the following tools are used on concrete, brick, block, stone, mortar, and other materials that contain crystalline silica:
Stationary masonry saws;
Handheld power saws;
Walk-behind saws;
Drivable saws;
Rig-mounted core saws or drills;
Handheld and stand-mounted drills (including impact and rotary hammer drills);
Dowel drilling rigs;
Vehicle-mounted drilling rigs;
Handheld grinders;
Jackhammers and handheld powered chipping tools;
Handheld grinders;
Walk-behind milling machines and floor grinders;
Drivable milling machines;
Crushing machines; and
Heavy equipment and utility vehicles when used to abrade or fracture silica containing materials (such as hoe-ramming or rock ripping) or during demolition activities, and for tasks such as grading and excavating.
Exposures to respirable crystalline silica also occur during tunneling operations and
during abrasive blasting when sand or other blasting agents containing crystalline silica are used, or when abrasive blasting is performed on substrates that contain crystalline silica, such as concrete.
Advance to the next slide.

## Slide 26: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
Stationary masonry saws;
Handheld power saws;
Walk-behind saws;
Drivable saws;
Rig-mounted core saws or drills;
Handheld and stand-mounted drills (including impact and rotary hammer drills);
Dowel drilling rigs;
Vehicle-mounted drilling rigs;
Handheld grinders;
Notes: Instructor shall continue reviewing the list of exposures.
Advance to the next slide.

## Slide 27: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
Jackhammers and handheld powered chipping tools;
Handheld grinders;
Walk-behind milling machines and floor grinders;
Drivable milling machines;
Crushing machines, and;
Heavy equipment and utility vehicles when used to abrade or fracture silica containing materials (such as hoe-ramming or rock ripping) or during demolition activities, and for tasks such as grading and excavating.
Notes: Instructor shall continued reviewing the list of exposures.
Advance to the next slide.

## Slide 28: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
Exposures to respirable crystalline silica also occur during tunneling operations and;
During abrasive blasting when sand or other blasting agents containing crystalline silica are used, or when abrasive blasting is performed on substrates that contain crystalline silica, such as concrete.
Notes: Instructor shall continued list of exposures.
Advance to the next slide.

## Slide 29: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
The U.S. Department of Labor (D.O.L.) first highlighted the hazards of respirable crystalline silica in the 1930s, after a wave of worker deaths.
The D.O.L. set standards to limit worker exposure in 1971, when OSHA was created. However, the standards are outdated and did not adequately protect workers from silica-related diseases.
Notes: The instructor will discuss the DOL knowledge of Silica hazard:
Crystalline silica is not new, this is been around for many years. The U.S. Department of Labor first highlighted the hazards of respirable crystalline silica in the 1930s, after a wave of worker deaths. The department set standards to limit worker exposure in 1971, when OSHA was created. However, the standards are outdated and did not adequately protect workers from silica-related diseases. Lets look at some history.
Advance to the next slide.

## Slide 30: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
Please click PLAY button or cut and paste link in to your browser to watch video on deadly dust https://youtu.be/oMduqVTFkBQ?t=145
Notes: Press start to start video.
In this video on Deadly Dust, from the DOL, the director discuss the original Silica report and the hazards. There is historical information on Bill Ellis, a typical painter and sand blaster from Tenn. Where he raised his family. He died of Silicosis in 2004. Dr. William Beckett, attending physician at Mount Auburn Hospital, speaks to health issues associated to silicosis. Dr. David Michaels, assistant secretary of labor for OSHA, discusses how exposure to silica is deadly. The short film shows exposure routs and effects of silicosis. Lanny Wade, safety consultant, speaks on silicosis signs and symptoms, giving an example of how difficult it is to breath. There is a section on Gary Sassi, a stone cutter. His father had passed from silicosis. David Michaels then speaks to the OSHA regulations and how precautions need to be applied across the board. Using techniques to prevent exposure. There are still people dying from Silicosis across the US. Even though these number have gone down over the years, but there are still people dying from silicosis each year. Bob Pritchard, Director of Safety for Western Construction Group points out that workers cutting and grinding on construction sites can pose a exposure to silica dust. Cyclonic vacuums have proven to be a valuable tool in removing silica dust. A superintendent from Western Waterproofing had a chance to work with the cyclonic vacuum system and felt that he was able to return home after working without exposure. Jake Davidson a Tuckpointer/Foreman discusses how his work produces large amount of silica dust, they use vacuum systems to control the dust exposure. A veteran of Granite Industry, Bernie Scott tells how his coworkers have died and had difficulty breathing. Michael Mangum, the Program Director, National Asphalt Pavement Association (NAPA) Worker Health and Safety Partnerships, discuss the need to protect the American workers and make the point that protecting the workers, protects the company. Bill Hohmeier, branch Manager, Western Waterproofing, stresses safety, financial, company stability. Reminding the worker that they want them to leave work in the same shape that they arrived at work. Dr. William Beckett, continues to discuss how he saw his first patients in the 1970s with Silicosis and how he thought that would be the last generation with this disease. He is still seeing these cases and people are still dying due to the exposure to silica. There is still no treatment so prevention is the key. OSHA estimates that hundreds of lives will be saved with the implementation of the new standard. The film then returns to the widow of Bill, an average American worker, where she remembers her husband and looks to share the message that preventing exposure to silica is the only acceptable answer.
Advance to the next slide.

## Slide 31: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
Workers are also being exposed to silica in new industries such as:
- stone or;
- artificial stone countertop fabrication and;
- hydraulic fracturing.
Notes: Instructor shall discuss new industry hazards:
There are new popular industries that are exposing workers to high levels of silica dust, stone or artificial stone countertop fabrication and hydraulic fracturing. Some of the new man-made stone countertops contain more silica than the naturally occurring rock.
Advance to the next slide.

## Slide 32: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
OSHA issued an updated final rule to control:
- lung cancer, silicosis, chronic obstructive pulmonary disease and;
- kidney disease in America's workers by limiting their exposure to respirable crystalline silica.
Notes: Instructor shall discuss why OSHA updated the standard:
The Occupational Safety and Health Administration (OSHA) issued an updated final rule to control lung cancer, silicosis, chronic obstructive pulmonary disease and kidney disease in America's workers by limiting their exposure to respirable crystalline silica. We are still seeing a large number of cases of silicosis among workers with cases of silicosis and cancer directly related to exposure to crystalline silica. Workers are still being exposed to crystalline silica through many of the same processes of cutting, grinding, breaking, and crushing.
Advance to the next slide.

## Slide 33: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
The rule is comprised of two standards:
- One for Construction and;
- One for General Industry and Maritime.
Notes: Instructor shall cover that the rule is based on two standards:
The rule is comprised of two standards, one for Construction and one for General Industry and Maritime. No rule currently controls the exposure in Agriculture, but the exposure is generally low.
Advance to the next slide.

## Slide 34: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
OSHA estimates that the rule will save over 600 lives and prevent more than 900 new cases of silicosis each year, once its effects are fully realized.
The Final Rule is projected to provide net benefits of about $7.7 billion, annually.
Notes: Instructor shall discuss how updating the rule will save lives and save money:
Based on studies, OSHA currently estimates that the new rule will save over 600 lives and prevent more than 900 new cases of silicosis each year, once its effects are fully realized. The Final Rule is projected to provide net benefits of about $7.7 billion, annually. We have to look at this data with a full understanding that even one life is too many.
Advance to the next slide.

## Slide 35: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
About 2.3 million workers are exposed to respirable crystalline silica in their workplaces;
Two million construction workers who drill, cut, crush, or grind silica-containing materials such as concrete and stone, and;
300,000 workers in general industry operations such as brick manufacturing, foundries, and hydraulic fracturing.
Notes: Instructor shall discuss the number of workers currently estimated to be exposed to silica in the US
Currently about 2.3 million workers are exposed to respirable crystalline silica in their workplaces, including 2 million construction workers who work with silica-containing materials such as concrete and stone, and approximately another 300,000 workers in general industry operations such as brick manufacturing, foundries, and hydraulic fracturing, also known as fracking contribute to the number of workers being exposed each year.
Advance to the next slide.

## Slide 36: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
Many employers have been protecting workers from harmful exposure to respirable crystalline silica for years, using widely-available equipment that controls dust with water, or a vacuum system.
Notes: Instructor shall discus how some employers have been using these methods to protect workers:
Again this is not a new hazard, many responsible employers have been protecting workers from harmful exposure to respirable crystalline silica for years, using widely-available equipment that controls dust with water or a vacuum system. There are many tools and types of equipment manufactured for use with materials that contain silica to prevent employee exposures from this harmful substance.
Advance to the next slide.

## Slide 37: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
Employer need to determine if the standard applies to their work.
If it is work covered by the standard, an employer has two options for limiting employee exposure to respirable crystalline silica:
- Specified exposure control methods or;
- Alternative exposure control methods.
Notes: Instructor shall discus how:
The first step for an employer is to determine if the standard applies to its work.
If its work is covered by the standard, an employer has two options for limiting employee exposure to respirable crystalline silica:
Specified exposure control methods; or
Alternative exposure control methods.
Advance to the next slide.

## Slide 38: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
Are employees being exposed to respirable crystalline silica at or above 25 µg/m3 as an 8-hour TWA under any foreseeable conditions, including the failure of engineering controls, while performing construction activities?
No: No further action is required under the silica standard.
Yes: Choose to comply with the standard using either the:
  Specified exposure control methods in Table 1, or
  The alternative methods of compliance
Notes: Instructor shall discus the employers exposure decision tree:
We 1st have to determine if employees are being exposed to respirable crystalline silica at or above 25 µg/m3 as an 8-hour TWA under any foreseeable conditions, including the failure of engineering controls, while performing activities?
If No: Then no further action is required under the silica standard.
If Yes: Then the company may choose to comply with the standard using either the:
  Specified exposure control methods in Table 1, or
  The alternative methods of compliance.
Either of the 2 methods is acceptable as long as the employees exposure is being reduced for limited below the action level.
Advance to the next slide.

## Slide 39: Module 2: OSHA ACT, Silica Standard, Table 1, and Overview
Notes: Instructor shall go over the chart to see if they need to comply or which method they can use:
This chart is a table to see if a company must follow the standard requirements. If they do, it will list what requirement based on task. Go over the elements of the chart. Focus on the requirements section, implementation from Table 1 and alternative exposure controls. Going over a few of these set the class can see how to use it.
Advance to the next slide.

## Slide 40: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
The standard does not apply where employee exposure will remain below 25 μg/m3 as an 8-hour TWA under any foreseeable conditions.
Notes: Instructor shall discus how:
The standard does not apply where employee exposure will remain below 25 μg/m3 as an 8-hour TWA under any foreseeable conditions.
Note: “any foreseeable conditions” refers to situations that can reasonably be anticipated. OSHA considers failure of engineering controls to be a situation that is reasonably foreseeable.
Advance to the next slide.

## Slide 41: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
Employee exposure can reasonably be anticipated to remain below 25 μg/m3 as an 8-hour TWA when performing certain tasks that involve only minimal exposure to respirable crystalline silica. Such tasks include:
Mixing concrete for post holes;
Pouring concrete footers, slab foundation, and foundation walls, and ;
Removing concrete formwork.
Notes: Instructor shall discus task that are expected to reasonably expose employees to higher levels of silica:
When these tasks are performed in isolation from tasks that generate significant exposures to respirable crystalline silica, the standard does not apply. These examples are not exclusive, and there may be other tasks that involve exposure under 25 μg/m3 as an 8-hour TWA under any foreseeable conditions.
Advance to the next slide.

## Slide 42: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
DEFINITIONS
Notes: Now we are going to go through a few of the definitions that you'll need to understand the before we continue.
Advance to the next slide.

## Slide 43: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
Action level - an airborne concentration of 25 μg/m3 calculated as an 8-hour TWA. Exposures at or above the action level trigger requirements for exposure assessment.
Notes: Instructor will go over definitions:
Action level - an airborne concentration of 25 μg/m3 calculated as an 8-hour TWA. Exposures at or above the action level trigger requirements for exposure assessment. Remember this is calculated over an 8 hour period, as an average throughout the day. You may have periods where it is higher or lower than the 25 µg. Just to give you an example, if you take the tip of the ballpoint pen and dipped it in powdered sugar you would be far above the 50 µg that is the maximum for exposure to crystalline silica.
Advance to the next slide.

## Slide 44: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
Competent person - an individual who is capable of identifying existing and foreseeable respirable crystalline silica hazards in the workplace and who has authorization to take prompt corrective measures to eliminate or minimize them.
The competent person must have the knowledge and ability necessary to implement the written exposure control plan required under the standard.
Notes: Instructor will go over definitions:
The definition in the silica standard for competent person is a little bit different than it is in some of the other standards that you may already be used to.
Competent person – is an individual who is capable of identifying existing and foreseeable respirable crystalline silica hazards in the workplace and who has authorization to take prompt corrective measures to eliminate or minimize them. The competent person must have the knowledge and ability necessary to implement the written exposure control plan required under the standard. There is no specific training requirement for the competent person within the standard.
Advance to the next slide.

## Slide 45: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
Employee exposure - the exposure to airborne respirable crystalline silica that would occur if the employee were not using a respirator.
Notes: Instructor will go over definitions:
Employee exposure - the exposure to airborne respirable crystalline silica that would occur if the employee were not using a respirator.
Advance to the next slide.

## Slide 46: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
High-efficiency particulate air (HEPA) filter - a filter that is at least 99.97 % efficient in removing mono-dispersed particles of 0.3 micrometers in diameter. HEPA-filtered vacuuming is an example of a housekeeping method that minimizes employee exposure to respirable crystalline silica, and some Table 1 tasks require HEPAfiltered vacuuming.
Notes: Instructor will go over definitions:
High-efficiency particulate air (HEPA) filter - a filter that is at least 99.97 percent efficient in removing mono-dispersed particles of 0.3 micrometers in diameter. HEPA-filtered vacuuming is an example of a housekeeping method that minimizes employee exposure to respirable crystalline silica, and some Table 1 tasks require HEPA filtered vacuuming. Remember, this is much different than a normal vacuum, it has a much higher efficiency in containing the material being vacuumed up within the container.
Advance to the next slide.

## Slide 47: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
Objective data - information, such as air monitoring data from industrywide surveys or calculations based on the composition of a substance, demonstrating employee exposure to respirable crystalline silica associated with a particular product or material or a specific process, task, or activity.
The data must reflect workplace conditions closely resembling or with a higher exposure potential than the processes, types of material, control methods, work practices, and environmental conditions in the employer’s current operations.
Notes: Instructor will go over definitions:
Objective data is sometimes referred to as historical data.
Objective data – is information, such as air monitoring data from industrywide surveys or calculations based on the composition of a substance, demonstrating employee exposure to respirable crystalline silica associated with a particular product or material or a specific process, task, or activity. The data must reflect workplace conditions closely resembling or with a higher exposure potential than the processes, types of material, control methods, work practices, and environmental conditions in the employer’s current operations.
Advance to the next slide.

## Slide 48: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
Physician or other licensed health care professional [PLHCP] is an individual whose legally permitted scope of practice (i.e., license, registration, or certification) allows him or her to independently provide or be delegated the responsibility to provide some or all of the particular healthcare services required by this standard.
Notes: Instructor will go over definitions:
Physician or other licensed health care professional [PLHCP] is an individual whose legally permitted scope of practice (i.e., license, registration, or certification) allows him or her to independently provide or be delegated the responsibility to provide some or all of the particular healthcare services required by this standard.
Advance to the next slide.

## Slide 49: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
Specialist means an American Board Certified Specialist in Pulmonary Disease or an American Board Certified Specialist in Occupational Medicine
Notes: Instructor will go over definitions:
Specialist means an American Board Certified Specialist in Pulmonary Disease or an American Board Certified Specialist in Occupational Medicine
Advance to the next slide.

## Slide 50: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
Respirable crystalline silica - quartz, cristobalite, and/or tridymite contained in airborne particles that are determined to be respirable by a sampling device designed to meet the characteristics for respirable-particle-size-selective samplers specified in the International Organization for Standardization (ISO) 7708:1995: Air Quality – Particle Size Fraction Definitions for Health-Related Sampling
Notes: Instructor will go over definitions:
Respirable crystalline silica - quartz, cristobalite, and/or tridymite contained in airborne particles that are determined to be respirable by a sampling device designed to meet the characteristics for respirable-particle-size-selective samplers specified in the International Organization for Standardization (ISO) 7708:1995: Air Quality – Particle Size Fraction Definitions for Health-Related Sampling. Quarts is the most common out of these 3, found in many substances. The other 2 are less frequent, but may be found in some the substances that you work with.
Advance to the next slide.

## Slide 51: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
Table 1
Notes: The following slides are Table 1, of the silica standard and is based on task and protective measures required or the PPE that is a suitable substitute.
Advance to the next slide.

## Slide 52: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
*pictures obtained from www.lhsfna.org
Notes: Instructor will go over details and use of Table 1:
At this time were just going to look at the equipment or task in the 1st column. There are 18 different items listed on this table. Table 1 contains the most common task using tools to break material that contain silica. We will focus on the other sections later in this course. You have a copy of table one in your box in a separate handout so that we can use this during exercises later.
(i) Stationary masonry saws
Use saw equipped with integrated water delivery system that continuously feeds water to the blade. Operate and maintain tool in accordance with manufacturer’s instructions to minimize dust emissions.
(ii) Handheld power saws (any blade diameter)
Use saw equipped with integrated water delivery system that continuously feeds water to the blade. Operate and maintain tool in accordance with manufacturer’s instructions to minimize dust emissions . − When used outdoors. − When used indoors or in an enclosed area.
Advance to the next slide.

## Slide 53: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
(iii) Handheld power saws for cutting fiber cement board *with blade diameter of 8 inches or less | For tasks performed outdoors only: Use saw equipped with commercially available dust collection system. Operate and maintain tool in accordance with manufacturer's instructions to minimize dust emissions. Dust collector must provide the air flow recommended by the tool manufacturer, or greater, and have a filter with 99% or greater efficiency. | None | None
(iv) Walk-behind saws | Use saw equipped with integrated water delivery system that continuously feeds water to the blade. Operate and maintain tool in accordance with manufacturer's instructions to minimize dust emissions. − When used outdoors. − When used indoors or in an enclosed area | None APF 10 | None APF 10
(v) Drivable saws | For tasks performed outdoors only: Use saw equipped with integrated water delivery system that continuously feeds water to the blade. Operate and maintain tool in accordance with manufacturer's instructions to minimize dust emissions | None | None
Notes: Instructor will go over details and use of Table 1:
Focus on the 1st column with the tools for this section.
(iii) Handheld power saws for cutting fibercement board (with blade diameter of 8 inches or less)
For tasks performed outdoors only: Use saw equipped with commercially available dust collection system. Operate and maintain tool in accordance with manufacturer's instructions to minimize dust emissions. Dust collector must provide the air flow recommended by the tool manufacturer, or greater, and have a filter with 99% or greater efficiency.
(iv) Walk-behind saws
Use saw equipped with integrated water delivery system that continuously feeds water to the blade. Operate and maintain tool in accordance with manufacturer's instructions to minimize dust emissions. − When used outdoors. − When used indoors or in an enclosed area
(v) Drivable saws
For tasks performed outdoors only: Use saw equipped with integrated water delivery system that continuously feeds water to the blade. Operate and maintain tool in accordance with manufacturer's instructions to minimize dust emissions
Advance to the next slide.

## Slide 54: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
(vi) Rig-mounted core saws or drills | Use tool equipped with integrated water delivery system that supplies water to cutting surface. Operate and maintain tool in accordance with manufacturer's instructions to minimize dust emissions. | None | None
(vii) Handheld and stand-mounted drills (including impact and rotary hammer drills) | Use drill equipped with commercially available shroud or cowling with dust collection system. Operate and maintain tool in accordance with manufacturer's instructions to minimize dust emissions. Dust collector must provide the air flow recommended by the tool manufacturer, or greater, and have a filter with 99% or greater efficiency and a filter-cleaning mechanism. Use a HEPA-filtered vacuum when cleaning holes | None | None
Notes: Instructor will go over details and use of Table 1:
Focus on the 1st column with the tools for this section.
(vi) Rig-mounted core saws or drills
Use tool equipped with integrated water delivery system that supplies water to cutting surface. Operate and maintain tool in accordance with manufacturer's instructions to minimize dust emissions.
(vii) Handheld and stand-mounted drills (including impact and rotary hammer drills)
Use drill equipped with commercially available shroud or cowling with dust collection system. Operate and maintain tool in accordance with manufacturer's instructions to minimize dust emissions. Dust collector must provide the air flow recommended by the tool manufacturer, or greater, and have a filter with 99% or greater efficiency and a filter-cleaning mechanism. Use a HEPA-filtered vacuum when cleaning holes
Advance to the next slide.

## Slide 55: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
(viii) Dowel drilling rigs for concrete | For tasks performed outdoors only: Use shroud around drill bit with a dust collection system. Dust collector must have a filter with 99% or greater efficiency and a filter-cleaning mechanism. Use a HEPA-filtered vacuum when cleaning holes | APF 10 | APF 10
(ix) Vehicle-mounted drilling rigs for rock and concrete | Use dust collection system with close capture hood or shroud around drill bit with a low-flow water spray to wet the dust at the discharge point from the dust collector. OR Operate from within an enclosed cab and use water for dust suppression on drill bit. | None | None
Notes: Instructor will go over details and use of Table 1:
Focus on the 1st column with the tools for this section.
(viii) Dowel drilling rigs for concrete
For tasks performed outdoors only: Use shroud around drill bit with a dust collection system. Dust collector must have a filter with 99% or greater efficiency and a filter-cleaning mechanism. Use a HEPA-filtered vacuum when cleaning holes
(ix) Vehicle-mounted drilling rigs for rock and concrete
Use dust collection system with close capture hood or shroud around drill bit with a low-flow water spray to wet the dust at the discharge point from the dust collector. OR Operate from within an enclosed cab and use water for dust suppression on drill bit.
Advance to the next slide.

## Slide 56: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
(x) Jackhammers and handheld powered chipping tools | Use tool with water delivery system that supplies a continuous stream or spray of water at the point of impact. − When used outdoors. − When used indoors or in an enclosed area; OR Use tool equipped with commercially available shroud and dust collection system. Operate and maintain tool in accordance with manufacturer's instructions to minimize dust emissions. Dust collector must provide the air flow recommended by the tool manufacturer, or greater, and have a filter with 99% or greater efficiency and a filter-cleaning mechanism. − When used outdoors. − When used indoors or in an enclosed area. | None APF 10 None APF 10 | APF 10 APF 10 APF 10 APF 10
Notes: Instructor will go over details and use of Table 1:
Focus on the 1st column with the tools for this section.
(x) Jackhammers and handheld powered chipping tools
Use tool with water delivery system that supplies a continuous stream or spray of water at the point of impact. − When used outdoors. − When used indoors or in an enclosed area. OR Use tool equipped with commercially available shroud and dust collection system. Operate and maintain tool in accordance with manufacturer's instructions to minimize dust emissions. Dust collector must provide the air flow recommended by the tool manufacturer, or greater, and have a filter with 99% or greater efficiency and a filter-cleaning mechanism. − When used outdoors. − When used indoors or in an enclosed area.
Advance to the next slide.

## Slide 57: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
(xi) Handheld grinders for mortar removal (i.e., tuckpointing) | Use grinder equipped with commercially available shroud and dust collection system. Operate and maintain tool in accordance with manufacturer's instructions to minimize dust emissions. Dust collector must provide 25 cubic feet per minute (cfm) or greater of airflow per inch of wheel diameter and have a filter with 99% or greater efficiency and a cyclonic pre-separator or filter-cleaning mechanism. | APF 10 | APF 25
(xii) Handheld grinders for uses other than mortar removal | For tasks performed outdoors only: Use grinder equipped with integrated water delivery system that continuously feeds water to the grinding surface. Operate and maintain tool in accordance with manufacturer’s instructions to minimize dust emissions. OR Use grinder equipped with commercially available shroud and dust collection system. Operate and maintain tool in accordance with manufacturer's instructions to minimize dust emissions. Dust collector must provide 25 cubic feet per minute (cfm) or greater of airflow per inch of wheel diameter and have a filter with 99% or greater efficiency and a cyclonic pre-separator or filter-cleaning mechanism. − When used outdoors. − When used indoors or in an enclosed area. | None | None
Notes: Instructor will go over details and use of Table 1:
Focus on the 1st column with the tools for this section.
(xi) Handheld grinders for mortar removal (i.e., tuckpointing)
Use grinder equipped with commercially available shroud and dust collection system. Operate and maintain tool in accordance with manufacturer's instructions to minimize dust emissions. Dust collector must provide 25 cubic feet per minute (cfm) or greater of airflow per inch of wheel diameter and have a filter with 99% or greater efficiency and a cyclonic pre-separator or filter-cleaning mechanism.
(xii) Handheld grinders for uses other than mortar removal
For tasks performed outdoors only: Use grinder equipped with integrated water delivery system that continuously feeds water to the grinding surface. Operate and maintain tool in accordance with manufacturer’s instructions to minimize dust emissions. OR Use grinder equipped with commercially available shroud and dust collection system. Operate and maintain tool in accordance with manufacturer's instructions to minimize dust emissions. Dust collector must provide 25 cubic feet per minute (cfm) or greater of airflow per inch of wheel diameter and have a filter with 99% or greater efficiency and a cyclonic pre-separator or filter-cleaning mechanism. − When used outdoors. − When used indoors or in an enclosed area.
Advance to the next slide.

## Slide 58: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
Notes: Instructor will go over details and use of Table 1:
Focus on the 1st column with the tools for this section.
(xiii) Walk-behind milling machines and floor grinders
Use machine equipped with integrated water delivery system that continuously feeds water to the cutting surface. Operate and maintain tool in accordance with manufacturer's instructions to minimize dust emissions. OR use machine equipped with dust collection system recommended by the manufacturer.
Operate and maintain tool in accordance with manufacturer's instructions to minimize dust emissions. Dust collector must provide the air flow
recommended by the manufacturer, or greater, and have a filter with 99% or greater efficiency and a filter-cleaning mechanism.
When used indoors or in an enclosed area, use a HEPA-filtered vacuum to remove loose dust in between passes.
Advance to the next slide.

## Slide 59: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
(xiv) Small drivable milling machines (less than half-lane) | Use a machine equipped with supplemental water sprays designed to suppress dust. Water must be combined with a surfactant. Operate and maintain machine to minimize dust emissions | None | None
(xv) Large drivable milling machines (half-lane and larger) | For cuts of any depth on asphalt only: Use machine equipped with exhaust ventilation on drum enclosure and supplemental water sprays designed to suppress dust. Operate and maintain machine to minimize dust emissions. For cuts of four inches in depth or less on any substrate: Use machine equipped with exhaust ventilation on drum enclosure and supplemental water sprays designed to suppress dust. Operate and maintain machine to minimize dust emissions. OR Use a machine equipped with supplemental water spray designed to suppress dust. Water must be combined with a surfactant. Operate and maintain machine to minimize dust emissions. | None | None
Notes: Instructor will go over details and use of Table 1:
Focus on the 1st column with the tools for this section.
(xiv) Small drivable milling machines (less than half-lane)
Use a machine equipped with supplemental water sprays designed to suppress dust. Water must be combined with a surfactant. Operate and maintain machine to minimize dust emissions
(xv) Large drivable milling machines (half-lane and larger)
For cuts of any depth on asphalt only: Use machine equipped with exhaust ventilation on drum enclosure and supplemental water sprays designed to suppress dust. Operate and maintain machine to minimize dust emissions. For cuts of four inches in depth or less on any substrate: Use machine equipped with exhaust ventilation on drum enclosure and supplemental water sprays designed to suppress dust. Operate and maintain machine to minimize dust emissions. OR Use a machine equipped with supplemental water spray designed to suppress dust. Water must be combined with a surfactant. Operate and maintain machine to minimize dust emissions.
(xv) Large drivable milling machines (half-lane and larger)
For cuts of any depth on asphalt only: Use machine equipped with exhaust ventilation on drum enclosure and supplemental water sprays designed to suppress dust. Operate and maintain machine to minimize dust emissions. For cuts of four inches in depth or less on any substrate: Use machine equipped with exhaust ventilation on drum enclosure and supplemental water sprays designed to suppress dust. Operate and maintain machine to minimize dust emissions. OR Use a machine equipped with supplemental water spray designed to suppress dust. Water must be combined with a surfactant. Operate and maintain machine to minimize dust emissions.
Advance to the next slide.

## Slide 60: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
*pictures obtained from www.lhsfna.org
Notes: Instructor will go over details and use of Table 1:
Focus on the 1st column with the tools for this section.
(xvi) Crushing machines
Use equipment designed to deliver water spray or mist for dust suppression at crusher and other points where dust is generated (e.g., hoppers, conveyers, sieves/sizing or vibrating components, and discharge points). Operate and maintain machine in accordance with manufacturer’s instructions to minimize dust emissions. Use a ventilated booth that provides fresh, climate-controlled air to the operator, or a remote control station.
Advance to the next slide.

## Slide 61: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
(xvii) Heavy equipment and utility vehicles used to abrade or fracture silica containing materials (e.g., hoe-ramming, rock ripping) or used during demolition activities involving silica-containing materials | Operate equipment from within an enclosed cab. When employees outside of the cab are engaged in the task, apply water and/or dust suppressants as necessary to minimize dust emissions. | None | None
(xviii) Heavy equipment and utility vehicles for tasks such as grading and excavating but not including: demolishing, abrading, or fracturing silica containing materials | Apply water and/or dust suppressants as necessary to minimize dust emissions. OR When the equipment operator is the only employee engaged in the task, operate equipment from within an enclosed cab. | None | None
Notes: Instructor will go over details and use of Table 1:
Focus on the 1st column with the tools for this section.
(xvii) Heavy equipment and utility vehicles used to abrade or fracture silica containing materials (e.g., hoe-ramming, rock ripping) or used during demolition activities involving silica-containing materials Operate equipment from within an enclosed cab. When employees outside of the cab are engaged in the task, apply water and/or dust suppressants as necessary to minimize dust emissions.
(xviii) Heavy equipment and utility vehicles for tasks such as grading and excavating but not including: demolishing, abrading, or fracturing silica containing materials
Apply water and/or dust suppressants as necessary to minimize dust emissions. OR When the equipment operator is the only employee engaged in the task, operate equipment from within an enclosed cab.
Advance to the next slide.

## Slide 62: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
All employers covered by the standard must:
Provide respiratory protection when required;
Restrict housekeeping practices that expose employees to respirable crystalline silica where feasible alternatives are available;
Establish and implement a written exposure control plan, including designating a competent person;
Offer medical exams to employees who will be required to wear a respirator under the standard for 30 or more days a year;
Communicate hazards and train employees; and
Keep records of medical examinations.
Notes: Instructor will go over what employers are covered under the standard must do:
Focus on the 1st column with the tools for this section.
All employers covered by the standard must:
Provide respiratory protection when required;
Restrict housekeeping practices that expose employees to respirable crystalline silica where feasible alternatives are available;
Establish and implement a written exposure control plan, including designating a competent person;
Offer medical exams to employees who will be required to wear a respirator under the standard for 30 or more days a year;
Communicate hazards and train employees; and
Keep records of medical examinations.
Advance to the next slide.

## Slide 63: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
All employers covered by the standard, including employers who fully and properly implement the specified exposure controls in Table 1, must develop and implement a written exposure control plan.
Written exposure control plans describe workplace exposures and ways to reduce those exposures, such as engineering controls, work practices, housekeeping methods, and restricting access to areas where high exposures occur.
Notes: Instructor will go over what employers are required to have in the written plan if thy are covered under the silica standard: Silica requires a written exposure control plan. This written exposure control plan describe workplace exposures and ways to reduce those exposures, such as engineering controls, work practices, housekeeping methods, and restricting access to areas where high exposures occur.
Advance to the next slide.

## Slide 64: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
The exposure control plan improves employee protections by making sure that employers identify all exposures and controls to prevent overexposures.
Exposure control plans are also useful for letting employees know what kind of protections they should expect to see on the job.
Notes: Instructor will go over what employers are required to have in the written plan:
The plans improve employee protections by making sure that employers identify all exposures and controls to prevent overexposures. Such plans are also important for letting employees know what kind of protections they should expect to see on the job.
Advance to the next slide.

## Slide 65: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
The written exposure control plan must include a description of workplace tasks involving exposures to respirable crystalline silica.
List all tasks that employees perform that could expose them to respirable crystalline silica dust.
Describe the equipment used and factors that affect exposures, such as types of silica-containing materials handled in those tasks (concrete or tile), weather conditions (wind or humidity), soil types (clay versus rock), and;
List if tasks are done outdoors versus indoors or in enclosed locations.
Notes: Instructor will go over what employers are required to have in the written plan:
The written exposure control plan must include a description of all workplace tasks involving exposures to respirable crystalline silica.
It must list all tasks that employees perform that could expose them to respirable crystalline silica dust, and describe the equipment used and factors that affect exposures, such as the types of silica-containing materials handled in those tasks (concrete or tile), weather conditions (wind or humidity), soil types (clay versus rock), and
List if tasks are done outdoors versus indoors or in other enclosed locations. In addition (Advance to the next slide.)

## Slide 66: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
The written exposure control plan must include a description of engineering controls, work practices, and respiratory protection used to limit employee exposure to respirable crystalline silica for each task.
Manufacturer’s recommended air flow
Filter with 99 percent efficiency,
Effective work practices, as in checking that water nozzles are not plugged, and if required,
Appropriate respiratory protection, like a respirator with an APF of 10.
Employers could also describe signs that controls are not working effectively
Notes: Instructor will go over what employers are required to have in the written plan:
In addition, the plan must include a description of engineering controls, work practices, and respiratory protection used to limit employee exposure to respirable crystalline silica for each task. Some of the examples would be:
Manufacturer’s recommended air flow
Filter with 99 percent efficiency,
Effective work practices, as in checking that water nozzles are not plugged, and if required,
Appropriate respiratory protection, like a respirator with an APF of 10.
Employers could also describe signs that controls are not working effectively
Advance to the next slide.

## Slide 67: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
This section of the written exposure control plan is especially important for construction employers who use controls in Table 1, because they are not required to measure exposures to make sure that controls are working.
including information such as manufacturer’s instructions for operating and maintaining tools to decrease dust, when possible, demonstrates that the employer has a complete understanding of those instructions and is using them to control dust.
Notes: Instructor will go over what employers are required to have in the written plan:
An important part of this section of the written exposure control plan is especially important for construction employers who use controls in Table 1, because they are not required to measure exposures to make sure that controls are working. It includes information such as manufacturer’s instructions for operating and maintaining tools to decrease dust, when possible, demonstrates that the employer has a complete understanding of those instructions and is using them to control dust.
Advance to the next slide.

## Slide 68: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
Example:
When cutting bricks using a stationary masonry saw (see slide 44) will be fully and properly implemented, including using a saw with an integrated water delivery system that delivers a steady stream of water to the cutting blade.
The saw operator will make sure that enough water for the saw is available before starting to cut, and that a steady stream of water can be seen while cutting. The operator will change water, when needed, to maintain flow of water to the blade.
Use the stationary masonry saw in accordance with manufacturer’s instructions to minimize the release of visible dust. Inspect dust controls daily to make sure they are functioning properly. Stop work and adjust controls if you see an increase in visible dust.
Notes: Instructor is to review the Example: (Read the slide) When cutting bricks using a stationary masonry saw, Table 1 will be fully and properly implemented, including using a saw with an integrated water delivery system that delivers a steady stream of water to the cutting blade. The saw operator will make sure that enough water for the saw is available before starting to cut, and that a steady stream of water can be seen while cutting. The operator will change water, when needed, to maintain flow of water to the blade. Use the stationary masonry saw in accordance with manufacturer’s instructions to minimize the release of visible dust. Inspect dust controls daily to make sure they are functioning properly. Stop work and adjust controls if you see an increase in visible dust.
Have the students discuss and decide if respiratory protection is required. Advance to show answer once they have an answer.
Answer: Respiratory protection is not required. The method used will provide adequate protection for the employee with a steady stream of water. As long as they have the required flow that the manufacture requires for the equipment. Regular changing of the water is required if it is a closed system.
Advance to the next slide.

## Slide 69: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
Example:
When cutting bricks using a stationary masonry saw (see slide 44) will be fully and properly implemented, including using a saw with an integrated water delivery system that delivers a steady stream of water to the cutting blade.
The saw operator will make sure that enough water for the saw is available before starting to cut, and that a steady stream of water can be seen while cutting. The operator will change water, when needed, to maintain flow of water to the blade.
Use the stationary masonry saw in accordance with manufacturer’s instructions to minimize the release of visible dust. Inspect dust controls daily to make sure they are functioning properly. Stop work and adjust controls if you see an increase in visible dust.
Respiratory protection is not required.
Notes: Instructor is to review the Example: (Read the slide) When cutting bricks using a stationary masonry saw, Table 1 will be fully and properly implemented, including using a saw with an integrated water delivery system that delivers a steady stream of water to the cutting blade. The saw operator will make sure that enough water for the saw is available before starting to cut, and that a steady stream of water can be seen while cutting. The operator will change water, when needed, to maintain flow of water to the blade. Use the stationary masonry saw in accordance with manufacturer’s instructions to minimize the release of visible dust. Inspect dust controls daily to make sure they are functioning properly. Stop work and adjust controls if you see an increase in visible dust.
Have the students discuss and decide if respiratory protection is required. Advance to show answer once they have an answer.
Answer: Respiratory protection is not required. The method used will provide adequate protection for the employee with a steady stream of water. As long as they have the required flow that the manufacture requires for the equipment. Regular changing of the water is required if it is a closed system.
Advance to the next slide.

## Slide 70: Module 2: OSHA ACT, Silica Standard, Table 1, and Overview
The plan must include a description of the housekeeping methods used to limit employee exposure to respirable crystalline silica.
While employees are cleaning, dust can become airborne and expose them to silica.
Notes: Instructor will continue to go over what employers are required to have in the written plan:
The written plan must include a description of the housekeeping methods used to limit employee exposure to respirable crystalline silica. While employees are cleaning, dust can become airborne and expose them to silica. We will be discussing this section in more detail at the end of the course.
Advance to the next slide.

## Slide 71: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
The plan must include a description of the procedures used to restrict access to work areas, when necessary, to limit the number of employees exposed to respirable crystalline silica and the levels to which they are exposed, including exposures generated by other employers or self-employed workers.
Notes: Instructor will go over what employers are required to have in the written plan:
The written plan must include a description of the procedures used to restrict access to work areas, when necessary, to limit the number of employees exposed to respirable crystalline silica and the levels to which they are exposed, including exposures generated by other employers or self-employed workers. It is important to keep others out of the area while work is going on that may expose them to the silica dust.
Advance to the next slide.

## Slide 72: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
The housekeeping section of the plan must describe how the employer restricts access to prevent exposures, such as:
Scheduling certain tasks when others are not around;
Telling employees to stay out of areas where dust is generated;
Moving employees to an area where they are not exposed to dust, or ;
Posting warning signs.
Notes: Instructor will go over how employers are required prevent access to areas with hazards of silica::
The housekeeping section of the plan must describe how the employer restricts access to prevent exposures, such as:
Scheduling certain tasks when others are not around,
Telling employees to stay out of areas where dust is generated,
Moving employees to an area where they are not exposed to dust, or
Posting warning signs.
Advance to the next slide.

## Slide 73: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
The employer or competent person must also restrict access, when needed, for exposures generated by another employer or self employed person.
Such a situation might occur if the other employer of self-employed person is conducting a task that generates clearly visible dust.
Notes: Instructor will go over how employers are required prevent access to areas with hazards of silica::
The employer or competent person must also restrict access, when needed, for exposures generated by another employer or self employed person.
Advance to the next slide.

## Slide 74: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
The respirable crystalline silica standard requires employers to review and evaluate the effectiveness of the written exposure control plan at least once a year and update it as necessary.
Notes: Instructor will go over when employers are required to review the written plan:
Each year the competent person must review the respirable crystalline silica written exposure control plan to ensure that it is effective and still within the standards to control silica exposure. With new technology and innovations, there maybe new tools or equipment that is more effective at reducing exposure.
Advance to the next slide.

## Slide 75: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
Employers must allow the written exposure control plan to be viewed or copied by each employee covered by the standard, their designated representative, and representatives from OSHA or NIOSH, upon request.
Notes: Instructor will go over who employers are required to have review the written plan:
Employees must be allow to be view or copy the written exposure control plan by the standard, or their designated representative, and representatives from OSHA or NIOSH, upon request.
Advance to the next slide.

## Slide 76: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
Competent Person Requirements:
The employer must designate a competent person to frequently and regularly inspect job sites, materials, and equipment to implement the written exposure control plan. A competent person is someone who:
Can identify existing and foreseeable respirable crystalline silica hazards;
Is authorized to promptly eliminate or minimize silica hazards; and
Has the knowledge and ability to implement the written exposure control plan.
Notes: Instructor will go over what role the competent person has based on the requirement: As we discussed earlier;
Competent Person Requirements:
The employer must designate a competent person to frequently and regularly inspect job sites, materials, and equipment to implement the written exposure control plan. A competent person is someone who:
Can identify existing and foreseeable respirable crystalline silica hazards;
Is authorized to promptly eliminate or minimize silica hazards; and
Has the knowledge and ability to implement the written exposure control plan.
Advance to the next slide.

## Slide 77: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
The standard does not require specific training for a competent person.
The employer is responsible for determining what training is necessary to provide the knowledge and ability for his or her competent person to implement the written exposure control plan.
Notes: Instructor will go over what employee training is required for the competent person:
The standard does not require specific training for a competent person. The employer is responsible for determining what training is necessary to provide the knowledge and ability for his or her competent person to implement the written exposure control plan.
Advance to the next slide.

## Slide 78: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
The standard specifies which employees must be offered medical surveillance, when and how often the examinations must offered, and the tests that make up medical examinations.
The standard also specifies the information that the employer must give to the physician or other licensed health care professional (PLHCP) who conducts the examinations and the information that the employer must ensure that the PLHCP provides to the employee and employer.
Notes: Instructor will go over what employers are required to have in place for medical surveillance and how often it will take place:
The standard specifies which employees must be offered medical surveillance, when and how often the examinations must offered, and the tests that make up medical examinations. These will be discussed in the medical section of this course. The standard also specifies the information that the employer must give to the physician or other licensed health care professional (PLHCP) who conducts the examinations and the information that the employer must ensure that the PLHCP provides to the employee and employer.
Advance to the next slide.

## Slide 79: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
Examples of Respiratory Protection Requirements for Employees who do more than one Table 1 Task
An employer anticipates that an employee will use a handheld grinder on a concrete wall outdoors for 3 hours and then use a chipping hammer outdoors for 2 hours (total Table 1 task duration of 5 hours per shift). The employer looks in the “< 4 hour/shift” column for each task to determine that no respiratory protection is required during use of the handheld grinder outdoors, but a respirator with an APF of 10 is required during use of the chipping hammer outdoors.
Notes: Instructor will go over examples:
Examples of Respiratory Protection Requirements for Employees who do more than one Table 1 Task
An employer anticipates that an employee will use a handheld grinder on a concrete wall outdoors for 3 hours and then use a chipping hammer outdoors for 2 hours (total Table 1 task duration of 5 hours per shift). The employer looks in the “> 4 hour/shift” column for each task to determine that no respiratory protection is required during use of the handheld grinder outdoors, but a respirator with an APF of 10 is required during use of the chipping hammer outdoors.
Students will discuss and form a opinion and share with the class: instructor will click and find that the answer is correct.
Advance to the next slide.

## Slide 80: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
Examples of Respiratory Protection Requirements for Employees who do more than one Table 1 Task
An employer anticipates that an employee will use a handheld grinder on a concrete wall outdoors for 3 hours and then use a chipping hammer outdoors for 2 hours (total Table 1 task duration of 5 hours per shift). The employer looks in the “< 4 hour/shift” column for each task to determine that no respiratory protection is required during use of the handheld grinder outdoors, but a respirator with an APF of 10 is required during use of the chipping hammer outdoors.
Yes, this is correct
Notes: Instructor will go over examples:
Examples of Respiratory Protection Requirements for Employees who do more than one Table 1 Task
An employer anticipates that an employee will use a handheld grinder on a concrete wall outdoors for 3 hours and then use a chipping hammer outdoors for 2 hours (total Table 1 task duration of 5 hours per shift). The employer looks in the “> 4 hour/shift” column for each task to determine that no respiratory protection is required during use of the handheld grinder outdoors, but a respirator with an APF of 10 is required during use of the chipping hammer outdoors.
Students will discuss and form a opinion and share with the class: instructor will click and find that the answer is correct.
Advance to the next slide.

## Slide 81: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
Examples of Respiratory Protection Requirements for Employees who do more than one Table 1 Task
An employer anticipates that an employee will use a stationary masonry saw to cut bricks for 1 hour and use a handheld power saw to cut concrete indoors for 1 hour over the course of a shift (total Table 1 task duration of two hours per shift). The employer looks in the “≤ 4 hour/shift” column for each task to determine that no respiratory protection is required during use of the stationary masonry saw, but a respirator with an APF of 10 is required during use of the handheld power saw indoors.
Notes: Instructor will go over examples:
Examples of Respiratory Protection Requirements for Employees who do more than one Table 1 Task
An employer anticipates that an employee will use a stationary masonry saw to cut bricks for 1 hour and use a handheld power saw to cut concrete indoors for 1 hour over the course of a shift (total Table 1 task duration of two hours per shift). The employer looks in the “≤ 4 hour/shift” column for each task to determine that no respiratory protection is required during use of the stationary masonry saw, but a respirator with an APF of 10 is required during use of the handheld power saw indoors.
Students will discuss and form an opinion if this is correct. It is correct
Advance to the next slide.

## Slide 82: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
Examples of Respiratory Protection Requirements for Employees who do more than one Table 1 Task
An employer anticipates that an employee will use a stationary masonry saw to cut bricks for 1 hour and use a handheld power saw to cut concrete indoors for 1 hour over the course of a shift (total Table 1 task duration of two hours per shift). The employer looks in the “≤ 4 hour/shift” column for each task to determine that no respiratory protection is required during use of the stationary masonry saw, but a respirator with an APF of 10 is required during use of the handheld power saw indoors.
Yes, this is correct
Notes: Instructor will go over examples:
Examples of Respiratory Protection Requirements for Employees who do more than one Table 1 Task
An employer anticipates that an employee will use a stationary masonry saw to cut bricks for 1 hour and use a handheld power saw to cut concrete indoors for 1 hour over the course of a shift (total Table 1 task duration of two hours per shift). The employer looks in the “≤ 4 hour/shift” column for each task to determine that no respiratory protection is required during use of the stationary masonry saw, but a respirator with an APF of 10 is required during use of the handheld power saw indoors.
Students will discuss and form an opinion if this is correct. It is correct
Advance to the next slide.

## Slide 83: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
Examples of Respiratory Protection Requirements for Employees who do more than one Table 1 Task
An employer anticipates that an employee will drive a half-lane milling machine for 4 hours and then operate a walk-behind milling machine equipped with an integrated water delivery system for 4 hours (total Table 1 task duration of 8 hours). The employer looks in the “> 4 hour/shift” column for each task to determine that no respiratory protection is required for either task.
Notes: Instructor will go over examples:
Examples of Respiratory Protection Requirements for Employees who do more than one Table 1 Task
An employer anticipates that an employee will drive a half-lane milling machine for 4 hours and then operate a walk-behind milling machine equipped with an integrated water delivery system for 4 hours (total Table 1 task duration of 8 hours). The employer looks in the “> 4 hour/shift” column for each task to determine that no respiratory protection is required for either task.
Students will review the information and discuss if this is true or false: It is true.
Advance to the next slide.

## Slide 84: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
Examples of Respiratory Protection Requirements for Employees who do more than one Table 1 Task
An employer anticipates that an employee will drive a half-lane milling machine for 4 hours and then operate a walk-behind milling machine equipped with an integrated water delivery system for 4 hours (total Table 1 task duration of 8 hours). The employer looks in the “> 4 hour/shift” column for each task to determine that no respiratory protection is required for either task.
Yes, this is correct
Notes: Instructor will go over examples:
Examples of Respiratory Protection Requirements for Employees who do more than one Table 1 Task
An employer anticipates that an employee will drive a half-lane milling machine for 4 hours and then operate a walk-behind milling machine equipped with an integrated water delivery system for 4 hours (total Table 1 task duration of 8 hours). The employer looks in the “> 4 hour/shift” column for each task to determine that no respiratory protection is required for either task.
Students will review the information and discuss if this is true or false: It is true.
Advance to the next slide.

## Slide 85: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
Summary:
  Describe the purpose of the Susan Harwood Training Grant Program
  List basic Workers Rights and Employer Responsibilities under the OSH Act
  What gives the employees the right to voice safety and health concerns free from retaliation?
  Describe How to file a complaint
Notes: The instructor will review the key points in the Summary students will be able to respond to each one;
  Describe the purpose of the Susan Harwood Training Grant Program
  List basic Workers Rights and Employer Responsibilities under the OSH Act
  What gives the employees the right to voice safety and health concerns free from retaliation?
  Describe how to file a complaint
Advance to the next slide.

## Slide 86: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
  Summary:
  What is Respirable Crystalline Silica?
  How is Table 1 used?
Notes:   The instructor will review the key points in the Summary students will be able to respond to each one;
  What is respirable crystalline silica?
  how is table 1 used?
Advance to the next slide.

## Slide 87: Module 2: OSH ACT, Silica Standard, Table 1, and Overview
  Any Questions?
Notes: Answer student questions, if any.
Students are to take the first break and the instructor shall switch to Tab 3.

## Slide 88: USF OTI Education Center Respirable Silica in the Construction Industry
Module 3
Notes: Advance to the next slide.

## Slide 89: Module 3
This material was produced under grant number SH-29661-SH6 from OSHA. It does not necessarily reflect the views or policies of the U.S. Department of Labor, nor does mention of trade names, commercial products, or organizations imply endorsement by the U.S. Government.
Silica Health Hazard Information and Medical Surveillance

## Slide 90: Module 3: Silica Health Hazard Information and Medical Surveillance:
Terminal Objectives:
  Trainees will be able to describe the requirements of the new silica standard for construction.
Notes: Instructor to review the Objectives with the students.
Terminal Objectives:
  Trainees will be able to discuss health hazards of respirable silica
  Trainees will be able to identify general silica dust hazards and controls in the workplace
Advance to the next slide.

## Slide 91: Module 3: Silica Health Hazard Information and Medical Surveillance:
Enabling objectives:
  Identify the major differences between the old and new silica standard;
  Identify the areas of the new standard that trainees should be concerned with.
Notes: Instructor to review the Objectives with the students.
Enabling objectives:
  Identify basic health risks, both short and long-term, associated with silica exposure
  Identify basic activities likely to expose workers to silica exposure
  Identify general differences between engineering and administrative controls and PPE
Advance to the next slide.

## Slide 92: Module 3: Silica Health Hazard Information and Medical Surveillance:
The Occupational Safety and Health Administration (OSHA) has issued a final rule to curb lung cancer, silicosis, chronic obstructive pulmonary disease and kidney disease in America's workers by limiting their exposure to respirable crystalline silica.
The rule is comprised of two standards, one for Construction and one for General Industry and Maritime.
Notes: Instructor to review the final rule on silica.
The Occupational Safety and Health Administration (OSHA) has issued a final rule to curb lung cancer, silicosis, chronic obstructive pulmonary disease and kidney disease in America's workers by limiting their exposure to respirable crystalline silica. The rule is comprised of two standards, one for Construction and one for General Industry and Maritime.
Advance to the next slide.

## Slide 93: Module 3: Silica Health Hazard Information and Medical Surveillance:
OSHA estimates that the rule will save over 600 lives and prevent more than 900 new cases of silicosis each year, once its effects are fully realized.
The Final Rule is projected to provide net benefits of about $7.7 billion, annually.
Notes: Instructor shall discuss how updating the rule will save lives and save money:
OSHA estimates that the rule will save over 600 lives and prevent more than 900 new cases of silicosis each year, once its effects are fully realized. The Final Rule is projected to provide net benefits of about $7.7 billion, annually.
Advance to the next slide.

## Slide 94: Module 3: Silica Health Hazard Information and Medical Surveillance:
About 2.3 million workers are exposed to respirable crystalline silica in their workplaces, including 2 million construction workers who drill, cut, crush, or grind silica-containing materials such as concrete and stone, and 300,000 workers in general industry operations such as brick manufacturing, foundries, and hydraulic fracturing, also known as fracking.
Notes: Instructor shall discuss how updating the rule will reduce exposures in the workplace.
About 2.3 million workers are exposed to respirable crystalline silica in their workplaces, including 2 million construction workers who drill, cut, crush, or grind silica-containing materials such as concrete and stone, and 300,000 workers in general industry operations such as brick manufacturing, foundries, and hydraulic fracturing, also known as fracking.
Advance to the next slide.

## Slide 95: Module 3: Silica Health Hazard Information and Medical Surveillance:
The U.S. Department of Labor first highlighted the hazards of respirable crystalline silica in the 1930s, after a wave of worker deaths. The department set standards to limit worker exposure in 1971, when OSHA was created. However, the standards are outdated and do not adequately protect workers from silica-related diseases.
Furthermore, workers are being exposed to silica in new industries such as stone or artificial stone countertop fabrication and hydraulic fracturing.
Notes: Instructor shall discuss when silica became highlighted.
The U.S. Department of Labor first highlighted the hazards of respirable crystalline silica in the 1930s, after a wave of worker deaths. The department set standards to limit worker exposure in 1971, when OSHA was created. However, the standards are outdated and do not adequately protect workers from silica-related diseases. Furthermore, workers are being exposed to silica in new industries such as stone or artificial stone countertop fabrication and hydraulic fracturing.
Advance to the next slide.

## Slide 96: Module 3: Silica Health Hazard Information and Medical Surveillance:
Please cut and paste link in to your browser to watch video https://youtu.be/oMduqVTFkBQ?t=145
Notes: Instructor will play the video:
This video is from the department of labor. Emphasizes the fact that silica is not a new hazard it was recognized in 1938 as a health hazard in mining and rock industries. OSHA has had a silica hazard PEL from the beginning, but it has been determined that it was not enough. Changes have been made to protect workers based on technology changes and more data of the harmful effects.
Advance to the next slide.

## Slide 97: Module 3: Silica Health Hazard Information and Medical Surveillance:
What is Silicosis?
  Lung fibrosis caused by the inhalation of dust containing silica.
Notes: Instructor will discuss how silica affects the lung:
What is Silicosis?
Lung fibrosis caused by the inhalation of dust containing silica. This is a hardening of the tissue in the lung due to scar tissue.
Advance to the next slide.

## Slide 98: Module 3: Silica Health Hazard Information and Medical Surveillance:
Silica is a hard-abrasive material found in most rocks and non-metal ores.
Sand and soil comes from the weathering of rock, therefore there is some silica in most sands and soils. The amount depends on the material that it originally came from.
Respirable Crystalline Silica comes from breaking the silica particles down to smaller parts through mechanical force.
Notes: Instructor shall discuss where silica is found:
Silica is a hard-abrasive material found in most rocks and non-metal ores.
Sand and soil comes from the weathering of rock, therefore there is some silica in most sands and soils. The amount depends on the material that it originally came from.
Respirable Crysalline Silica comes from breaking the silica particles down to smaller parts through mechanical force.
Advance to the next slide.

## Slide 99: Module 3: Silica Health Hazard Information and Medical Surveillance:
It is important to know how much silica is in the material that you are working with.
SDS’s will list the amount of silica in a percentage on those products that contain at least 1% silica.
Notes: Instructor will go over how to locate the information on how much silica is in a substance.
It is important to know how much silica is in the material that you are working with.
SDS’s will list the amount of silica in a percentage on those products that contain at least 1% silica. Employees should review the SDS for all products prior to working with them to understand the hazards. OSHA 29 CFR 1910.1200 gives them the right to know about all hazardous chemicals in the workplace.
Advance to the next slide.

## Slide 100: Module 3: Silica Health Hazard Information and Medical Surveillance:
Notes: Instructor to review the example SDS with students. Focus on the silica content.
Example SDS with Silica containing material
Advance to the next slide.

## Slide 101: Module 3: Silica Health Hazard Information and Medical Surveillance:
There are three types of silica:
Quartz
Cristobalite
Tridymite
Quartz – is the most abundant, found in most rock and nonmetal ores;
Cristobalite and Tridymite are more toxic but less abundant.
Notes: Instructor to discuss how there are three types of silica.
There are three types of silica
Quartz,
Cristobalite,
and Tridymite
Quartz – is the most abundant, found in most rock and nonmetal ores
Cristobalite and Tridymite are more toxic but less abundant
Advance to the next slide.

## Slide 102: Module 3: Silica Health Hazard Information and Medical Surveillance:
The Human respiratory system allows us to exchange air.
Air enters the body through the nose and down the trachea and then enters the Bronchial tubes and the Bronchioles and ends up in the Alveoli.
This is where the oxygen enters the blood stream and CO2 leaves our bodies.
Anything that can significantly change our body’s ability to exchange air can cause health problems.
Notes: Instructor shall discuss how air gets into the body through the respiratory system.
The Human respiratory system allows us to exchange air.
Air enters the body through the nose and down the trachea and then enters the Bronchial tubes and the Bronchioles and ends up in the Alveoli.
This is where the oxygen enters the blood stream and CO2 leaves our bodies.
Anything that can significantly change our body’s ability to exchange air can cause health problems.
Advance to the next slide.

## Slide 103: Module 3: Silica Health Hazard Information and Medical Surveillance:
Nose
Trachea
Bronchial tubes
Bronchioles
Alveoli
Notes: Instructor goes over the Diagram of the human respiratory system. Point out the main areas:
Nose – This is the point of entry for the silica dust. There are hairs and mucus to remove large particles and some of the dust will be captured within this area.
Trachea – the air way that has some protection for larger particles with mucus and the mucociliary escalator with cilia.
Bronchial tubes – Here the respiratory system begins to reduce and some particles will be captured.
Bronchioles – Smaller branches of the airway and lead to the Aveoli
Aveoli – This is the main area of concern if silica makes it to the Alveolar sacs, the dust will have the greatest affect and cause breathing issues.
Advance to the next slide.

## Slide 104: Module 3: Silica Health Hazard Information and Medical Surveillance:
The respiratory system generally cleans itself. The hairs and mucus in our nose capture larger particles and then we blow those out. In the airway the mucociliary escalator it works like a conveyor and traps the particles and pushes them back up the airway. If the silica particles are very small they can get past our normal defense and into the lungs.
Notes: Instructor shall discuss how the respiratory system is able to remove large particles.
The respiratory system generally cleans itself. The hairs and mucus in our nose capture larger particles and then we blow those out. In the airway the mucociliary escalator it works like a conveyor and traps the particles and pushes them back up the airway. If the silica particles are very small they can get past our normal defense and into the lungs.
Advance to the next slide.

## Slide 105: Module 3: Silica Health Hazard Information and Medical Surveillance:
If the silica gets into the lungs then we have a secondary defense called Macrophage cells. These Macrophage cells operate like a pac-man game eating up particles and getting rid of them up the mucociliary escalator or through the lymphatic drainage system.
If there are too many of the particles the macrophage cells get over loaded and cannot remove the particles from the lungs. If too much silica particles are inhaled over a long period of time it overwhelms the lungs defense mechanism.
Notes: Instructor is to discuss how silica gets into the lungs and can start a process that will have damaging effects:
If the silica gets into the lungs then we have a secondary defense called Macrophage cells. These Macrophage cells operate like a pac-man game eating up particles and getting rid of them up the mucociliary escalator or through the lymphatic drainage system. If there are too many of the particles the macrophage cells get over loaded and cannot remove the particles from the lungs. If too much silica particles are inhaled over a long period of time it over whelms the lungs defense mechanism.
Advance to the next slide.

## Slide 106: Module 3: Silica Health Hazard Information and Medical Surveillance:
Macrophage cells
Notes: Instructor shall discuss how Macrophage cells look as they surround silica dust in the lungs:
Macrophage cells surrounding silica dust on the lung tissue. The large Macrophage cells (stained blue) are actively looking for the intruding silica (stained pink) and other dust in the lungs. Where they surround the damaging particles.
Advance to the next slide.

## Slide 107: Module 3: Silica Health Hazard Information and Medical Surveillance:
This starts an inflammatory process in the lungs, as the macrophage cells get over loaded they rupture and release cellular fluid that causes inflammation.
This triggers other special cells called fiber blast to come to the area to surround the particles and protect the lung.
This creates scar tissue similar to what happens after you cut your finger.
Notes: Instructor shall discuss how the lung tissue reacts to the attack:
This starts an inflammatory process in the lungs, as the macrophage cells get over loaded they rupture and release cellular fluid that causes inflammation.
This triggers other special cells called fiber-blast to come to the area to surround the particles and protect the lung.
This creates scar tissue. Which is similar to what happens after you cut your finger.
Advance to the next slide.

## Slide 108: Module 3: Silica Health Hazard Information and Medical Surveillance:
Notes: Instructor will compare the scar tissue forming on this finger to the scar tissue in the lung:
scar tissue forming on a cut finger forms to protect the wound and hardens.
Advance to the next slide.

## Slide 109: Module 3: Silica Health Hazard Information and Medical Surveillance:
As scaring happens in the lung the process continues to progress. It can reduce the lungs ability to expand and contract as well as reducing the lungs ability to exchange oxygen.
One can develop complicated silicosis which maybe causes long term health issues and possibly death.
The amount of exposure to silica dust affect the chance for disease process. Along with other factors like smoking that has already caused damage to the lungs.
Notes: Instructor shall discuss how the scar tissue can continue and cause complications in breathing.
When this scaring occurs in the lung(s) it will continue to progress. It can reduce the lungs ability to expand and contract as well as reducing the lungs ability to exchange oxygen. If too much healthy tissue is replaced by scar tissue you may develop complicated silicosis, which could cause long term health issues and possibly death. The amount of exposure to silica dust affects your chance for disease process. Along with other factors like smoking that has already caused damage to your lungs and made them more sensitive to exposure.
Advance to the next slide.

## Slide 110: Module 3: Silica Health Hazard Information and Medical Surveillance:
The amount and duration of the exposure characterizes how fast the lungs get overloaded.
Acute Silicosis can develop within a few weeks to five years of the exposure to exceptionally high levels of silica dust.
This often results in death due to the rapid overloading of the lungs.
Notes: Instructor shall discuss how the lung can get overloaded:
The amount and duration of the exposure characterizes how fast the lungs get overloaded.
Acute Silicosis can develop within a few weeks to 5 years of the exposure to exceptionally high levels of silica dust. This often results in death due to the rapid overloading of the lungs.
Advance to the next slide.

## Slide 111: Module 3: Silica Health Hazard Information and Medical Surveillance:
People with Acute silicosis experience:
Cough
Weight loss
Tiredness
May have fever*
Sharp chest pain
Notes: Instructor shall discuss acute silicosis symptoms:
People with Acute silicosis experience:
cough,
weight loss,
tiredness,
may have fever, or
sharp chest pain.
Advance to the next slide.

## Slide 112: Module 3: Silica Health Hazard Information and Medical Surveillance:
They may have shortness of breath over time, especially with chronic silicosis.
A healthcare provider might hear crackles or wheezing when they listen to the lungs.
Having silicosis increases the risk of other problems, such as:
  tuberculosis;
  lung cancer, and;
  chronic bronchitis.
Notes: Instructor shall discuss acute silicosis symptoms:
People with Acute silicosis may also have shortness of breath over time, especially with chronic silicosis. A healthcare provider might hear crackles or wheezing when they listen to your lungs.
Having silicosis increases the risk of other problems, such as tuberculosis, lung cancer, and chronic bronchitis.
Advance to the next slide.

## Slide 113: Module 3: Silica Health Hazard Information and Medical Surveillance:
Accelerated silicosis comes from high concentrations of respirable silica for a period of 5-10 years.
It is disabling and often results in death. It progress even after the exposure has been removed.
In accelerated silicosis, swelling in the lungs and symptoms occur faster than in chronic silicosis.
Notes: Instructor shall discuss accelerated silicosis causes and symptoms:
Accelerated silicosis comes from high concentrations of respirable silica for a period of 5-10 years. Accelerated silicosis is disabling and often results in death. It progress even after the exposure has been removed.
In accelerated silicosis, swelling in the lungs and symptoms occur faster than in chronic silicosis.
Advance to the next slide.

## Slide 114: Module 3: Silica Health Hazard Information and Medical Surveillance:
Chronic silicosis is the most common and is formed as a result of exposure to low concentrations of silica over a long period, ten or more years.
In chronic silicosis, the silica dust causes areas of swelling in the lungs and chest lymph nodes, which makes breathing more difficult.
Notes: Instructor shall discuss chronic silicosis exposure and symptoms:
Chronic silicosis is the most common and is formed as a result of exposure to low concentrations of silica over a long period, ten or more years.
In chronic silicosis, the silica dust causes areas of swelling in the lungs and chest lymph nodes, which makes breathing more difficult.
Advance to the next slide.

## Slide 115: Module 3: Silica Health Hazard Information and Medical Surveillance:
Chronic silicosis progresses very slowly and goes undetected for many years before it can be diagnosed. It will cause health issues and may result in death.
Notes: Instructor shall discuss chronic silicosis exposure:
Chronic silicosis progresses very slowly and can go undetected for many years before it can be diagnosed. Chronic silicosis will cause health issues and may result in death.
Advance to the next slide.

## Slide 116: Module 3: Silica Health Hazard Information and Medical Surveillance:
The Common Symptoms of all types of silicosis are shortness of breath, fatigue, and difficult performing task.
The severity and how soon they occur differ among the different three types of silicosis.
Chest x-rays are the best means of detecting early stages of silicosis.
Notes: Instructor shall discuss common silicosis symptoms:
The Common Symptoms of all types of silicosis are shortness of breath, fatigue, and difficult performing task.
The severity and how soon they occur differ among the different three types of silicosis. Chest x-rays are the best means of detecting early stages of silicosis.
Advance to the next slide.

## Slide 117: Module 3: Silica Health Hazard Information and Medical Surveillance:
The purpose of the x-ray is to detect early scaring in the lungs.
If detected early, employers can act to protect you against additional exposures. This can reduce the progression of the disease.
Chest x-rays should be taken close as possible to starting work with a company and every three years after that to monitor for changes in the lungs.
Notes: Instructor shall discuss testing for silicosis exposure:
The purpose of the x-ray is to detect early scaring in the lungs. If detected early, employers can act to protect you against additional exposures. This can reduce the progression of the disease.
Chest x-rays should be taken close as possible to starting work with a company and every 3 years after that to monitor for changes in the lungs.
Advance to the next slide.

## Slide 118: Module 3: Silica Health Hazard Information and Medical Surveillance:
Normal Lung
Abnormal Lung
Notes: Instructor shall discuss testing for silicosis exposure and the x-rays taken for determining exposure and level of progression:
The normal lung on the left with clear lungs shown by the even darker color that represents air in the lungs. The abnormal lung shows extreme abounds of scar tissue in the central part of both lungs, represented by the lighter areas of the lungs that show a solid tissue rather than the pockets of air.
Advance to the next slide.

## Slide 119: Module 3: Silica Health Hazard Information and Medical Surveillance:
Notes: Instructor shall discuss testing for silicosis exposure and the x-rays taken for determining exposure and level of progression:
There are small areas of scar tissue in the upper part of both lungs, shown by the lighter sections within the lungs.
Advance to the next slide.

## Slide 120: Module 3: Silica Health Hazard Information and Medical Surveillance:
Notes: Instructor shall discuss testing for silicosis exposure and the x-rays taken for determining exposure and level of progression:
This x-ray shows both masses and infusion of the lower section of both lungs.
Advance to the next slide.

## Slide 121: Module 3: Silica Health Hazard Information and Medical Surveillance:
Notes: Instructor shall discuss testing for silicosis exposure and the x-rays taken for determining exposure and level of progression:
This x-ray shows a large number of nodules throughout the lung with calcification indicating that this is a long term exposure with damage over many years.
Advance to the next slide.

## Slide 122: Module 3: Silica Health Hazard Information and Medical Surveillance:
There is no cure for silicosis so early detection is important.
Some people may need urgent treatment with oxygen and support for breathing.
Others may need medicines to decrease sputum production, such as inhaled steroids.
Some may need inhaled bronchodilators, which relax the air tubes.
Notes: Instructor shall discuss medical limitation in treatment and point out that there is no cure:
There is no cure for silicosis so early detection is important.
Some people may need urgent treatment with oxygen and support for breathing. Others may need medicines to decrease sputum production, such as inhaled steroids.
Some may need inhaled bronchodilators, which relax the air tubes.
Advance to the next slide.

## Slide 123: Module 3: Silica Health Hazard Information and Medical Surveillance:
Protection methods:
Substitution;
Engineering controls;
Ventilation;
Good housekeeping;
Good work practices;
Avoid areas that are dusty, and;
Wear respiratory protection if the dust cannot be otherwise controlled.
Notes: Instructor shall discuss protection methods:
Protection methods:
Substitution,
engineering controls,
ventilation,
good housekeeping,
good work practices,
avoid areas that are dusty, and
wear respiratory protection if the dust cannot be otherwise controlled.
Advance to the next slide.

## Slide 124: Module 3: Silica Health Hazard Information and Medical Surveillance:
Prevention is a combination of all the methods of protection such as:
Training;
Using SDS information;
Wet working;
Vacuum capture systems;
Monitoring;
Using a good medical surveillance program;
Physical examinations and;
X-rays/ pulmonary function test.
Notes: Instructor shall discuss protection methods:
Prevention is a combination of all the methods of protection such as:
Training,
using SDS information,
wet working,
vacuum capture systems,
monitoring,
using a good medical surveillance program,
physical examinations,
and x-rays/ pulmonary function test.
Advance to the next slide.

## Slide 125: Module 3: Silica Health Hazard Information and Medical Surveillance:
Silicosis is a preventable disease by reducing exposure.
We all play an important role in preventing silicosis.
Notes: Instructor shall discuss prevention:
Silicosis is a preventable disease by reducing exposure.
We all play an important role in preventing silicosis.
Advance to the next slide.

## Slide 126: Module 3: Silica Health Hazard Information and Medical Surveillance:
Grinding
Cutting
Breaking
Crushing
Sweeping
Blowing
On materials that contain silica or silica dust.
What activities are most likely to cause exposure to silica?
Notes: Instructor shall discuss activities that are likely to cause silica dust exposure:
What activities are most likely to cause exposure to silica?
Grinding
Cutting
Breaking
Crushing
Sweeping
Blowing
On materials that contain silica or silica dust.
Advance to the next slide.

## Slide 127: Module 3: Silica Health Hazard Information and Medical Surveillance:
Medical surveillance is intended to identify respirable crystalline silica-related diseases so that employees with those diseases can take actions to protect their health; to determine if an employee has any condition, such as a lung disease, that might make him or her more sensitive to respirable crystalline silica exposure; and to determine the employee’s fitness to use respirators.
Notes: Instructor shall discuss medical surveillance program:
Medical surveillance is intended to identify respirable crystalline silica-related diseases so that employees with those diseases can take actions to protect their health; to determine if an employee has any condition, such as a lung disease, that might make him or her more sensitive to respirable crystalline silica exposure; and to determine the employee’s fitness to use respirators.
Advance to the next slide.

## Slide 128: Module 3: Silica Health Hazard Information and Medical Surveillance:
Employer(s) must offer medical examinations:
Within 30 days of initial assignment, unless the employee has had an examination that meets the requirements of the silica standard within the last three years.
Every three years from the employee’s last examination that met the requirements of the silica standard, or more frequently if recommended by the PLHCP, if the employee will continue to perform tasks that require respirator use under the silica standard for 30 or more days per year.
Notes: Instructor shall discuss medical surveillance program:
Employers must offer medical examinations:
Within 30 days of initial assignment, unless the employee has had an examination that meets the requirements of the silica standard within the last three years.
Every three years from the employee’s last examination that met the requirements of the silica standard, or more frequently if recommended by the PLHCP, if the employee will continue to perform tasks that require respirator use under the silica standard for 30 or more days per year.
Advance to the next slide.

## Slide 129: Module 3: Silica Health Hazard Information and Medical Surveillance:
A PLHCP might recommend more frequent medical examinations based on factors such as high exposure levels or a medical finding such as an X-ray suggesting silicosis.
Notes: Instructor shall discuss medical surveillance program:
A PLHCP might recommend more frequent medical examinations based on factors such as high exposure levels or a medical finding such as an X-ray suggesting silicosis.
Advance to the next slide.

## Slide 130: Module 3: Silica Health Hazard Information and Medical Surveillance:
Employers must make sure that employees receive a dated copy of the PLHCP’s written medical opinion for the employer, and the employee can present that opinion to a new employer as proof of a current medical examination.
Notes: Instructor shall discuss medical surveillance program:
Employers must make sure that employees receive a dated copy of the PLHCP’s written medical opinion for the employer, and the employee can present that opinion to a new employer as proof of a current medical examination.
Advance to the next slide.

## Slide 131: Module 3: Silica Health Hazard Information and Medical Surveillance:
Medical Evaluation Requirements under the Respiratory Protection Standard. Employees who are required to wear respirators must receive medical evaluations required by the respiratory protection standard before they are fit tested for a respirator or wear a respirator in the workplace.
Notes: Instructor shall discuss medical surveillance program:
Medical Evaluation Requirements under the Respiratory Protection Standard:
Employees who are required to wear respirators must receive medical evaluations required by the respiratory protection standard before they are fit tested for a respirator or wear a respirator in the workplace.
Advance to the next slide.

## Slide 132: Module 3: Silica Health Hazard Information and Medical Surveillance:
The medical evaluation for the respiratory protection standard can be combined with the medical examination for silica, and employers could have the PLHCP conduct both the evaluation for respirator use and examination for silica at the same time.
They could also have employees evaluated for respirator use before they wear a respirator and then offer the silica examination later, according to the required time limits of the silica standard.
Notes: Instructor shall discuss medical surveillance program:
The medical evaluation for the respiratory protection standard can be combined with the medical examination for silica, and employers could have the PLHCP conduct both the evaluation for respirator use and examination for silica at the same time.
They could also have employees evaluated for respirator use before they wear a respirator and then offer the silica examination later, according to the required time limits of the silica standard.
Advance to the next slide.

## Slide 133: Module 3: Silica Health Hazard Information and Medical Surveillance:
An initial medical examination provided under the silica standard consists of:
A medical and work history
A physical examination that focuses on the respiratory system;
A digital or film chest X-ray;
A lung function (spirometry) testing for latent tuberculosis infection, and;
Any other tests deemed appropriate by the PLHCP.
Notes: Instructor shall discuss medical surveillance program:
An initial medical examination provided under the silica standard consists of:
A medical and work history that focuses on: past, present, and anticipated exposure to respirable crystalline silica, dust, and other agents affecting the respiratory system; any history of respiratory system dysfunction, including signs and symptoms of respiratory disease (for example, shortness of breath, cough, wheezing); history of tuberculosis; and smoking status and history;
A physical examination that focuses on the respiratory system;
A digital or film chest X-ray interpreted according to the International Labor Office (ILO) International Classification of Radiographs of Pneumoconioses by a National Institute for Occupational Safety and Health (NIOSH)-certified B Reader (this involves a certified physician reading the X-ray according to certain procedures to determine if it shows signs of diseases such as silicosis);
A lung function (spirometry) test that includes forced vital capacity (the total amount of air that is forcefully blown out after taking a full breath), forced expiratory volume in one second (the amount of air forcefully blown out in the first second), and FEV1/FVC ratio (the speed of air that is forcefully blown out), administered by a spirometry technician with a current certificate from a NIOSH approved spirometry course;
Testing for latent tuberculosis infection;
Any other tests deemed appropriate (medically necessary and related to respirable crystalline silica exposure) by the PLHCP.
Advance to the next slide.

## Slide 134: Module 3: Silica Health Hazard Information and Medical Surveillance:
The employer must get a written medical opinion from the PLHCP within 30 days of the medical examination. The written opinion must contain only the following information:
The date of the examination;
A statement that the examination has met the requirements of the silica standard; and
Any recommended limitations on the employee’s use of respirators.
Notes: Instructor shall discuss medical surveillance program:
If the employee gives written authorization, the written medical opinion to the employer must also contain one or both of the following: ■ Any recommended limitations on the employee’s exposure to respirable crystalline silica; ■ A statement that the employee should be examined by a specialist if the B reader classifies the chest X-ray provided under the silica standard as 1/0 or higher (X-ray evidence of silicosis in employees exposed to respirable crystalline silica), or if the PLHCP otherwise recommends referral to a specialist.
Advance to the next slide.

## Slide 135: Module 3: Silica Health Hazard Information and Medical Surveillance:
Employers must make sure that each employee receives a copy of the written medical opinion within 30 days of each medical examination.
Notes: Instructor shall discuss medical surveillance program:
Employers must make sure that each employee receives a copy of the written medical opinion within 30 days of each medical examination.
Advance to the next slide.

## Slide 136: Module 3: Silica Health Hazard Information and Medical Surveillance:
Training
Employers must train and inform employees covered by the silica standard about respirable crystalline silica hazards and the methods the employer uses to limit their exposures to those hazards.
Employers must cover the cost of training and must pay employees for the time spent in training.
Notes: Instructor shall discuss training program requirements:
Training
Employers must train and inform employees covered by the silica standard about respirable crystalline silica hazards and the methods the employer uses to limit their exposures to those hazards. Employers must cover the cost of training and must pay employees for the time spent in training.
Advance to the next slide.

## Slide 137: Module 3: Silica Health Hazard Information and Medical Surveillance:
Employees must be trained at the time they are assigned to a position involving exposure to respirable crystalline silica.
Additional training must be provided as often as necessary to ensure that employees know and understand respirable crystalline silica hazards and the protections available in their workplace.
Notes: Instructor shall discuss training program requirements:
Employees must be trained at the time they are assigned to a position involving exposure to respirable crystalline silica.
Additional training must be provided as often as necessary to ensure that employees know and understand respirable crystalline silica hazards and the protections available in their workplace.
Advance to the next slide.

## Slide 138: Module 3: Silica Health Hazard Information and Medical Surveillance:
Employers must make a copy of the respirable crystalline silica standard available at no cost to each employee covered by the standard.
Notes: Instructor shall discuss program requirements:
Employers must make a copy of the respirable crystalline silica standard available at no cost to each employee covered by the standard.
Advance to the next slide.

## Slide 139: Module 3: Silica Health Hazard Information and Medical Surveillance:
Recordkeeping
Employers are required to make and keep accurate records of air monitoring data and objective data used to assess employee exposures to respirable crystalline silica under the standard, as well as records of medical surveillance provided under the standard.
Notes: Instructor shall discuss recordkeeping program requirements:
Recordkeeping
Employers are required to make and keep accurate records of air monitoring data and objective data used to assess employee exposures to respirable crystalline silica under the standard, as well as records of medical surveillance provided under the standard.
Advance to the next slide.

## Slide 140: Module 3: Silica Health Hazard Information and Medical Surveillance:
Recordkeeping
Employers are required to make and keep accurate records of air monitoring data and objective data used to assess employee exposures to respirable crystalline silica under the standard, as well as records of medical surveillance provided under the standard.
Notes: Instructor shall discuss recordkeeping program requirements:
Recordkeeping
Employers are required to make and keep accurate records of air monitoring data and objective data used to assess employee exposures to respirable crystalline silica under the standard, as well as records of medical surveillance provided under the standard.
Advance to the next slide.

## Slide 141: Module 3: Silica Health Hazard Information and Medical Surveillance:
Example of silica dust exposure
Notes: Instructor will go over the example picture and note the exposure from the dust. Also asking what methods can be used to control this dust?
Example of cutting cement without the proper engineering control method in place. Note the dust.
Advance to the next slide.

## Slide 142: Module 3: Silica Health Hazard Information and Medical Surveillance:
Example of silica dust exposure
Notes: Instructor will go over the example picture and note the exposure from the dust. Also asking what methods can be used to control this dust?
Example of cutting cement without the proper engineering control method in place. Note the dust.
Advance to the next slide.

## Slide 143: Module 3: Silica Health Hazard Information and Medical Surveillance:
Example of silica dust exposure
Notes: Instructor will go over the example picture and note the exposure from the dust. Also asking what methods can be used to control this dust?
Example of cutting cement without the proper engineering control method in place. Note the dust.
Advance to the next slide.

## Slide 144: Module 3: Silica Health Hazard Information and Medical Surveillance:
Example of silica dust exposure
Notes: Instructor will go over the example picture and note the exposure from the dust. Also asking what methods can be used to control this dust?
Example of cutting cement without the proper engineering control method in place. Note the dust.
Advance to the next slide.

## Slide 145: Module 3: Silica Health Hazard Information and Medical Surveillance:
Example of silica dust exposure
Notes: Instructor will go over the example picture and note the exposure from the dust. Also asking what methods can be used to control this dust?
Example of cutting granite without the proper engineering control method in place. Note the dust.
Advance to the next slide.

## Slide 146: Module 3: Silica Health Hazard Information and Medical Surveillance:
Example of silica dust exposure
Notes: Instructor will go over the example picture and note the exposure from the dust. Also asking what methods can be used to control this dust?
Example of cutting cement without the proper engineering control method in place. Note the dust.
Advance to the next slide.

## Slide 147: Module 3: Silica Health Hazard Information and Medical Surveillance:
Example of silica dust exposure
Notes: Instructor will go over the example picture and note the exposure from the dust. Also asking what methods can be used to control this dust?
Example of jackhammering without the proper engineering control method or PPE in place. Note the dust.
Advance to the next slide.

## Slide 148: Module 3: Silica Health Hazard Information and Medical Surveillance:
Example of silica dust exposure
Notes: Instructor will go over the example picture and note the exposure from the dust. Also asking what methods can be used to control this dust?
Example of cutting cement block without the proper engineering control method in place. Note the dust.
Advance to the next slide.

## Slide 149: Module 3: Silica Health Hazard Information and Medical Surveillance:
Example of silica dust exposure
Notes: Instructor will go over the example picture and note the exposure from the dust. Also asking what methods can be used to control this dust?
Example of cutting cement block without the proper engineering control method in place. Note the dust.
Advance to the next slide.

## Slide 150: Module 3: Silica Health Hazard Information and Medical Surveillance:
Example of silica dust exposure
Notes: Instructor will go over the example picture and note the exposure from the dust. Also asking what methods can be used to control this dust?
Example of breaking cement without the proper engineering control method in place. Note the dust.
Advance to the next slide.

## Slide 151: Module 3: Silica Health Hazard Information and Medical Surveillance:
Example of silica dust exposure
Notes: Instructor will go over the example picture and note the exposure from the dust. Also asking if this methods can be used to control this dust?
Example of cutting pavers with the proper engineering control method in place. Note no dust.
Advance to the next slide.

## Slide 152: Module 3: Silica Health Hazard Information and Medical Surveillance:
Example of silica dust exposure
Notes: Instructor will go over the example picture and note the exposure from the dust. Also asking if this methods can be used to control this dust?
Example of cutting cement block with the proper engineering control method in place. Note no dust.
Advance to the next slide.

## Slide 153: Module 3: Silica Health Hazard Information and Medical Surveillance:
Example of silica dust exposure
Notes: Instructor will go over the example picture and note the exposure from the dust. Also asking if this method can be used to control this dust?
Example of cutting cement with the proper engineering control method in place. Note no dust.
Advance to the next slide.

## Slide 154: Module 3: Silica Health Hazard Information and Medical Surveillance:
Example of silica dust equipment
Notes: Instructor will go over the example picture and note the system on this unit.
Example of cutting tool with the proper engineering control method in place.
Click to highlight the water tank.
Advance to the next slide.

## Slide 155: Module 3: Silica Health Hazard Information and Medical Surveillance:
Example of silica dust equipment
Notes: Instructor will go over the example picture and note the system on this unit.
Example of cutting tool with the proper engineering control method in place.
Click to highlight the connection point for water to the saw.
Advance to the next slide.

## Slide 156: Module 3: Silica Health Hazard Information and Medical Surveillance:
Example of silica dust equipment
Notes: Instructor will go over the example picture and note the system on this unit.
Example of cutting tool with the proper engineering control method in place.
Click to highlight the tank for water supply.
Note that this water needs to changed and disposed of safely. Once it dries it is becomes a hazard for clean-up.
Advance to the next slide.

## Slide 157: Module 3: Silica Health Hazard Information and Medical Surveillance:
Take steps now to ensure the requirements can be met by the compliance dates:
1. Implement specified exposure control methods in Table 1.
2. Complete exposure assessments needed to select
appropriate engineering controls and respiratory protection
for tasks not in Table 1.
3. Set up respiratory protection programs where required.
Notes: Instructor is to review the steps to ensure compliance:
Take steps now to ensure the requirements can be met by the compliance dates.
1. Implement specified exposure control methods in Table 1.
2. Complete exposure assessments needed to select appropriate engineering controls and respiratory protection for tasks not in Table 1.
3. Set up respiratory protection programs where required.
Advance to the next slide.

## Slide 158: Module 3: Silica Health Hazard Information and Medical Surveillance:
Take steps now to ensure the requirements can be met by the compliance dates. (Continued)
4. Get appropriate equipment, controls, and respirators.
5. Arrange for medical surveillance.
6. Take actions such as the following to meet all other
requirements:
a. Determine appropriate housekeeping
methods.
b. Prepare a written exposure control plan.
c. Set up a training program.
d. Set up a recordkeeping system.
Notes: Instructor is to review the steps to ensure compliance:
Take steps now to ensure the requirements can be met by the compliance dates. (Continued)
4. Get appropriate equipment, controls, and respirators.
5. Arrange for medical surveillance.
6. Take actions such as the following to meet all other requirements: a. Determine appropriate housekeeping methods. b. Prepare a written exposure control plan. c. Set up a training program. d. Set up a recordkeeping system.
Advance to the next slide.

## Slide 159: Module 3: Silica Health Hazard Information and Medical Surveillance:
Summary:
  Identify the basic health risks, both short and long-term, associated with silica exposure.
  Identify the basic activities likely to expose workers to silica exposure.
  Identify some general differences between engineering and administrative controls and PPE.
Notes: Instructor is to review the health risk, methods of exposure, as well as different control methods:
Summary:
  Identify the basic health risks, both short and long-term, associated with silica exposure
  Identify the basic activities likely to expose workers to silica exposure
  Identify some general differences between engineering and administrative controls and PPE
Advance to the next slide.

## Slide 160: Module 3: Silica Health Hazard Information and Medical Surveillance:
Any Questions?
Notes: Instructor will answer any student questions and then prepare to start Tab 4.

## Slide 161: USF OTI Education Center Respirable Silica in the Construction Industry
Module 4
Notes: Instructor will welcome students back.
Advance to the next slide.

## Slide 162: Module 4
This material was produced under grant number SH-29661-SH6 from OSHA. It does not necessarily reflect the views or policies of the U.S. Department of Labor, nor does mention of trade names, commercial products, or organizations imply endorsement by the U.S. Government.
Specific control Methods - Training and group activities

## Slide 163: Module 4: Specific control Methods - Training and group activities:
Terminal Objective:
  Trainees will be able to discuss health hazards of respirable silica.
  Trainees will be able to identify silica dust hazards and controls in the workplace.
Enabling Objective:
  Identify health risks, both short and long-term, associated with silica exposure.
  Identify activities likely to expose workers to silica.
  Identify the differences between engineering and administrative controls and PPE.
Notes: Instructor to review the Objectives with the students.
Terminal Objective:
  Trainees will be able to describe the control methods of the new silica standard for construction
Enabling Objective:
  Identify general differences between the old and new silica standard
  Identify general the areas of the new standard that trainees should be concerned with
Advance to the next slide.

## Slide 164: Module 4: Specific control Methods - Training and group activities:
Major Provisions of the Construction Standard the standard for construction includes provisions for employers to:
• Measure the amount of silica that workers are exposed to if it may be at or above an action level of 25 μg/m3 (micrograms of silica per cubic meter of air), averaged over an 8-hour day;
• Protect workers from respirable crystalline silica exposures above the PEL of 50 μg/m3, averaged over an 8-hour day;
• Limit workers’ access to areas where they could be exposed above the PEL;
• Use dust controls to protect workers from silica exposures above the PEL;
Notes: Instructor to review major provision of the Construction Standard on Silica with the students.
Major Provisions of the Construction Standard the standard for construction includes provisions for employers to:
• Measure the amount of silica that workers are exposed to if it may be at or above an action level of 25 μg/m3 (micrograms of silica per cubic meter of air), averaged over an 8-hour day;
• Protect workers from respirable crystalline silica exposures above the PEL of 50 μg/m3, averaged over an 8-hour day;
• Limit workers’ access to areas where they could be exposed above the PEL;
• Use dust controls to protect workers from silica exposures above the PEL;
Advance to the next slide.

## Slide 165: Module 4: Specific control Methods - Training and group activities:
Major Provisions (continued)
• Provide respirators to workers when dust controls cannot limit exposures to the PEL;
• Offer medical exams—including chest X-rays and lung function tests—every three years for workers exposed above the PEL for 30 or more days per year;
• Train workers on work operations that result in silica exposure and ways to limit exposure; and
• Keep records of workers’ silica exposure and medical exams.
Notes: Instructor to review major provision of the Construction Standard on Silica with the students.
Major Provisions (continued)
• Provide respirators to workers when dust controls cannot limit exposures to the PEL;
• Offer medical exams—including chest X-rays and lung function tests—every three years for workers exposed above the PEL for 30 or more days per year;
• Train workers on work operations that result in silica exposure and ways to limit exposure; and
• Keep records of workers’ silica exposure and medical exams.
Advance to the next slide.

## Slide 166: Module 4: Specific control Methods - Training and group activities:
Control Methods
Notes: Instructor will inform the students about the next session is on control methods.
.
Control Methods
In this section specific control measures will be discuss.
Advance to the next slide.

## Slide 167: Module 4: Specific control Methods - Training and group activities:
The silica standard for construction provides a flexible approach for construction employers to achieve compliance.
The standard includes Table 1, which lists 18 common tasks using various types of tools or equipment found at construction sites.
For each employee engaged in a task in Table 1, employers who choose to follow the Table for that task are required to fully and properly implement the engineering controls, work practices, and respiratory protection specified in Table 1.
Employers who comply with Table 1 are not required to conduct exposure assessments or comply with a PEL for those employees
Notes: Instructor to the two methods to prevent exposure to Silica with the students.
The silica standard for construction provides a flexible approach for construction employers to achieve compliance. The standard includes Table 1, which lists 18 common tasks using various types of tools or equipment found at construction sites. For each employee engaged in a task in Table 1, employers who choose to follow the Table for that task are required to fully and properly implement the engineering controls, work practices, and respiratory protection specified in Table 1. Employers who comply with Table 1 are not required to conduct exposure assessments or comply with a PEL for those employees
Advance to the next slide.

## Slide 168: Module 4: Specific control Methods - Training and group activities:
Notes: Instructor will discuss Table 1 and focus on the control methods:
(i) Stationary masonry saws
Use saw equipped with integrated water delivery system that continuously feeds water to the blade. Operate and maintain tool in accordance with manufacturer’s instructions to minimize dust emissions.
(ii) Handheld power saws (any blade diameter)
Use saw equipped with integrated water delivery system that continuously feeds water to the blade. Operate and maintain tool in accordance with manufacturer’s instructions to minimize dust emissions . − When used outdoors. − When used indoors or in an enclosed area.
Advance to the next slide.

## Slide 169: Module 4: Specific control Methods - Training and group activities (i):
Stationary masonry saws must be equipped with an integrated water delivery system (commercially developed specifically for the type of tool in use) that continuously feeds water to the blade.
The water delivery system includes a nozzle for spraying water attached near the blade that is connected to a water basin by a hose and pump.
The tool must be operated and maintained in accordance with manufacturer’s instructions to minimize dust emissions. Stationary masonry saws equipped with an integrated system for blade cooling also suppress dust and meet the requirements of Table 1.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
Stationary masonry saws must be equipped with an integrated water delivery system (commercially developed specifically for the type of tool in use) that continuously feeds water to the blade. The water delivery system usually includes a nozzle for spraying water attached near the blade that is connected to a water basin by a hose and pump. The tool must be operated and maintained in accordance with manufacturer’s instructions to minimize dust emissions. Stationary masonry saws equipped with an integrated system for blade cooling also suppress dust and meet the requirements of Table 1.
Advance to the next slide.

## Slide 170: Module 4: Specific control Methods - Training and group activities (i):
Full and proper implementation of water controls on stationary masonry saws requires the employer to ensure that:
An adequate supply of water for dust suppression is used;
The spray nozzle is working properly to apply water at the point of dust generation;
The spray nozzle is not clogged or damaged; and
All hoses and connections are intact.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
Full and proper implementation of water controls on stationary masonry saws requires the employer to ensure that:
An adequate supply of water for dust suppression is used;
The spray nozzle is working properly to apply water at the point of dust generation;
The spray nozzle is not clogged or damaged; and
All hoses and connections are intact.
Advance to the next slide.

## Slide 171: Module 4: Specific control Methods - Training and group activities (i):
Table 1 does not specify a minimum flow rate; however, water must be applied at the flow rates specified by the manufacturer.
When using a stationary masonry saw indoors or in an enclosed space (areas where airborne dust can buildup, such as a structure with a roof and three walls), employers must provide additional exhaust as needed to minimize the accumulation of visible airborne dust.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
Table 1 does not specify a minimum flow rate; however, water must be applied at the flow rates specified by the manufacturer.
When using a stationary masonry saw indoors or in an enclosed space (areas where airborne dust can buildup, such as a structure with a roof and three walls), employers must provide additional exhaust as needed to minimize the accumulation of visible airborne dust.
Advance to the next slide.

## Slide 172: Module 4: Specific control Methods - Training and group activities:
Respiratory protection is not required for work with stationary masonry saws regardless of task duration.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
See the section on Indoors or Enclosed Areas for more information.
Respiratory protection is not required for work with stationary masonry saws regardless of task duration.
Advance to the next slide.

## Slide 173: Module 4: Specific control Methods - Training and group activities (ii):
Handheld power saws with any blade diameter must be equipped with an integrated water delivery system that continuously feeds water to the blade.
The water delivery system includes a nozzle for spraying water attached near the blade that is connected to a water basin via a hose and pump.
The tool must be operated and maintained in accordance with manufacturer’s instructions to minimize dust emissions.
Handheld power saws equipped with an integrated water delivery system for blade cooling also suppress dusts and meet the requirements of Table 1.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
Handheld power saws with any blade diameter must be equipped with an integrated water delivery system (commercially developed specifically for the type of tool in use) that continuously feeds water to the blade. The water delivery system usually includes a nozzle for spraying water attached near the blade that is connected to a water basin via a hose and pump. The tool must be operated and maintained in accordance with manufacturer’s instructions to minimize dust emissions. Handheld power saws equipped with an integrated water delivery system for blade cooling also suppress dusts and meet the requirements of Table 1
Advance to the next slide.

## Slide 174: Module 4: Specific control Methods - Training and group activities (ii):
Full and proper implementation of water controls on handheld power saws requires the employer to ensure that:
An adequate supply of water for dust suppression is used;
The spray nozzle is working properly to apply water at the point of dust generation;
The spray nozzle is not clogged or damaged;
All hoses and connections are intact.
Table 1 does not specify a minimum flow rate; however, water must be applied at the flow rate specified by the manufacturer.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
Full and proper implementation of water controls on handheld power saws requires the employer to ensure that:
An adequate supply of water for dust suppression is used;
The spray nozzle is working properly to apply water at the point of dust generation;
The spray nozzle is not clogged or damaged;
All hoses and connections are intact.
Table 1 does not specify a minimum flow rate; however, water must be applied at the flow rate specified by the manufacturer.
Advance to the next slide.

## Slide 175: Module 4: Specific control Methods - Training and group activities (ii):
When working with handheld power saws of any blade diameter, respiratory protection with a minimum APF of 10 is required for work done outdoors for more than four hours per shift and for work done indoors, or in an enclosed location, regardless of task duration.
When using a handheld saw indoors or in enclosed spaces (areas where airborne dust can buildup, such as a structure with a roof and three walls), employers must provide additional exhaust, as needed to minimize the accumulation of visible airborne dust.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
When working with handheld power saws of any blade diameter, respiratory protection with a minimum APF of 10 is required for work done outdoors for more than four hours per shift and for work done indoors, or in an enclosed location, regardless of task duration.
When using a handheld saw indoors or in enclosed spaces (areas where airborne dust can buildup, such as a structure with a roof and three walls), employers must provide additional exhaust, as needed to minimize the accumulation of visible airborne dust. See the section on Indoors or Enclosed Areas for more information.
Advance to the next slide.

## Slide 176: Module 4: Specific control Methods - Training and group activities:
(iii) Handheld power saws for cutting fiber cement board (with blade diameter of 8 inches or less) *picture obtained from www.lhsfna.org | For tasks performed outdoors only: Use saw equipped with commercially available dust collection system. Operate and maintain tool in accordance with manufacturer's instructions to minimize dust emissions. Dust collector must provide the air flow recommended by the tool manufacturer, or greater, and have a filter with 99% or greater efficiency. | None | None
(iv) Walk-behind saws *picture obtained from www.lhsfna.org | Use saw equipped with integrated water delivery system that continuously feeds water to the blade. Operate and maintain tool in accordance with manufacturer's instructions to minimize dust emissions. − When used outdoors. − When used indoors or in an enclosed area | None APF 10 | None APF 10
(v) Drivable saws *picture obtained from www.lhsfna.org | For tasks performed outdoors only: Use saw equipped with integrated water delivery system that continuously feeds water to the blade. Operate and maintain tool in accordance with manufacturer's instructions to minimize dust emissions | None | None
Notes: Instructor will discuss Table 1 and focus on the control methods:
(iii) Handheld power saws for cutting fiber cement board (with blade diameter of 8 inches or less)
For tasks performed outdoors only: Use saw equipped with commercially available dust collection system. Operate and maintain tool in accordance with manufacturer's instructions to minimize dust emissions. Dust collector must provide the air flow recommended by the tool manufacturer, or greater, and have a filter with 99% or greater efficiency.
(iv) Walk-behind saws
Use saw equipped with integrated water delivery system that continuously feeds water to the blade. Operate and maintain tool in accordance with manufacturer's instructions to minimize dust emissions. − When used outdoors. − When used indoors or in an enclosed area
(v) Drivable saws
For tasks performed outdoors only: Use saw equipped with integrated water delivery system that continuously feeds water to the blade. Operate and maintain tool in accordance with manufacturer's instructions to minimize dust emissions
Advance to the next slide.

## Slide 177: Module 4: Specific control Methods - Training and group activities (iii):
Specialty handheld power saws for cutting fiber-cement board (with a blade diameter of 8 inches or less) must be equipped with commercially available dust collection systems and a filter with a 99 percent or greater efficiency.
The saws must be operated and maintained in accordance with the manufacturer’s instructions to minimize dust emissions, and provide the air flow rate recommended by the manufacturer or greater. When employers are complying with Table 1, the saws must only be used outdoors
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
Specialty handheld power saws for cutting fiber-cement board (with a blade diameter of 8 inches or less) must be equipped with commercially available dust collection systems and a filter with a 99 percent or greater efficiency.
The saws must be operated and maintained in accordance with the manufacturer’s instructions to minimize dust emissions, and provide the air flow rate recommended by the manufacturer or greater. When employers are complying with Table 1, the saws must only be used outdoors
Advance to the next slide.

## Slide 178: Module 4: Specific control Methods - Training and group activities (iii):
Full and proper implementation of dust collection systems on handheld power saws for cutting fiber-cement board requires the employer to ensure that:
The shroud or cowling is intact and installed in accordance with the manufacturer’s instructions;
The hose connecting the tool to the vacuum is intact and without kinks or tight bends;
The filter(s) on the vacuum are cleaned or changed in accordance with the manufacturer’s instructions to prevent clogging; and
The dust collection bags are emptied to avoid overfilling.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
Full and proper implementation of dust collection systems on handheld power saws for cutting fiber-cement board requires the employer to ensure that:
The shroud or cowling is intact and installed in accordance with the manufacturer’s instructions;
The hose connecting the tool to the vacuum is intact and without kinks or tight bends;
The filter(s) on the vacuum are cleaned or changed in accordance with the manufacturer’s instructions to prevent clogging; and
The dust collection bags are emptied to avoid overfilling.
Advance to the next slide.

## Slide 179: Module 4: Specific control Methods - Training and group activities:
Respiratory protection is not required for work outdoors with specialty handheld power saws while cutting fiber-cement board regardless of task duration
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
Respiratory protection is not required for work outdoors with specialty handheld power saws while cutting fiber-cement board regardless of task duration
Advance to the next slide.

## Slide 180: Module 4: Specific control Methods - Training and group activities (iv):
Walk-behind saws must be equipped with an integrated water delivery system (commercially developed specifically for the type of tool in use) that continuously feeds water to the blade.
The tool must be operated and maintained in accordance with manufacturer’s instructions to minimize dust emissions.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
Walk-behind saws must be equipped with an integrated water delivery system (commercially developed specifically for the type of tool in use) that continuously feeds water to the blade. The tool must be operated and maintained in accordance with manufacturer’s instructions to minimize dust emissions.
Advance to the next slide.

## Slide 181: Module 4: Specific control Methods - Training and group activities (iv):
Full and proper implementation of water controls on walk-behind saws requires the employer to ensure that:
An adequate supply of water for dust suppression is used;
The spray nozzles are working properly to apply water at the point of dust generation;
The spray nozzles are not clogged or damaged; and
All hoses and connections are intact.
Table 1 does not specify a minimum flow rate; however, water must be applied at the flow rate specified by the manufacturer.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
Full and proper implementation of water controls on walk-behind saws requires the employer to ensure that:
An adequate supply of water for dust suppression is used;
The spray nozzles are working properly to apply water at the point of dust generation;
The spray nozzles are not clogged or damaged; and
All hoses and connections are intact.
Table 1 does not specify a minimum flow rate; however, water must be applied at the flow rate specified by the manufacturer.
Advance to the next slide.

## Slide 182: Module 4: Specific control Methods - Training and group activities (iv):
Walk-behind saws used to cut roads and cut pavement are most commonly used outdoors, though they can also be used indoors to cut concrete floors. When using walk-behind saws indoors or in enclosed areas (areas where airborne dust can
buildup, such as a structure with a roof and three walls), employers must provide additional exhaust, as needed to minimize the accumulation of visible airborne dust.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
Walk-behind saws used to cut roads and cut pavement are most commonly used outdoors, though they can also be used indoors to cut concrete floors. When using walk-behind saws indoors or in enclosed areas (areas where airborne dust can
buildup, such as a structure with a roof and three walls), employers must provide additional exhaust, as needed to minimize the accumulation of visible airborne dust. See the section on Indoors or Enclosed Areas for more information.
Advance to the next slide.

## Slide 183: Module 4: Specific control Methods - Training and group activities:
When working outdoors, respiratory protection is not required for work with walk-behind saws regardless of task duration. When working indoors, or in an enclosed location, respiratory protection with a minimum APF of 10 is required regardless of task duration.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
When working outdoors, respiratory protection is not required for work with walk-behind saws regardless of task duration. When working indoors, or in an enclosed location, respiratory protection with a minimum APF of 10 is required regardless of task duration.
Advance to the next slide.

## Slide 184: Module 4: Specific control Methods - Training and group activities (v):
Drivable saws used to cut silica-containing materials (such as concrete, asphalt, granite and terrazzo) must be equipped with an integrated water delivery system (commercially developed specifically for the type of tool in use) that continuously feeds water to the blade and must be operated and maintained in accordance with manufacturer’s instructions to minimize dust emissions. Employers following Table 1 must only allow the saws to be used outdoors.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
Drivable saws used to cut silica-containing materials (such as concrete, asphalt, granite and terrazzo) must be equipped with an integrated water delivery system (commercially developed specifically for the type of tool in use) that continuously feeds water to the blade and must be operated and maintained in accordance with manufacturer’s instructions to minimize dust emissions. Employers following Table 1 must only allow the saws to be used outdoors.
Advance to the next slide.

## Slide 185: Module 4: Specific control Methods - Training and group activities (v):
Full and proper implementation of water controls on drivable saws requires the employer to ensure that:
An adequate supply of water for dust suppression is used;
The spray nozzles produce a pattern that applies water at the point of dust generation;
The spray nozzles are not clogged or damaged; and
All hoses and connections are intact.
Respiratory protection is not required for work with drivable saws regardless of task duration.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
Full and proper implementation of water controls on drivable saws requires the employer to ensure that:
An adequate supply of water for dust suppression is used;
The spray nozzles produce a pattern that applies water at the point of dust generation;
The spray nozzles are not clogged or damaged; and
All hoses and connections are intact.
Respiratory protection is not required for work with drivable saws regardless of task duration.
Advance to the next slide.

## Slide 186: Module 4: Specific control Methods - Training and group activities:
(vi) Rig-mounted core saws or drills *picture obtained from www.lhsfna.org | Use tool equipped with integrated water delivery system that supplies water to cutting surface. Operate and maintain tool in accordance with manufacturer's instructions to minimize dust emissions. | None | None
(vii) Handheld and stand-mounted drills (including impact and rotary hammer drills) *picture obtained from www.lhsfna.org | Use drill equipped with commercially available shroud or cowling with dust collection system. Operate and maintain tool in accordance with manufacturer's instructions to minimize dust emissions. Dust collector must provide the air flow recommended by the tool manufacturer, or greater, and have a filter with 99% or greater efficiency and a filter-cleaning mechanism. Use a HEPA-filtered vacuum when cleaning holes | None | None
Notes: Instructor will discuss Table 1 and focus on the control methods:
(vi) Rig-mounted core saws or drills
Use tool equipped with integrated water delivery system that supplies water to cutting surface. Operate and maintain tool in accordance with manufacturer's instructions to minimize dust emissions.
(vii) Handheld and stand-mounted drills (including impact and rotary hammer drills)
Use drill equipped with commercially available shroud or cowling with dust collection system. Operate and maintain tool in accordance with manufacturer's instructions to minimize dust emissions. Dust collector must provide the air flow recommended by the tool manufacturer, or greater, and have a filter with 99% or greater efficiency and a filter-cleaning mechanism. Use a HEPA-filtered vacuum when cleaning holes
Advance to the next slide.

## Slide 187: Module 4: Specific control Methods - Training and group activities (vi):
Rig-mounted core saws or drills must be equipped with an integrated water delivery system (commercially developed specifically for the type of tool in use) that supplies water to the cutting surface, and must be operated and maintained in accordance with manufacturer’s instructions to minimize dust emissions.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
Rig-mounted core saws or drills must be equipped with an integrated water delivery system (commercially developed specifically for the type of tool in use) that supplies water to the cutting surface, and must be operated and maintained in accordance with manufacturer’s instructions to minimize dust emissions.
Advance to the next slide.

## Slide 188: Module 4: Specific control Methods - Training and group activities (vi):
Full and proper implementation of water controls on rig-mounted core saws or drills requires the employer to ensure that:
An adequate supply of water for dust suppression is used;
The spray nozzles produce a pattern that applies water at the point of dust generation;
The spray nozzles are not clogged or damaged; and
All hoses and connections are intact.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
Full and proper implementation of water controls on rig-mounted core saws or drills requires the employer to ensure that:
An adequate supply of water for dust suppression is used;
The spray nozzles produce a pattern that applies water at the point of dust generation;
The spray nozzles are not clogged or damaged; and
All hoses and connections are intact.
Advance to the next slide.

## Slide 189: Module 4: Specific control Methods - Training and group activities (vii):
Handheld and stand-mounted drills (including impact and rotary hammer drills). Handheld and stand-mounted drills must be equipped with a commercially available shroud or cowling with a dust collection system that provides at least the minimum air flow recommended by the manufacturer.
The dust collection system must include a filter cleaning mechanism and be equipped with a filter with 99 percent or greater efficiency.
In addition, the tool must be operated and maintained in accordance with manufacturer’s instructions to minimize dust emissions.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
Handheld and stand-mounted drills (including impact and rotary hammer drills). Handheld and stand-mounted drills must be equipped with a commercially available shroud or cowling with a dust collection system that provides at least the minimum air flow recommended by the manufacturer. The dust collection system must include a filter cleaning mechanism and be equipped with a filter with 99 percent or greater efficiency. In addition, the tool must be operated and maintained in accordance with manufacturer’s instructions to minimize dust emissions.
Advance to the next slide.

## Slide 190: Module 4: Specific control Methods - Training and group activities (vii):
Full and proper implementation of dust collection systems on handheld drills requires the employer to ensure that:
The shroud or cowling is intact and installed in accordance with the manufacturer’s instructions;
The hose connecting the tool to the vacuum is intact and without kinks or tight bends;
The filter(s) on the vacuum are cleaned or changed in accordance with the manufacturer’s instructions; and
The dust collection bags are emptied to avoid overfilling.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
Full and proper implementation of dust collection systems on handheld drills requires the employer to ensure that:
The shroud or cowling is intact and installed in accordance with the manufacturer’s instructions;
The hose connecting the tool to the vacuum is intact and without kinks or tight bends;
The filter(s) on the vacuum are cleaned or changed in accordance with the manufacturer’s instructions; and
The dust collection bags are emptied to avoid overfilling.
Advance to the next slide.

## Slide 191: Module 4: Specific control Methods - Training and group activities:
A HEPA-filtered vacuum must be used when cleaning holes. Compressed air can be used to clean holes when used in conjunction with a HEPA-filtered vacuum to capture the dust or a hole cleaning kit designed for use with compressed air.
When using handheld and stand-mounted drills indoors or in enclosed areas (areas where airborne dust can buildup, such as a structure with a roof and three walls), employers must provide additional exhaust, as needed to minimize the accumulation of visible airborne dust.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
A HEPA-filtered vacuum must be used when cleaning holes. Compressed air can be used to clean holes when used in conjunction with a HEPA-filtered vacuum to capture the dust or a hole cleaning kit designed for use with compressed air.
When using handheld and stand-mounted drills indoors or in enclosed areas (areas where airborne dust can buildup, such as a structure with a roof and three walls), employers must provide additional exhaust, as needed to minimize the accumulation of visible airborne dust. See the section on Indoors or Enclosed Areas for more information.
Advance to the next slide.

## Slide 192: Module 4: Specific control Methods - Training and group activities:
Respiratory protection is not required when using handheld or stand-mounted drills equipped with a dust collection system, including for overhead drilling, regardless of task duration.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
Respiratory protection is not required when using handheld or stand-mounted drills equipped with a dust collection system, including for overhead drilling, regardless of task duration.
Worker
Advance to the next slide.

## Slide 193: Module 4: Specific control Methods - Training and group activities (vi):
When using rig-mounted core saws or drills indoors or in enclosed areas (areas where airborne dust can buildup, such as a structure with a roof and three walls), employers must provide additional exhaust, as needed to minimize the accumulation of visible airborne dust. See the section on Indoors or Enclosed Areas for more information.
Respiratory protection is not required for work with rig-mounted core saws or drills regardless of task duration.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
When using rig-mounted core saws or drills indoors or in enclosed areas (areas where airborne dust can buildup, such as a structure with a roof and three walls), employers must provide additional exhaust, as needed to minimize the accumulation of visible airborne dust. See the section on Indoors or Enclosed Areas for more information.
Respiratory protection is not required for work with rig-mounted core saws or drills regardless of task duration.
Advance to the next slide.

## Slide 194: Module 4: Specific control Methods - Training and group activities (vii):
Full and proper implementation of dust collection systems on handheld drills requires the employer to ensure that:
The shroud or cowling is intact and installed in accordance with the manufacturer’s instructions; The hose connecting the tool to the vacuum is intact and without kinks or tight bends;
The filter(s) on the vacuum are cleaned or changed in accordance with the manufacturer’s instructions; and
The dust collection bags are emptied to avoid overfilling.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
Full and proper implementation of dust collection systems on handheld drills requires the employer to ensure that:
The shroud or cowling is intact and installed in accordance with the manufacturer’s instructions; The hose connecting the tool to the vacuum is intact and without kinks or tight bends;
The filter(s) on the vacuum are cleaned or changed in accordance with the manufacturer’s instructions; and
The dust collection bags are emptied to avoid overfilling.
Advance to the next slide.

## Slide 195: Module 4: Specific control Methods - Training and group activities:
(viii) Dowel drilling rigs for concrete *picture obtained from www.lhsfna.org | For tasks performed outdoors only: Use shroud around drill bit with a dust collection system. Dust collector must have a filter with 99% or greater efficiency and a filter-cleaning mechanism. Use a HEPA-filtered vacuum when cleaning holes. | APF 10 | APF 10
(ix) Vehicle-mounted drilling rigs for rock and concrete *picture obtained from www.lhsfna.org | Use dust collection system with close capture hood or shroud around drill bit with a low-flow water spray to wet the dust at the discharge point from the dust collector; or Operate from within an enclosed cab and use water for dust suppression on drill bit. | None | None
Notes: Instructor will discuss Table 1 and focus on the control methods:
(viii) Dowel drilling rigs for concrete
For tasks performed outdoors only: Use shroud around drill bit with a dust collection system. Dust collector must have a filter with 99% or greater efficiency and a filter-cleaning mechanism. Use a HEPA-filtered vacuum when cleaning holes
(ix) Vehicle-mounted drilling rigs for rock and concrete
Use dust collection system with close capture hood or shroud around drill bit with a low-flow water spray to wet the dust at the discharge point from the dust collector. OR Operate from within an enclosed cab and use water for dust suppression on drill bit.
Advance to the next slide.

## Slide 196: Module 4: Specific control Methods - Training and group activities (viii):
Dowel drills for concrete (i.e., gang drills) are drills equipped with multiple drill bits that are used to drill several holes at the same time.
Dowel drills must be equipped with a shroud around the drill bit and a dust collection system that has a filter with 99 percent or greater efficiency. The dust collection equipment must be equipped with a filter cleaning mechanism.
Employers following Table 1 must allow dowel drilling rigs to only be used outdoors.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
Dowel drills for concrete (i.e., gang drills) are drills equipped with multiple drill bits that are used to drill several holes at the same time. Dowel drills must be equipped with a shroud around the drill bit and a dust collection system that has a filter with 99 percent or greater efficiency. The dust collection equipment must be equipped with a filter cleaning mechanism. Employers following Table 1 must allow dowel drilling rigs to only be used outdoors.
Advance to the next slide.

## Slide 197: Module 4: Specific control Methods - Training and group activities (viii):
Full and proper implementation of dust collection systems on dowel drilling rigs requires the employer to ensure that:
The shroud is intact and installed in accordance with the manufacturer’s instructions;
The hose connecting the tool to the vacuum is intact and without kinks or tight bends;
The filter(s) on the vacuum are cleaned or changed in accordance with the manufacturer’s instructions; and
The dust collection bags are emptied to avoid overfilling.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
Full and proper implementation of dust collection systems on dowel drilling rigs requires the employer to ensure that:
The shroud is intact and installed in accordance with the manufacturer’s instructions;
The hose connecting the tool to the vacuum is intact and without kinks or tight bends;
The filter(s) on the vacuum are cleaned or changed in accordance with the manufacturer’s instructions; and
The dust collection bags are emptied to avoid overfilling.
Advance to the next slide.

## Slide 198: Module 4: Specific control Methods - Training and group activities (ix):
Vehicle-mounted rock and concrete drilling rigs must be equipped with a dust collection system with a close capture hood or shroud around the drill bit, and a low-flow water spray to wet the dust discharged from the dust collector. This combination of local exhaust ventilation (LEV) and water application controls dust at all emission points that can contribute to the operator’s and other employees’ exposures.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
Vehicle-mounted rock and concrete drilling rigs must be equipped with a dust collection system with a close capture hood or shroud around the drill bit, and a low-flow water spray to wet the dust discharged from the dust collector. This combination of local exhaust ventilation (LEV) and water application controls dust at all emission points that can contribute to the operator’s and other employees’ exposures.
Advance to the next slide.

## Slide 199: Module 4: Specific control Methods - Training and group activities:
Employers also have the option to have the drill operator work within an enclosed cab and, when necessary, apply water at the drill bit, as described above, to reduce exposures to other employees in the area. See the section on Enclosed Cabs for more information on how to make sure cabs meet the requirements of Table 1.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
Employers also have the option to have the drill operator work within an enclosed cab and, when necessary, apply water at the drill bit, as described above, to reduce exposures to other employees in the area. See the section on Enclosed Cabs for more information on how to make sure cabs meet the requirements of Table 1.
Advance to the next slide.

## Slide 200: Module 4: Specific control Methods - Training and group activities:
Full and proper implementation of dust collection systems on vehicle-mounted drilling rigs requires the employer to ensure that:
The shroud or hood is intact and installed in accordance with the manufacturer’s instructions;
The hose connecting the tool to the vacuum is intact and without kinks or tight bends;
The filter(s) on the vacuum are cleaned or changed in accordance with the manufacturer’s instructions; and
The dust collection bags are emptied to avoid overfilling.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
Full and proper implementation of dust collection systems on vehicle-mounted drilling rigs requires the employer to ensure that:
The shroud or hood is intact and installed in accordance with the manufacturer’s instructions;
The hose connecting the tool to the vacuum is intact and without kinks or tight bends;
The filter(s) on the vacuum are cleaned or changed in accordance with the manufacturer’s instructions; and
The dust collection bags are emptied to avoid overfilling.
Advance to the next slide.

## Slide 201: Module 4: Specific control Methods - Training and group activities:
Full and proper implementation of water controls on vehicle-mounted drilling rigs requires the employer to ensure that:
An adequate supply of water for dust suppression is used;
The spray nozzles are working properly and produce a pattern that applies water on the discharge point from the dust collector;
The spray nozzles are not clogged or damaged; and
All hoses and connections are intact.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
Full and proper implementation of water controls on vehicle-mounted drilling rigs requires the employer to ensure that:
An adequate supply of water for dust suppression is used;
The spray nozzles are working properly and produce a pattern that applies water on the discharge point from the dust collector;
The spray nozzles are not clogged or damaged; and
All hoses and connections are intact.
Advance to the next slide.

## Slide 202: Module 4: Specific control Methods - Training and group activities:
Respiratory protection is not required for work with vehicle-mounted drilling rigs regardless of task duration.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
Respiratory protection is not required for work with vehicle-mounted drilling rigs regardless of task duration.
Advance to the next slide.

## Slide 203: Module 4: Specific control Methods - Training and group activities:
*pictures obtained from www.lhsfna.org
Notes: Instructor will discuss Table 1 and focus on the control methods:
(x) Jackhammers and handheld powered chipping tools
Use tool with water delivery system that supplies a continuous stream or spray of water at the point of impact. − When used outdoors. − When used indoors or in an enclosed area. OR Use tool equipped with commercially available shroud and dust collection system. Operate and maintain tool in accordance with manufacturer's instructions to minimize dust emissions. Dust collector must provide the air flow recommended by the tool manufacturer, or greater, and have a filter with 99% or greater efficiency and a filter-cleaning mechanism. − When used outdoors. − When used indoors or in an enclosed area.
Advance to the next slide.

## Slide 204: Module 4: Specific control Methods - Training and group activities (x):
Jackhammers and handheld powered chipping tools must be operated using either a water delivery system that supplies a continuous stream or spray of water at the point of impact, or a tool equipped with a commercially available shroud and vacuum dust collection system. Jackhammers and other handheld powered chipping tools must be operated and maintained in accordance with manufacturer’s instructions to minimize dust emissions.
If using the shroud and dust collection system, the vacuum dust collection system must provide at least the air flow recommended by the tool manufacturer, and have a filter with 99 percent or greater efficiency and a filter cleaning mechanism
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
Jackhammers and handheld powered chipping tools must be operated using either a water delivery system that supplies a continuous stream or spray of water at the point of impact, or a tool equipped with a commercially available shroud and vacuum dust collection system. Jackhammers and other handheld powered chipping tools must be operated and maintained in accordance with manufacturer’s instructions to minimize dust emissions.
If using the shroud and dust collection system, the vacuum dust collection system must provide at least the air flow recommended by the tool manufacturer, and have a filter with 99 percent or greater efficiency and a filter cleaning mechanism
Advance to the next slide.

## Slide 205: Module 4: Specific control Methods - Training and group activities:
The water delivery system is not required to be integrated or mounted on the tool; it can be assembled and installed by the employer. However, it must deliver a continuous stream or spray of water at the point of impact.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
The water delivery system is not required to be integrated or mounted on the tool; it can be assembled and installed by the employer. However, it must deliver a continuous stream or spray of water at the point of impact.
Advance to the next slide.

## Slide 206: Module 4: Specific control Methods - Training and group activities (x):
Full and proper implementation of water controls on jackhammers and other handheld powered chipping tools requires the employer to ensure that:
An adequate supply of water for dust suppression is used;
The water sprays are working properly and produce a pattern that applies water at the point of dust generation;
The spray nozzles are not clogged or damaged; and
All hoses and connections are intact.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
Full and proper implementation of water controls on jackhammers and other handheld powered chipping tools requires the employer to ensure that:
An adequate supply of water for dust suppression is used;
The water sprays are working properly and produce a pattern that applies water at the point of dust generation;
The spray nozzles are not clogged or damaged; and
All hoses and connections are intact.
Advance to the next slide.

## Slide 207: Module 4: Specific control Methods - Training and group activities:
Acceptable water delivery systems include direct connections to fixed water lines or portable water tank systems. These water delivery systems can be operated by one worker or could require a second worker to supply the water at the point of impact.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
Acceptable water delivery systems include direct connections to fixed water lines or portable water tank systems. These water delivery systems can be operated by one worker or could require a second worker to supply the water at the point of impact.
Advance to the next slide.

## Slide 208: Module 4: Specific control Methods - Training and group activities:
Full and proper implementation of dust collection systems requires the employer to ensure that:
The shroud is intact and installed in accordance with the manufacturer’s instructions;
The hose connecting the tool to the vacuum is intact and without kinks or tight bends;
The filter(s) on the vacuum are cleaned or changed in accordance with the manufacturer’s instructions; and
The dust collection bags are emptied to avoid overfilling.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
Full and proper implementation of dust collection systems requires the employer to ensure that:
The shroud is intact and installed in accordance with the manufacturer’s instructions;
The hose connecting the tool to the vacuum is intact and without kinks or tight bends;
The filter(s) on the vacuum are cleaned or changed in accordance with the manufacturer’s instructions; and
The dust collection bags are emptied to avoid overfilling.
Advance to the next slide.

## Slide 209: Module 4: Specific control Methods - Training and group activities:
Respiratory protection with an APF of 10 is required when the task is done outdoors for more than four hours per shift, or when the task is done indoors or in an enclosed location regardless of task duration.
When working indoors or in an enclosed space (areas where airborne dust can buildup, such as a structure with a roof and three walls), employers must provide additional exhaust, as needed to minimize the accumulation of visible airborne dust.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
Respiratory protection with an APF of 10 is required when the task is done outdoors for more than four hours per shift, or when the task is done indoors or in an enclosed location regardless of task duration.
When working indoors or in an enclosed space (areas where airborne dust can buildup, such as a structure with a roof and three walls), employers must provide additional exhaust, as needed to minimize the accumulation of visible airborne dust. See the section on Indoors or Enclosed Areas for more information.
Advance to the next slide.

## Slide 210: Module 4: Specific control Methods - Training and group activities:
(xi) Handheld grinders for mortar removal (i.e., tuck-pointing) *picture obtained from www. lhsfna.org | Use grinder equipped with commercially available shroud and dust collection system. Operate and maintain tool in accordance with manufacturer's instructions to minimize dust emissions. Dust collector must provide 25 cubic feet per minute (cfm) or greater of airflow per inch of wheel diameter and have a filter with 99% or greater efficiency and a cyclonic pre-separator or filter-cleaning mechanism. | APF 10 | APF 25
(xii) Handheld grinders for uses other than mortar removal *picture obtained from www. lhsfna.org | For tasks performed outdoors only: Use grinder equipped with integrated water delivery system that continuously feeds water to the grinding surface. Operate and maintain tool in accordance with manufacturer’s instructions to minimize dust emissions. OR Use grinder equipped with commercially available shroud and dust collection system. Operate and maintain tool in accordance with manufacturer's instructions to minimize dust emissions. Dust collector must provide 25 cubic feet per minute (cfm) or greater of airflow per inch of wheel diameter and have a filter with 99% or greater efficiency and a cyclonic pre-separator or filter-cleaning mechanism. − When used outdoors. − When used indoors or in an enclosed area. | None | None
Notes: Instructor will discuss Table 1 and focus on the control methods:
(xi) Handheld grinders for mortar removal (i.e., tuckpointing)
Use grinder equipped with commercially available shroud and dust collection system. Operate and maintain tool in accordance with manufacturer's instructions to minimize dust emissions. Dust collector must provide 25 cubic feet per minute (cfm) or greater of airflow per inch of wheel diameter and have a filter with 99% or greater efficiency and a cyclonic pre-separator or filter-cleaning mechanism.
(xii) Handheld grinders for uses other than mortar removal
For tasks performed outdoors only: Use grinder equipped with integrated water delivery system that continuously feeds water to the grinding surface. Operate and maintain tool in accordance with manufacturer’s instructions to minimize dust emissions. OR Use grinder equipped with commercially available shroud and dust collection system. Operate and maintain tool in accordance with manufacturer's instructions to minimize dust emissions. Dust collector must provide 25 cubic feet per minute (cfm) or greater of airflow per inch of wheel diameter and have a filter with 99% or greater efficiency and a cyclonic pre-separator or filter-cleaning mechanism. − When used outdoors. − When used indoors or in an enclosed area.
Advance to the next slide.

## Slide 211: Module 4: Specific control Methods - Training and group activities (xi):
Handheld grinders for mortar removal (i.e., tuckpointing). Tuckpointing involves removing deteriorating mortar from between bricks using a handheld grinder and replacing it with fresh mortar.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
Handheld grinders for mortar removal (i.e., tuckpointing). Tuckpointing involves removing deteriorating mortar from between bricks using a handheld grinder and replacing it with fresh mortar.
Advance to the next slide.

## Slide 212: Module 4: Specific control Methods - Training and group activities (xi):
The handheld grinders must be equipped with a commercially available shroud and dust collection system and operated and maintained in accordance with manufacturer’s instructions to minimize dust emissions.
The dust collection system must provide at least 25 cfm of air flow per inch of wheel diameter and have a filter that has a 99 percent or greater efficiency and either a cyclonic pre-separator or a filter-cleaning mechanism. Cyclonic pre-separators and filter-cleaning mechanisms improve the suction of dust collection systems by preventing debris from building up on the filter.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
The handheld grinders must be equipped with a commercially available shroud and dust collection system and operated and maintained in accordance with manufacturer’s instructions to minimize dust emissions. The dust collection system must provide at least 25 cfm of air flow per inch of wheel diameter and have a filter that has a 99 percent or greater efficiency and either a cyclonic pre-separator or a filter-cleaning mechanism. Cyclonic pre-separators and filter-cleaning mechanisms improve the suction of dust collection systems by preventing debris from building up on the filter.
Advance to the next slide.

## Slide 213: Module 4: Specific control Methods - Training and group activities:
Full and proper implementation of dust collection systems on handheld grinders requires the employer to ensure that:
The shroud is intact, encloses most of the grinding blade, and is installed in accordance with the manufacturer’s instructions;
The hose connecting the tool to the vacuum is intact and without kinks or tight bends;
The filter(s) on the vacuum are cleaned or changed in accordance with the manufacturer’s instructions;
The dust collection bags are emptied to avoid overfilling;
The blade is kept flush against the surface whenever possible; and
The tool is operated against the direction of blade rotation, whenever practical.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
Full and proper implementation of dust collection systems on handheld grinders requires the employer to ensure that:
The shroud is intact, encloses most of the grinding blade, and is installed in accordance with the manufacturer’s instructions;
The hose connecting the tool to the vacuum is intact and without kinks or tight bends;
The filter(s) on the vacuum are cleaned or changed in accordance with the manufacturer’s instructions;
The dust collection bags are emptied to avoid overfilling;
The blade is kept flush against the surface whenever possible; and
The tool is operated against the direction of blade rotation, whenever practical.
Advance to the next slide.

## Slide 214: Module 4: Specific control Methods - Training and group activities:
When using handheld grinders for mortar removal indoors or in enclosed areas (areas where airborne dust can buildup, such as a structure with a roof and three walls), employers must provide additional exhaust if needed to minimize the accumulation of visible airborne dust.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
When using handheld grinders for mortar removal indoors or in enclosed areas (areas where airborne dust can buildup, such as a structure with a roof and three walls), employers must provide additional exhaust if needed to minimize the accumulation of visible airborne dust. See the section on Indoors or Enclosed Areas for more information on how to determine when those work situations apply.
Advance to the next slide.

## Slide 215: Module 4: Specific control Methods - Training and group activities:
Respiratory protection with a minimum APF of 10 is required for work with handheld grinders for mortar removal lasting four hours or less in a shift. Respiratory protection with a minimum APF of 25 is required for work lasting more than four hours per shift.
APF 10 APF 25
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
Respiratory protection with a minimum APF of 10 is required for work with handheld grinders for mortar removal lasting four hours or less in a shift. Respiratory protection with a minimum APF of 25 is required for work lasting more than four hours per shift.
Advance to the next slide.

## Slide 216: Module 4: Specific control Methods - Training and group activities (xii):
Handheld grinders may also be used for tasks other than mortar removal, such as to remove thin layers of concrete and surface coatings. Two control options may be used:
(1) A grinder equipped with an integrated water delivery system (commercially developed specifically for the type of tool in use) that continuously feeds water to the grinding surface operated for outdoor work only; and
(2) a dust collector equipped with a commercially available shroud and dust collection system with the same features as the dust collection system used for mortar removal for outdoor and indoor work.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
Handheld grinders may also be used for tasks other than mortar removal, such as to remove thin layers of concrete and surface coatings. Two control options may be used:
(1) A grinder equipped with an integrated water delivery system (commercially developed specifically for the type of tool in use) that continuously feeds water to the grinding surface operated for outdoor work only; and
(2) a dust collector equipped with a commercially available shroud and dust collection system with the same features as the dust collection system used for mortar removal for outdoor and indoor work.
Advance to the next slide.

## Slide 217: Module 4: Specific control Methods - Training and group activities:
The dust collector must be rated to provide 25 cfm or greater air flow per inch of wheel diameter, have a filter with a 99 percent or greater efficiency, and a cyclonic pre-separator or filter-cleaning mechanism. Cyclonic pre-separators and filter-cleaning mechanisms improve the suction of dust collection systems by preventing debris from building up on the filter.
The grinder and both controls must be operated and maintained in accordance with manufacturer’s instructions to minimize dust emissions.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
The dust collector must be rated to provide 25 cfm or greater air flow per inch of wheel diameter, have a filter with a 99 percent or greater efficiency, and a cyclonic pre-separator or filter-cleaning mechanism. Cyclonic pre-separators and filter-cleaning mechanisms improve the suction of dust collection systems by preventing debris from building up on the filter. The grinder and both controls must be operated and maintained in accordance with manufacturer’s instructions to minimize dust emissions.
Advance to the next slide.

## Slide 218: Module 4: Specific control Methods - Training and group activities:
The integrated water delivery system can be a free-flowing water system designed for blade cooling as well as manufacturers’ systems designed for dust suppression alone. This option applies only when grinders are used outdoors.
Full and proper implementation of water controls on grinders requires the employer to ensure that:
An adequate supply of water for dust suppression is used;
The spray nozzles are working properly and produce a pattern that applies water at the point of dust generation;
The spray nozzles are not clogged or damaged; and
All hoses and connections are intact.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
The integrated water delivery system can be a free-flowing water system designed for blade cooling as well as manufacturers’ systems designed for dust suppression alone. This option applies only when grinders are used outdoors.
Full and proper implementation of water controls on grinders requires the employer to ensure that:
An adequate supply of water for dust suppression is used;
The spray nozzles are working properly and produce a pattern that applies water at the point of dust generation;
The spray nozzles are not clogged or damaged; and
All hoses and connections are intact.
Advance to the next slide.

## Slide 219: Module 4: Specific control Methods - Training and group activities (xii):
Handheld grinders equipped with dust collection systems may be used outdoors or indoors. Full and proper implementation of dust collection systems on handheld grinders requires the employer to ensure that:
The shroud is intact and installed in accordance with the manufacturer’s instructions;
The hose connecting the tool to the vacuum is intact and without kinks or tight bends;
The filter(s) on the vacuum are cleaned or changed in accordance with the manufacturer’s instructions; and
The dust collection bags are emptied to avoid overfilling.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
Handheld grinders equipped with dust collection systems may be used outdoors or indoors. Full and proper implementation of dust collection systems on handheld grinders requires the employer to ensure that:
The shroud is intact and installed in accordance with the manufacturer’s instructions;
The hose connecting the tool to the vacuum is intact and without kinks or tight bends;
The filter(s) on the vacuum are cleaned or changed in accordance with the manufacturer’s instructions; and
The dust collection bags are emptied to avoid overfilling.
Advance to the next slide.

## Slide 220: Module 4: Specific control Methods - Training and group activities:
Respiratory protection is not required when water-based dust suppression systems are used regardless of task duration. When dust collection systems are used, respiratory protection with a minimum APF of 10 is required only when engaged in a task indoors or in an enclosed location for more than four hours per shift.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
Respiratory protection is not required when water-based dust suppression systems are used regardless of task duration. When dust collection systems are used, respiratory protection with a minimum APF of 10 is required only when engaged in a task indoors or in an enclosed location for more than four hours per shift.
Advance to the next slide.

## Slide 221: Module 4: Specific control Methods - Training and group activities:
When using handheld grinders indoors or in enclosed areas (areas where airborne dust can buildup, such as a structure with a roof and three walls), employers must provide additional exhaust as needed to minimize the accumulation of visible airborne dust.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
When using handheld grinders indoors or in enclosed areas (areas where airborne dust can buildup, such as a structure with a roof and three walls), employers must provide additional exhaust as needed to minimize the accumulation of visible airborne dust. See the section on Indoors or Enclosed Areas for more information.
Advance to the next slide.

## Slide 222: Module 4: Specific control Methods - Training and group activities:
Notes: Instructor will discuss Table 1 and focus on the control methods:
(xiii) Walk-behind milling machines and floor grinders
Use machine equipped with integrated water delivery system that continuously feeds water to the cutting surface. Operate and maintain tool in accordance with manufacturer's instructions to minimize dust emissions. OR use machine equipped with dust collection system recommended by the manufacturer.
Operate and maintain tool in accordance with manufacturer's instructions to minimize dust emissions. Dust collector must provide the air flow
recommended by the manufacturer, or greater, and have a filter with 99% or greater efficiency and a filter-cleaning mechanism.
When used indoors or in an enclosed area, use a HEPA-filtered vacuum to remove loose dust in between passes.
Advance to the next slide.

## Slide 223: Module 4: Specific control Methods - Training and group activities (xiii):
Two control options may be used when using walk-behind milling machines and floor grinders. Regardless of control option used, the tool must also be operated and maintained in accordance with manufacturer’s instructions for minimizing dust emissions.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
Two control options may be used when using walk-behind milling machines and floor grinders. Regardless of control option used, the tool must also be operated and maintained in accordance with manufacturer’s instructions for minimizing dust emissions.
Advance to the next slide.

## Slide 224: Module 4: Specific control Methods - Training and group activities:
Option one is to use an integrated water delivery system (commercially developed specifically for the type of tool in use) that continuously feeds water to the cutting surface. Table 1 does not specify a minimum flow rate; however, water must be applied at flow rates specified by the manufacturer.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
Option one is to use an integrated water delivery system (commercially developed specifically for the type of tool in use) that continuously feeds water to the cutting surface. Table 1 does not specify a minimum flow rate; however, water must be applied at flow rates specified by the manufacturer.
Advance to the next slide.

## Slide 225: Module 4: Specific control Methods - Training and group activities:
Full and proper implementation of water controls on walk-behind milling machines and floor grinders requires the employer to ensure that:
An adequate supply of water for dust suppression is used; The spray nozzles are working properly and produce a pattern that applies water at the point of dust generation;
The spray nozzles are not clogged or damaged; and
All hoses and connections are intact.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
Full and proper implementation of water controls on walk-behind milling machines and floor grinders requires the employer to ensure that:
An adequate supply of water for dust suppression is used; The spray nozzles are working properly and produce a pattern that applies water at the point of dust generation;
The spray nozzles are not clogged or damaged; and
All hoses and connections are intact.
Advance to the next slide.

## Slide 226: Module 4: Specific control Methods - Training and group activities:
Option two is to use a dust collection system recommended by the manufacturer of the milling machine or floor grinder and a filter with 99 percent or greater efficiency and a filter-cleaning mechanism. The dust collection system used must be capable of maintaining the air flow recommended by the manufacturer.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
Option two is to use a dust collection system recommended by the manufacturer of the milling machine or floor grinder and a filter with 99 percent or greater efficiency and a filter-cleaning mechanism. The dust collection system used must be capable of maintaining the air flow recommended by the manufacturer.
Advance to the next slide.

## Slide 227: Module 4: Specific control Methods - Training and group activities:
Full and proper implementation of dust collection systems on walk-behind milling machines and floor grinders requires the employer to ensure that:
The hose connecting the tool to the vacuum is intact and without kinks or tight bends;
The filter(s) on the vacuum are cleaned or changed in accordance with the manufacturer’s instructions to prevent clogging; and
The dust collection bags are emptied to avoid overfilling.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
Full and proper implementation of dust collection systems on walk-behind milling machines and floor grinders requires the employer to ensure that:
The hose connecting the tool to the vacuum is intact and without kinks or tight bends;
The filter(s) on the vacuum are cleaned or changed in accordance with the manufacturer’s instructions to prevent clogging; and
The dust collection bags are emptied to avoid overfilling.
Advance to the next slide.

## Slide 228: Module 4: Specific control Methods - Training and group activities:
When using a dust collector system indoors or in enclosed areas (areas where airborne dust can buildup, such as a structure with a roof and three walls), loose dust must be cleaned with a HEPA-filtered vacuum in between passes of the milling machine or floor grinder to prevent the loose dust from being re-suspended. Removing loose dust with a HEPA vacuum also maximizes vacuum suction by improving the seal between the machine and floor. For indoor and enclosed spaces, employers must provide additional ventilation as needed to minimize the accumulation of visible airborne dust.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
When using a dust collector system indoors or in enclosed areas (areas where airborne dust can buildup, such as a structure with a roof and three walls), loose dust must be cleaned with a HEPA-filtered vacuum in between passes of the milling machine or floor grinder to prevent the loose dust from being re-suspended. Removing loose dust with a HEPA vacuum also maximizes vacuum suction by improving the seal between the machine and floor. For indoor and enclosed spaces, employers must provide additional ventilation as needed to minimize the accumulation of visible airborne dust.
Advance to the next slide.

## Slide 229: Module 4: Specific control Methods - Training and group activities:
Respiratory protection is not required for work with walk-behind milling machines and floor grinders regardless of task duration.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
Respiratory protection is not required for work with walk-behind milling machines and floor grinders regardless of task duration.
Advance to the next slide.

## Slide 230: Module 4: Specific control Methods - Training and group activities:
(xiv) Small drivable milling machines (less than half-lane) | Use a machine equipped with supplemental water sprays designed to suppress dust. Water must be combined with a surfactant. Operate and maintain machine to minimize dust emissions | None | None
(xv) Large drivable milling machines (half-lane and larger) *pictures obtained from www. lhsfna.org | For cuts of any depth on asphalt only: Use machine equipped with exhaust ventilation on drum enclosure and supplemental water sprays designed to suppress dust. Operate and maintain machine to minimize dust emissions. For cuts of four inches in depth or less on any substrate: Use machine equipped with exhaust ventilation on drum enclosure and supplemental water sprays designed to suppress dust. Operate and maintain machine to minimize dust emissions; or Use a machine equipped with supplemental water spray designed to suppress dust. Water must be combined with a surfactant. Operate and maintain machine to minimize dust emissions. | None | None
Notes: Instructor will discuss Table 1 and focus on the control methods:
(xiv) Small drivable milling machines (less than half-lane)
Use a machine equipped with supplemental water sprays designed to suppress dust. Water must be combined with a surfactant. Operate and maintain machine to minimize dust emissions
(xv) Large drivable milling machines (half-lane and larger)
For cuts of any depth on asphalt only: Use machine equipped with exhaust ventilation on drum enclosure and supplemental water sprays designed to suppress dust. Operate and maintain machine to minimize dust emissions. For cuts of four inches in depth or less on any substrate: Use machine equipped with exhaust ventilation on drum enclosure and supplemental water sprays designed to suppress dust. Operate and maintain machine to minimize dust emissions. OR Use a machine equipped with supplemental water spray designed to suppress dust. Water must be combined with a surfactant. Operate and maintain machine to minimize dust emissions.
(xv) Large drivable milling machines (half-lane and larger)
For cuts of any depth on asphalt only: Use machine equipped with exhaust ventilation on drum enclosure and supplemental water sprays designed to suppress dust. Operate and maintain machine to minimize dust emissions. For cuts of four inches in depth or less on any substrate: Use machine equipped with exhaust ventilation on drum enclosure and supplemental water sprays designed to suppress dust. Operate and maintain machine to minimize dust emissions. OR Use a machine equipped with supplemental water spray designed to suppress dust. Water must be combined with a surfactant. Operate and maintain machine to minimize dust emissions.
Advance to the next slide.

## Slide 231: Module 4: Specific control Methods - Training and group activities (xiv):
Small drivable milling machines must be used with supplemental water sprays designed to suppress dust and must be operated and maintained to minimize dust emissions. The water used must be combined with a surfactant.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
Small drivable milling machines must be used with supplemental water sprays designed to suppress dust and must be operated and maintained to minimize dust emissions. The water used must be combined with a surfactant.
Advance to the next slide.

## Slide 232: Module 4: Specific control Methods - Training and group activities (xiv):
Full and proper implementation of water controls on small drivable milling machines requires the employer to ensure that:
An adequate supply of water for dust suppression is used;
The spray nozzles are working properly and produce a pattern that applies water at the point of dust generation;
The spray nozzles are not clogged or damaged; and
All hoses and connections are intact.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
Full and proper implementation of water controls on small drivable milling machines requires the employer to ensure that:
An adequate supply of water for dust suppression is used;
The spray nozzles are working properly and produce a pattern that applies water at the point of dust generation;
The spray nozzles are not clogged or damaged; and
All hoses and connections are intact.
Advance to the next slide.

## Slide 233: Module 4: Specific control Methods - Training and group activities (xiv):
When using small drivable milling machines indoors or in enclosed areas (areas where airborne dust can buildup, such as a structure with a roof and three walls), the employer must provide additional exhaust as needed to prevent the accumulation of visible airborne dust.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
When using small drivable milling machines indoors or in enclosed areas (areas where airborne dust can buildup, such as a structure with a roof and three walls), the employer must provide additional exhaust as needed to prevent the accumulation of visible airborne dust.
Advance to the next slide.

## Slide 234: Module 4: Specific control Methods - Training and group activities:
Respiratory protection is not required for work with small drivable milling machines (less than half-lane) regardless of task duration.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
Respiratory protection is not required for work with small drivable milling machines (less than half-lane) regardless of task duration.
Advance to the next slide.

## Slide 235: Module 4: Specific control Methods - Training and group activities (xv):
Employers whose employees operate large (one-half lane or wider) milling machines have two control options for cuts of four inches in depth or less on any substrate and one control option for cuts of any depth on asphalt. When using any of the control options, the machine must be operated and maintained to minimize dust emissions.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
Employers whose employees operate large (one-half lane or wider) milling machines have two control options for cuts of four inches in depth or less on any substrate and one control option for cuts of any depth on asphalt. When using any of the control options, the machine must be operated and maintained to minimize dust emissions.
Advance to the next slide.

## Slide 236: Module 4: Specific control Methods - Training and group activities:
The two control options for making cuts of four inches or less on any combination of roadway material (asphalt and concrete), are to:
  (1) use a machine equipped with exhaust ventilation on the drum enclosure and supplemental water sprays designed to suppress dust; or
  (2) use a machine equipped with a supplemental water spray, combined with a surfactant, designed to suppress dust.
When making cuts of any depth on roadway material containing asphalt only, the only control option is to use a machine equipped with exhaust ventilation on the drum enclosure and supplemental water sprays designed to suppress dust.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
The two control options for making cuts of four inches or less on any combination of roadway material (asphalt and concrete), are to:
  (1) use a machine equipped with exhaust ventilation on the drum enclosure and supplemental water sprays designed to suppress dust; or
  (2) use a machine equipped with a supplemental water spray, combined with a surfactant, designed to suppress dust.
When making cuts of any depth on roadway material containing asphalt only, the only control option is to use a machine equipped with exhaust ventilation on the drum enclosure and supplemental water sprays designed to suppress dust.
Advance to the next slide.

## Slide 237: Module 4: Specific control Methods - Training and group activities:
Respiratory protection is not required for work with large drivable milling machines (half-lane or larger) regardless of task duration.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
Respiratory protection is not required for work with large drivable milling machines (half-lane or larger) regardless of task duration.
Advance to the next slide.

## Slide 238: Module 4: Specific control Methods - Training and group activities:
*picture obtained from www.lhsfna.org
Notes: Instructor will discuss Table 1 and focus on the control methods:
(xvi) Crushing machines
Use equipment designed to deliver water spray or mist for dust suppression at crusher and other points where dust is generated (e.g., hoppers, conveyers, sieves/sizing or vibrating components, and discharge points). Operate and maintain machine in accordance with manufacturer’s instructions to minimize dust emissions. Use a ventilated booth that provides fresh, climate-controlled air to the operator, or a remote control station.
Advance to the next slide.

## Slide 239: Module 4: Specific control Methods - Training and group activities (xvi):
Crushing machines, employers must provide workers with a remote control station or ventilated booth that provides fresh, climate-controlled air to the operator. Water sprays or mists must be used for dust suppression at the crusher and other points where dust is generated (e.g., at hoppers, conveyors, sieves/sizing or vibrating components, and discharge points). See the section on Enclosed Cabs for more information on how to make sure enclosures meet the requirements of the rule. Table 1 also requires that the machine be operated and maintained according to the manufactures instructions to minimize dust emissions.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
Crushing machines, employers must provide workers with a remote control station or ventilated booth that provides fresh, climate-controlled air to the operator. Water sprays or mists must be used for dust suppression at the crusher and other points where dust is generated (e.g., at hoppers, conveyors, sieves/sizing or vibrating components, and discharge points). See the section on Enclosed Cabs for more information on how to make sure enclosures meet the requirements of the rule. Table 1 also requires that the machine be operated and maintained according to the manufactures instructions to minimize dust emissions.
Advance to the next slide.

## Slide 240: Module 4: Specific control Methods - Training and group activities:
The water spray systems can be installed so that they can be activated by remote control. To prevent airborne dust from being generated, full and proper implementation of controls requires that:
Nozzles are located upstream of dust generation points and positioned to thoroughly wet the material;
The volume and size of droplets is adequate to sufficiently wet the material (optimal droplet size is between 10 and 150 μm); and
Spray nozzles are located far enough from the target area to provide complete water;
Coverage but not so far that the water is carried away by wind.
*These are some best practices not listed in the standards.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
The water spray systems can be installed so that they can be activated by remote control. To prevent airborne dust from being generated, full and proper implementation of controls requires that:
Nozzles are located upstream of dust generation points and positioned to thoroughly wet the material;
The volume and size of droplets is adequate to sufficiently wet the material (optimal droplet size is between 10 and 150 μm); and
Spray nozzles are located far enough from the target area to provide complete water
coverage but not so far that the water is carried away by wind.
Advance to the next slide.

## Slide 241: Module 4: Specific control Methods - Training and group activities:
Respiratory protection is not required for crusher operators regardless of task duration.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
Respiratory protection is not required for crusher operators regardless of task duration.
Advance to the next slide.

## Slide 242: Module 4: Specific control Methods - Training and group activities:
(xvii) Heavy equipment and utility vehicles used to abrade or fracture silica containing materials (e.g., hoe-ramming, rock ripping) or used during demolition activities involving silica-containing materials | Operate equipment from within an enclosed cab. When employees outside of the cab are engaged in the task, apply water and/or dust suppressants as necessary to minimize dust emissions. | None | None
*picture obtained from www.lhsfna.org

## Slide 243: Module 4: Specific control Methods - Training and group activities:
(xviii) Heavy equipment and utility vehicles for tasks such as grading and excavating but not including: demolishing, abrading, or fracturing silica containing materials | Apply water and/or dust suppressants as necessary to minimize dust emissions; OR When the equipment operator is the only employee engaged in the task, operate equipment from within an enclosed cab. | None | None
Notes: Instructor will discuss Table 1 and focus on the control methods:
(xvii) Heavy equipment and utility vehicles used to abrade or fracture silica containing materials (e.g., hoe-ramming, rock ripping) or used during demolition activities involving silica-containing materials Operate equipment from within an enclosed cab. When employees outside of the cab are engaged in the task, apply water and/or dust suppressants as necessary to minimize dust emissions.
(xviii) Heavy equipment and utility vehicles for tasks such as grading and excavating but not including: demolishing, abrading, or fracturing silica containing materials
Apply water and/or dust suppressants as necessary to minimize dust emissions. OR When the equipment operator is the only employee engaged in the task, operate equipment from within an enclosed cab.
Advance to the next slide.

## Slide 244: Module 4: Specific control Methods - Training and group activities (xvii) (xviii):
Heavy equipment and utility vehicles used to abrade or fracture silica-containing materials (e.g., hoe-ramming, rock ripping) or used during demolition activities involving silica-containing materials.
These include activities such as fracturing or abrading rock and soil; demolishing concrete or masonry structures; and loading, dumping, and removing demolition debris.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
Heavy equipment and utility vehicles used to abrade or fracture silica-containing materials (e.g., hoe-ramming, rock ripping) or used during demolition activities involving silica-containing materials.
These include activities such as fracturing or abrading rock and soil; demolishing concrete or masonry structures; and loading, dumping, and removing demolition debris.
Advance to the next slide.

## Slide 245: Module 4: Specific control Methods - Training and group activities (xvii) (xviii):
The operator must be in an enclosed cab. Modern heavy equipment already comes equipped with enclosed, filtered cabs that meet the requirements of Table 1.
See the section on Enclosed Cabs for more information on how to make sure that the cab meets the requirements of the rule. When other employees are engaged in the task, water, dust suppressants, or both must also be applied as necessary to minimize dust emissions.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
The operator must be in an enclosed cab. Modern heavy equipment already comes equipped with enclosed, filtered cabs that meet the requirements of Table 1.
See the section on Enclosed Cabs for more information on how to make sure that the cab meets the requirements of the rule. When other employees are engaged in the task, water, dust suppressants, or both must also be applied as necessary to minimize dust emissions.
Advance to the next slide.

## Slide 246: Module 4: Specific control Methods - Training and group activities:
Respiratory protection is not required for heavy equipment operators and laborers who assist heavy equipment operators during demolition activities involving silica containing materials or activities where silica containing materials are abraded or fractured, regardless of the duration of the task.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
Respiratory protection is not required for heavy equipment operators and laborers who assist heavy equipment operators during demolition activities involving silica containing materials or activities where silica containing materials are abraded or fractured, regardless of the duration of the task.
Advance to the next slide.

## Slide 247: Module 4: Specific control Methods - Training and group activities:
When the operator exits the enclosed cab and is no longer actively preforming the task, the operator is considered to have stopped the task.
However, if other abrading, fracturing, or demolition work is performed by other heavy equipment and utility vehicles in the area while an operator is outside the cab, that operator is considered to be an employee “engaged in the task” and must be protected by the application of water and/or dust suppressants.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
NOTE: When the operator exits the enclosed cab and is no longer actively preforming the task, the operator is considered to have stopped the task. However, if other abrading, fracturing, or demolition work is performed by other heavy equipment and utility vehicles in the area while an operator is outside the cab, that operator is considered to be an employee “engaged in the task” and must be protected by the application of water and/or dust suppressants.
Advance to the next slide.

## Slide 248: Module 4: Specific control Methods - Training and group activities (xviii):
Heavy equipment and utility vehicles used for tasks such as grading and excavating do not involve demolition or the fracturing or abrading of silica. Tasks include earthmoving, grading, and excavating; other activities such as moving, loading, and dumping soil and rock; and dumping and grading of ballast in the railroad industry, which is generally subject to OSHA’s Construction standards.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
Heavy equipment and utility vehicles used for tasks such as grading and excavating do not involve demolition or the fracturing or abrading of silica. Tasks include earthmoving, grading, and excavating; other activities such as moving, loading, and dumping soil and rock; and dumping and grading of ballast in the railroad industry, which is generally subject to OSHA’s Construction standards.
Advance to the next slide.

## Slide 249: Module 4: Specific control Methods - Training and group activities:
Employers have two control options when the operator is the only employee engaged in the task and one option when employees other than the operator are engaged in the task.
The first option requires the equipment operator to operate the equipment within an enclosed cab when the operator is the only employee in the area. Most heavy equipment already comes equipped with enclosed, filtered cabs that meet the requirements of Table 1.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
Employers have two control options when the operator is the only employee engaged in the task and one option when employees other than the operator are engaged in the task.
The first option requires the equipment operator to operate the equipment within an enclosed cab when the operator is the only employee in the area. Most heavy equipment already comes equipped with enclosed, filtered cabs that meet the requirements of Table 1. See the section on Enclosed Cabs for more information on how to make sure that the cab meets the requirements of the rule.
Advance to the next slide.

## Slide 250: Module 4: Specific control Methods - Training and group activities:
The second option requires the application of water and/or dust suppressants as necessary to minimize dust emissions. Water must be applied at rates sufficient to minimize release of visible dust. The following scenarios are examples of when the employer must use water and/or dust suppressants as necessary to minimize dust emissions:
  (1) equipment for grading and excavating is not equipped with enclosed, pressurized cabs or
  (2) employees other than the operator are engaged in the task. If water or dust suppressants are applied as necessary to minimize visible dust, the employer need not provide an enclosed, filtered cab for the operator.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
The second option requires the application of water and/or dust suppressants as necessary to minimize dust emissions. Water must be applied at rates sufficient to minimize release of visible dust. The following scenarios are examples of when the employer must use water and/or dust suppressants as necessary to minimize dust emissions:
  (1) equipment for grading and excavating is not equipped with enclosed, pressurized cabs or
  (2) employees other than the operator are engaged in the task. If water or dust suppressants are applied as necessary to minimize visible dust, the employer need not provide an enclosed, filtered cab for the operator.
Advance to the next slide.

## Slide 251: Module 4: Specific control Methods - Training and group activities:
Respiratory protection is not required for work with heavy equipment when it is operated from within an enclosed cab, or when water or other dust suppressants are used, regardless of task duration.
Notes: Instructor will discuss Table 1 and focus on the control methods for this section’s task/ use of equipment:
Respiratory protection is not required for work with heavy equipment when it is operated from within an enclosed cab, or when water or other dust suppressants are used, regardless of task duration.
Advance to the next slide.

## Slide 252: Module 4: Specific control Methods - Training and group activities:
Group Activity
Notes: Instructor will lead the group activity on control methods.
Advance to the next slide.

## Slide 253: Module 4: Specific control Methods - Training and group activities:
The students will practice picking the correct control methods for situation.
Notes: Instructor will handout the exercise sheet and students will work in groups to make the recommendations to protect the employees. Once completed the instructor will have the students review these situations with the rest of the class. Students are to use Table 1 information to make the determinations.
Advance to the next slide.

## Slide 254: Module 4: Specific control Methods - Training and group activities:
Summary:
  Identify general differences between the old and new silica standard.
  Identify general the areas of the new standard that employees should be concerned with.
Notes: Instructor will review the difference between the old and new silica standard and discuss the general areas of the new standards.
Summary:
  Identify general differences between the old and new silica standard.
  Identify general the areas of the new standard that employees should be concerned with.

## Slide 255: Module 4 : Specific control Methods Training and group activities:
  Any Questions?
Notes: Answer student questions, if any.
Students are to take the final test and the instructor shall grade and go over the results.

## Slide 256: USF OTI Education Center Respirable Silica in the Construction Industry
Module 5
Notes: This module discusses specific methods to control and reduce exposure to silica dust at worksites. Using work practices and specific tools following manufacture requirements will reduce the amount of silica exposure. Table 1 address when to wear respirators to protect employees based on the amount of possible exposure. Making the correct selection of respiratory protection is critical for the employees working in high hazard areas. The participants will have the chance to use scenarios that will let them practice the skill of determining the proper method to reduce the exposure to the workers.

## Slide 257: Module 5
This material was produced under grant number SH-29661-SH6 from OSHA. It does not necessarily reflect the views or policies of the U.S. Department of Labor, nor does mention of trade names, commercial products, or organizations imply endorsement by the U.S. Government.
Respirator selection, use, and care and Lab - Part I

## Slide 258: Module 5: Respirator selection, use, and care and Lab - Part I:
Terminal Objective
  Trainees will be able to describe the requirements for Table 1 tasks.
Notes: The instructor shall go over terminal objectives. The trainee shall be evident describe the requirements for table 1 task.

## Slide 259: Module 5: Respirator selection, use, and care and Lab - Part I:
Enabling Objectives:
  Identify the significance of including the specified exposure control methods.
  Identify tasks likely to expose workers to silica exposure.
  Identify ways to avoid and abate hazards associated with silica exposure.
  Identify requirements for engineering controls
  Identify appropriate work practice controls.
  Identify requirements for respiratory protection.
Notes: The instructor shall go through the enabling objectives. This includes identifying the significance of' specified exposure control methods. Identifying task likely to expose workers to silica. Identifying ways to avoid and abate hazards associated with silica exposure. Identifying requirements for engineering controls. Identifying appropriate work practice controls. And identifying requirements for respiratory protection, which will be discussed during this section.

## Slide 260: Module 5: Respirator selection, use, and care and Lab - Part I
Table 1:
Is based on the most common silica dust generating task found on a construction site.
Notes: Respirators provide protection from respiratory hazards only when they are properly selected and used in compliance with the Respiratory Protection standard (29 CFR 1910.134 and 29 CFR 1926.103).
The instructor should survey participants to identify the most common tasks that they perform that might include silica. Summarize how many students do tasks that are listed on table one that we've discussed today.

## Slide 261: Module 5: Methods of control
Table 1:
Specified exposure control methods;
Alternative exposure control methods.
Notes: Have the students pull out table 1. While they have reviewed this during other sections they will need it for the exercises and discussion.

## Slide 262: Module 5: Methods of control
Employers who choose the specified exposure controls option must fully and properly implement protections for the tasks or equipment listed in Table 1 of the standard.
Notes: For those employers who choose to use table 1, they will choose the specified exposure control method and fully implement protection for the task and the equipment used.

## Slide 263: Module 5: Ways to reduce silica exposure
Table 1 tasks requirements:
Operate and maintain tools according to manufacturers’ instructions for minimizing dust emissions.
Notes: Table 1 requires that you must operate and maintain all tools according to manufacturer requirements for minimizing dust omission.

## Slide 264: Module 5: Manufactures instructions for :
Manufacturer’s instructions for minimizing dust can include:
Water flow rates,
Vacuum equipment air flow rate and capacity,
Rotation of the blade (speed, direction),
Maintaining and changing blades, and
Frequency for changing water.
Notes: The manufacturer's instruction will discuss proper water flow rates, vacuuming equipment flow, rotation and blade speed, and proper maintenance of changing water for closed systems.

## Slide 265: Module 5: Methods of control
Several Table 1 items have requirements for the use of respiratory protection with a minimum “assigned protection factor” (APF).
Notes: Several items from table 1 have requirement for the use of respiratory protection with a minimum assigned protection factor. The employer needs to ensure that their meeting these protection factors based on the task and the exposure.

## Slide 266: Module 5: Respiratory requirements
Respirator requirements in Table 1 are divided by task duration:
Less than or equal to four hours/shift,
Greater than four hours/shift.
Notes: The respiratory requirements are divided by task and duration. It's depending on whether the task lasts more than 4 hours or less than 4 hours. Looking at table 1 you'll see that there are 2 columns to represent this.

## Slide 267: Module 5: Alternate option for reducing exposure to silica
For tasks not listed or where the employer does not fully and properly implement the engineering controls, work practices, and respiratory protection described in Table 1, the employer shall assess the exposure of each employee who is or may reasonably be expected to be exposed to respirable crystalline silica at or above the action level.
Notes: Whenever a task is not listed or when the employer is unable to fully or properly implement the engineering controls or work practices they must assess the exposure of each employee who may reasonably be expected to be exposed to respiratory silica at or above the action level.

## Slide 268: Module 5: Work practice controls
Proper work practices are also important in reducing potential silica exposures.
When possible, equipment should be positioned so that operators and others can work upwind from dust emissions.
Notes: It's important in reducing potential exposures to use proper work practices. Other employees in the area should not be in the dust omissions from the tools or equipment being used. Consideration needs to be taken for others in the area to determine if they need respiratory protection to prevent exposure.

## Slide 269: Module 5: Work practice controls
Put dust control equipment on a regular maintenance schedule.
Train employees to watch for sources of dust and to make necessary adjustments or repairs to reduce emissions – and their own exposure
Notes: Regular maintenance needs to be scheduled on dust control equipment to ensure that it's working correctly. Employees need to be trained for watch resources of dust and make necessary adjustments or repairs to ensure a mission is below the exposure level. They also need to be trained to stay out of areas where exposure may occur.

## Slide 270: Module 5: Work practice controls
Continued:
Common work practices can help employees limit their exposure to silica.
Examples include:
Clean up spills and waste before dust can spread.
Notes: Many common work practices can help employees limit their exposure to silica, including proper cleaning up of spills and waste before dust can spread.

## Slide 271: Module 5: Work practice controls
Continued:
Wear a rubber apron to keep wet dust off clothing. When it dries, the dust can become airborne.
Whenever possible, work upwind of any dust sources. This can be as simple as working from the other side of the pile when shoveling debris.
Notes: Employees need to wear things like rubber aprons to keep wet dust off their clothing, when it dries the desk and become airborne. This creates an exposure. Employees need to work upwind of any dust source.

## Slide 272: Module 5: Work practice controls
Continued:
Keep roadways damp at sites where the surface includes high silica aggregate or crushed concrete.
Wet down silica-containing debris and rock spoil piles prior to removal or disturbance.
Notes: In areas where there's vehicle or traffic keep the roadways damp, and ensure areas where high silica aggregate or crushed concrete is used are kept wet to avoid silica dust as the vehicles drive over them. Silica dust can be formed from the crushing of those substances used in roadways on worksites. When possible wet down silica containing debris and rock spoil piles prior to removal or disturbance.

## Slide 273: Module 5: Work practice controls
Continued:
Encourage employees to watch for dust sources containing silica and make adjustments or use dust control methods to reduce their silica exposure.
Notes: Employee should be encouraged to watch for dust sources and make necessary adjustments for dust control of silica when there is a hazard.

## Slide 274: Module 5: Work practice controls
Continued:
When Silica dust cannot be controlled through wet methods or other engineering controls, it may be necessary to use a respirator.
Notes: Whenever silica dust cannot be controlled through web methods or other engineering controls it may become necessary to use a respirator to protect the employees.

## Slide 275: Module 5: Selection of Respirators
The competent person must select a respirator certified by the National Institute for Occupational Safety and Health (NIOSH) which must be used in compliance with the conditions of its certification.
Notes: The company's competent person must select a respirator certified by NIOSH. The respirator will be marked with an IRS protection level such as N95, P95 N100 or P100.

## Slide 276: Module 5: Selection of Respirators
The competent person must identify and evaluate the respiratory hazards in the workplace, including a reasonable estimate of employee exposures, and identification of the contaminant’s chemical state and physical form.
Notes: The competent person will identify and evaluate all the respiratory hazards in the workplace including reasonable estimate of the exposure possible from the silica products.

## Slide 277: Module 5: Selection of Respirators
For protection against particulates, the employer shall provide:
an atmosphere-supplying respirator; or
an air-purifying respirator equipped with high efficiency particulate air (HEPA) filters certified by NIOSH.
Notes: For protection against particulates, the employer shall provide:
an atmosphere-supplying respirator; or
an air-purifying respirator equipped with high efficiency particulate air (HEPA) filters certified by NIOSH under 30 CFR Part 11 or with filters certified for particulates under 42 CFR Part 84
or an air-purifying respirator equipped with any filter certified for particulates by NIOSH for contaminants consisting primarily of particles with mass median aerodynamic diameters of at least 2 micrometers.

## Slide 278: Module 5: Use of Respirators
Any Tight-fitting respirators shall not be worn by employees who have facial hair or any condition that interferes with the face-to-facepiece seal or valve function.
Notes: Respirators that are tightfitting require that employees not have any facial hair that interferes with the face to face piece or valve function.

## Slide 279: Module 5: Use of Respirators
Employees shall perform a user seal check each time they put on a tight-fitting respirator using the proper procedures.
Notes: The individual who uses a tight-fitting respirator is to perform a user seal check to ensure that an adequate seal is achieved each time the respirator is put on. Either the positive and negative pressure checks listed in this appendix, or the respirator manufacturer's recommended user seal check method shall be used. User seal checks are not substitutes for qualitative or quantitative fit tests.
I. Facepiece Positive and/or Negative Pressure Checks
A. Positive pressure check. Close off the exhalation valve and exhale gently into the facepiece. The face fit is considered satisfactory if a slight positive pressure can be built up inside the facepiece without any evidence of outward leakage of air at the seal. For most respirators this method of leak testing requires the wearer to first remove the exhalation valve cover before closing off the exhalation valve and then carefully replacing it after the test.
B. Negative pressure check. Close off the inlet opening of the canister or cartridge(s) by covering with the palm of the hand(s) or by replacing the filter seal(s), inhale gently so that the facepiece collapses slightly, and hold the breath for ten seconds. The design of the inlet opening of some cartridges cannot be effectively covered with the palm of the hand. The test can be performed by covering the inlet opening of the cartridge with a thin latex or nitrile glove. If the facepiece remains in its slightly collapsed condition and no inward leakage of air is detected, the tightness of the respirator is considered satisfactory.
II. Manufacturer's Recommended User Seal Check Procedures
The respirator manufacturer's recommended procedures for performing a user seal check may be used instead of the positive and/or negative pressure check procedures provided that the employer demonstrates that the manufacturer's procedures are equally effective.

## Slide 280: Module 5: Use of Respirators
All employees using a negative or positive pressure tight-fitting face piece respirator must pass an appropriate qualitative fit test (QLFT) or quantitative fit test (QNFT).
Notes: All employees using a negative or positive pressure tight-fitting facepiece respirator must pass an appropriate qualitative fit test (QLFT) or quantitative fit test (QNFT).

## Slide 281: Module 5: Use of Respirators
Respirator selection requires the employer to evaluate respiratory hazard(s) in the workplace, identify relevant workplace and user factors, and base respirator selection on the hazard.
Notes: To select the correct type of respirator a hazard analysis needs to be completed to identify the hazards and corresponding protective measure. For silica there is a requirement that the competent person conduct this hazard assessment.

## Slide 282: Module 5: Exposure
What are some common tasks on a jobsite that produce silica?
Notes: The instructor shall asked the class what are some common task on a jobsite that produced silica dust that can become respirable.
The students should be able to answer some of the following: cutting, grinding, chipping, crushing, and driving over silica -containing materials. Some of the materials that contain silica are: concrete, brick, stone, granite, and mortar.

## Slide 283: Module 5: Exposure
Employees who are engaged in an activity
Employees who are not engaged in an activity
Notes: Discuss the OSHA hierarchy of controls. Elimination, substitution, engineering, administration controls, and PPE.
Ask the students to identify those whom are or are not engaged in a silica producing act but may be exposed to silica on a job site.

## Slide 284: Module 5: Scenario
Exercise
Notes: Employees will use the scenario sheet to answer 3 basic questions about each scenario give them 15 minutes to complete these tasks. They may work in groups for larger classes or individuals for smaller classes. Once the groups have completed these exercises we will go over them as a class with each group having a representative read their scenario and selection of correct

## Slide 285: Module 5: Scenario 1
Questions to ask before starting:
What engineering controls must be used?
What work practices can be in place to reduce exposure?
What respiratory protection will need to be used?
Notes: Using table 1, evaluate the scenario.
him asking the following questions:
what engineering controls must be used?
Proper engineering control would be to have the boards cut outside, and use a vacuum or dust collection system attached to the saw.
Proper work practices would include: operating and maintaining the tool in accordance with the manufacturer's instruction to minimize the dust omissions Ensure that the dust collector provides adequate air flow required by the tool manufacturer or have a filter with 99% or greater efficiency.
If this activity is done outside, there would be no requirement for respiratory protection. But if done inside, either respiratory protection would be required by all employees, or the competent person would be required to evaluate the level of exposure through testing and take adequate precautions.

## Slide 286
Module 5: Scenario 1
Two employees are installing a brick wall along the road where there was a fence for eight hours.
Employee 1: is cutting the bricks to the right size for proper placement using a masonry stationary saw.
Employee 2: is placing the bricks on the wall less than 10 feet away.
Notes: Discuss the risk that a user will experience an adverse health outcome when relying on respiratory protection is a function of the toxicity or hazardous nature of the air contaminants present, the concentrations of the contaminants in the air, the duration of exposure, and the degree of isolation provided by the respirator. The hazard may not be visible and the adverse health outcome may be delayed.
In scenario 1, 2 employees are installing a brick wall along the road outside. Employee one is cutting the bricks using a stationary masonry saw. An employee to his place in the bricks on the wall less than 10 feet away.
Students will evaluate the scenario and answer the 3 basic questions on the next slide.

## Slide 287: Module 5: Scenario 2
There are 5 employees working in a room putting up fiber cement board for 3 hours.
As a part of this process the employees must cut the boards to fit.
One employee uses a hand-held power saw for cutting the cement board. (The diameter of the blade is less than 8 inches) all the other employees are putting the boards on the wall.
Notes: The instructor will read scenario 2: There are 5 employees working in a room putting up fiber cement board. As a part of this process the employees must cut the boards. One employees uses a hand-held power saw for cutting the cement board. (The diameter of the blade is less than 8 inches) all the other employees are putting the boards on the wall.
The instructor will change slides and ask the appropriate questions

## Slide 288: Module 5: Scenario 2
Engineering Controls?
Work Practices?
Respiratory Protection?
Notes: Using table 1 determine the proper engineering controls, work practices, or protective measures that need to be taken. Do these employees need respiratory protection?
The saw should be equipped with integrated water delivery system that continuously feeds water to the blade. Based on table 1: no respiratory protection would be needed in this case for the operator of the saw.
It is important to note, that the saw needs to be turned so that no exhaust goes towards the 2nd employee. Factors like wind also need to be taken into consideration in the location of the saw.

## Slide 289: Module 5: Scenario 3
Two employees are using the Dow drilling rig for concrete to take core samples out of a new foundation.
The employees are taking six samples around the new foundation. Over an 8 hour period they will take 6 samples. Each sample takes half an hour to complete.
Notes: The instructor will go over the scenario 3.
Two employees are using the Dow drilling rig for concrete to take core samples out of a new foundation. The employees are taking six samples around the new foundation. Over an 8 hour period they will take 6 samples. Each sample takes half an hour to complete.
The instructor will then ask the questions on the next slide.

## Slide 290: Module 5: Scenario 3
Questions to ask before starting
What engineering controls must be used?
What work practices can be in place to reduce exposure?
What respiratory protection will need to be used?
Notes: The instructor will ask questions that the employees would need to know before starting work.
What engineering controls Must be used?
The employee should use the shroud around the drill bit with a dust collection system. The dust collector must have a filter with a 99% or greater efficiency and have a filter cleaning mechanism.
A filtered vacuum should be used when cleaning the holes out.
What work practices can be in place to reduce exposure?
No other employees should be in the area during this process. The area should be blocked off to ensure no one else comes in the area.
What respiratory protection will need to be used?
A respirator with the AFP 10 would be required for this task.

## Slide 291: Module 5: Scenario 4
An employee is using a jackhammer to open a hole in a cement foundation within a building, the employee is using a continuous stream of water spray at the point of impact.
The employee is conducting this operation for a total of 5 hours in an 8 hour day.
Notes: The instructor will go over the scenario 4;
An employee is using a jackhammer to open a hole in a cement foundation within a building, the employee is using a continuous stream of water spray at the point of impact. The employee is conducting this operation for a total of 5 hours in an 8 hour day.
The instructor will review the questions on the next slide.

## Slide 292: Module 5: Scenario 4
Questions to ask before starting
What engineering controls Must be used?
What work practices can be in place to reduce exposure?
What respiratory protection will need to be used?
Notes: The instructor shall ask the students the following questions:
What engineering controls Must be used?
There are 2 options that a student can use to control silica dust in the situation. They can use a water delivery system that supplies a continuous stream of water at the point of impact or a dust collector that must provide an airflow recommended by the tool manufacture or greater and have a filtration system with 99% of efficiency and a filter cleaning mechanism.
What work practices can be in place to reduce exposure?
The employee, needs to block off the area to keep others out due to the exposure to silica dust.
What respiratory protection will need to be used?
For this scenario, because they are in an indoors location and using a water delivery system a respirator would be required with the minimum assigned factor of ATF 10.

## Slide 293: Module 5: Respirator selection, use, and care and Lab - Part I:
Summary:
1) Identify the significance of including the specified exposure control methods
2) Identify tasks likely to expose workers to silica exposure
3) Identify ways to avoid and abate hazards associated with silica exposure
4) Identify requirements for engineering controls
5) Identify appropriate work practice controls
6) Identify requirements for respiratory protection
Notes: In this part of the course, we have reviewed how to use protection methods including respirators. It's important to select the correct respirator for the task at hand. A competent person needs to make that selection for the employees using a hazard assessment for each situation.
The instructor shall go through the Summary.
This includes: identifying the significance of' specified exposure control methods. Identifying task likely to expose workers to silica. Identifying ways to avoid and abate hazards associated with silica exposure. Identifying requirements for engineering controls. Identifying appropriate work practice controls. And identifying requirements for respiratory protection, which will be discussed during this section.

## Slide 294: Module 5 : Respirator selection, use, and care and Lab-Part I:
  Any Questions?
Notes: Answer student questions, if any.
Students are to take the final test and the instructor shall grade and go over the results.

## Slide 295: USF OTI Education Center Respirable Silica in the Construction Industry
Module 6

## Slide 296: Module 6
This material was produced under grant number SH-29661-SH6 from OSHA. It does not necessarily reflect the views or policies of the U.S. Department of Labor, nor does mention of trade names, commercial products, or organizations imply endorsement by the U.S. Government.
Respirator selection, use, and care and Lab - Part II

## Slide 297: Module 6: Respirator selection, use, and care and Lab - Part II:
Terminal Objective
  Trainees will be able to demonstrate basic knowledge and use of proper respiratory protection equipment
Notes: The instructor will review the terminal objective with the students.
Trainees will be able to demonstrate basic knowledge and use of proper respiratory protection equipment

## Slide 298: Module 6: Respirator selection, use, and care and Lab - Part II:
Enabling Objectives:
  Identify basic types of PPE used to reduce health hazards associated with silica exposure
  Identify importance of respiratory protection
  Identify proper use of respiratory protection
  Identify when to perform and how to perform a user seal check
  Identify how to maintain and care for respiratory protection
  Identify when it is time to replace/change a respirator
Notes: The instructor shall review the enabling objectives:
  Identify basic types of PPE used to reduce health hazards associated with silica exposure
  Identify importance of respiratory protection
  Identify proper use of respiratory protection
  Identify when to perform and how to perform a user seal check
  Identify how to maintain and care for respiratory protection
  Identify when it is time to replace/change a respirator

## Slide 299: Module 6: Importance of respiratory protection
Respirators are devices that protect employees from inhaling harmful substances, including chemical, biological, and radiological agents. These substances can be in the form of airborne vapors, gases, dust, fogs, fumes, mists, smokes, or sprays
Notes: Review what respirators are used for, respirators or devices that protect employees from inhaling harmful substances. Substances such as chemicals, biologicals, and radiological agents. That can be found in the form of airborne vapors, gases, dust, fogs, fumes, mists, smokes, and sprays.
The instructor needs to emphasize that not all respirators will protect you against all things. The correct selection of the respirator is very important.

## Slide 300: Module 6: Importance of respiratory protection
Employers must supply employees with respirators when all preferred methods of protecting them from breathing contaminated air have been determined to be insufficient to reduce the contamination to nonhazardous levels.
Notes: Remind the students of the OSHA hierarchy of controls. Substitution, engineering and administration controls.
Employers are required to provide employees with the proper PPE at no cost. This includes respirators when they are required. Respirators should only be used when all preferred methods of protection have been determined to be an effective.

## Slide 301: Module 6: Importance of respiratory protection
Respirators provide protection from respiratory hazards only when they are properly selected and used properly
Notes: Discuss the importance of a complete and comprehensive written respiratory program. Explain that the respirator is only a physical object with no inherent ability to provide protection. The respirator in conjunction with requirements out lined in the Respiratory Protection standard (29CFR 1910.134) provide the protection

## Slide 302: Module 6: Importance of respiratory protection
When employees are exposed to harmful airborne hazards, respirators reduce the risk of harm from both acute and chronic toxic effects.
Notes: Discuss the risk that a user will experience an adverse health outcome when relying on respiratory protection is a function of the toxicity or hazardous nature of the air contaminants present, the concentrations of the contaminants in the air, the duration of exposure, and the degree of isolation provided by the respirator. The hazard may not be visible and the adverse health outcome may be delayed

## Slide 303: Module 6: Basic types of respirators
Basic types of PPE used to reduce health hazards associated with silica exposure are as follows:
Notes: Respirators provide protection from respiratory hazards only when they are properly selected and used in compliance with the Respiratory Protection standard (29 CFR 1910.134 and 29 CFR 1926.103).

## Slide 304: Module 6: Basic types of respirator
An air-purifying respirator (APR) is a respirator which removes contaminants from the air.
An atmosphere-supplying respirator, or Supplied-air respirator (SAR), is one which provides clean breathing air from an uncontaminated source.
Notes: The instructor will discuss air purifying respirators, which remove contaminants from the air by filtration or exposure to chemicals within the filter. As where an atmospheric supplying respirator otherwise known as a supplied air respirator provides an atmosphere for breathing from an uncontaminated source.

## Slide 305: Module 6: Basic types of respirator
Atmosphere-supplying respirators are used to provide breathing air from a source independent of the ambient atmosphere.
These respirators supply breathing air that are generally used in highly hazardous work environments.
.
Notes: The atmosphere supplying respirators provide breathing air from an independent source. These respirators supply breathing air that is generally used in highly hazardous working environments.

## Slide 306: Module 6: Basic types of respirator
The two types atmosphere supplying:
Self-contained breathing apparatus (SCBA) units, for which air is supplied from a tank (a cylinder of compressed air or oxygen).
Supplied-air respirators (SARs) (also known as airline respirators), which receive air from a connecting hose. The source of air is either a pressurized cylinder or an air compressor.
Notes: There are 2 types of atmospheric supplying systems, self-contained breathing apparatus and supplied air respirators. The self-contained breathing apparatus is a compressed air cylinder that you carry with you or are directly connected to with a pressure reducing device that allows you to breathe in the air. These can be placed in on demand, where you pull the air in with each breath, or constant flow, where there is a consistent flow of fresh air coming into your respirator from the source. The constant flow is more protective in even the most dangerous IDLH atmosphere. The SCBA systems are limited by the size of the tank. And the SAR system is limited by the length of the hose.

## Slide 307: Module 6: Basic types of respirator
An air-purifying respirator (APR) is a respirator which removes contaminants from the air.
Filtering face piece
Elastomeric face piece
Notes: Air purifying respirators are respirators which remove contaminants from the air. There are several different classes of air purifying respirators and filters based on the hazards that they are designed to overcome. Some of the filtering face pieces are loosefitting, held in place with straps and a nose piece that can be cramped. Other air purifying respirators are made out of a special rubber, and are tightfitting to the face. Both of the's are designed to be worn without facial hair to provide a tight Seal. The Elastometric facepiece requires a fitness test to ensure that it is tight on the face, each time it is put on. It also requires the correct filter systems for the hazard.
Elastomeric facepieces include facepieces made from Natural or Synthetic Rubber (e.g., EPDM); EPDM is an acronym for a specific type of rubber; that is, Ethylene propylene diene M-class rubber. Discuss the loose face piece and the tight fitting face piece.

## Slide 308: Module 6: Proper use of respiratory protection
When the use of respirators is required a respiratory protection program must be established and maintained.
Notes: When respirators are used during operations where exposures exceed OSHA’s permissible exposure limit (PEL), use of properly functioning respirators is essential to ensure that employees are not placed at significant risk of material impairment of health.

## Slide 309: Module 6: Proper use of respiratory protection
The respirator protection program must be written.
The program must have procedures specific to the work site
The program must be updated as necessary
Notes: Respiratory protection programs must be written and managed to ensure proper compliance and protection. The programs must have specific procedures for the worksite. The written program must be reviewed and updated as necessary, and at least annually.

## Slide 310: Module 6: Proper use of respiratory protection
All requirements of the respiratory protection program must be followed by employees who wear a respirator
Notes: Discuss the elements of a written respiratory protection program. • Selecting appropriate respirators for use in the workplace. • Training employees in the proper use of respirators (including putting them on and removing them), the limitations on their use, and their maintenance. • Providing medical evaluation of employees who must use respirators. • Fit testing tight-fitting respirators. • Using respirators properly in routine situations as well as in reasonably foreseeable emergencies. • Ensuring adequate air supply, quantity, and flow of breathing air for atmosphere-supplying respirators. • Establishing and adhering to schedules for cleaning, disinfecting, storing, inspecting, repairing, removing from service or discarding, and o • Regularly evaluating the effectiveness of the program

## Slide 311: Module 6: Proper use of respiratory protection
A program administrator must be designated to run the program and evaluate its effectiveness.
Notes: Discuss the qualifications of a program administrator. An individual is qualified to be a program administrator if he or she has appropriate training or experience in accord with the program’s level of complexity.

## Slide 312: Module 6: Proper use of respiratory protection
Specific procedures are required to:
  Prevent leaks in the respirator face piece seal.
  Prevent employees from removing respirators in hazardous environments.
Notes: Facepiece seals and valves are important in tight-fitting respirators. Tight-fitting respirators should be able to provide a complete seal to the face. If there is a leak in the seal of a tight-fitting respirator or valve, then the respirator cannot effectively reduce the wearer’s exposures to respiratory hazards. You must be sure that nothing interferes with the seal of the respirator to the employee’s face or with the valves. Conditions that can interfere with the seal or valve are specified in the standard and include: • Facial hair; • Facial scars; • Jewelry or headgear that projects under the facepiece seal; • Missing dentures; and • Corrective glasses or goggles or other protective equipment such as: - Face shields - Protective clothing - Helmets - Eyeglass insert or spectacle kits

## Slide 313: Module 6: Proper use of respiratory protection
How to don a respirator:
  Remove from container
  Inspect
  Loosen straps
  Place on face
  Pull straps over head
  Tighten straps
  Perform seal check
Notes: The instructor will demonstrate and instruct the students on the proper way to don and doff respirators that would be commonly found on a job site.
  Remove from container
  Inspect
  Loosen straps
  Place on face
  Pull straps over head
  Tighten straps
  Perform seal check

## Slide 314: Module 6: Proper use of respiratory protection
User seal check must be performed each time a worker put on a tight-fitting respirator.
Notes: The instructor will show the class how to do a proper check for a seal wearing a respirator. Students will not be allowed to wear respirators during this class due to the requirements for the medical evaluation. To conduct a user seal check, the employee must follow either the procedures for a user seal check that are contained in Appendix B-1 to § 1910.134: User Seal Check Procedures (Mandatory), or equally effective procedures that the respirator manufacturer recommends for conducting a user seal check

## Slide 315: Module 6: Proper use of respiratory protection
How to doff a respirator
  Loosen straps
  Pull straps over head
  Lean forward and pull mask directly away from face downward
Notes: The instructor shall instruct the students how to doff or remove the respirator.
  Loosen straps
  Pull straps over head
  Lean forward and pull mask directly away from face downward
Pulling the respirator off downward and away from the face prevents contaminates from getting on the wearer.

## Slide 316: Module 6: Proper use of respiratory protection
• Ensure that respirators operate effectively throughout the work shift.
• Protect employees entering IDLH atmospheres.
Notes: The written program shall address how a respirator will operate effectively throughout the work shift, including how to identify when a respirator is clogged with material so they can identify when you change the filtration or the respirator.
The written program shall address if employees working in an IDL H atmosphere are required to protect themselves with a respiratory protection system.

## Slide 317: Module 6: Proper use of respiratory protection
Continuing respirator effectiveness:
  Be aware of conditions in work areas where employees are using respirators.
  Leave the respirator use area to perform any activity that involves removing or adjusting a respirator face piece
Notes: Employees shall be trained to be aware of conditions in the work area where respirators are ineffective or become an effective. The employees are to leave the respirator use area to perform any activity that involves removing or adjusting a respirator facepiece. if there is any indication that a respirator may not be fully effective. If there is any indication that they are not functioning properly, you must repair or discard and replace respirators.

## Slide 318: Module 6: Maintenance and care for respiratory protection
Include respirator care and maintenance as a part of your respiratory protection program.
Notes: The instructor shall discuss the proper care and maintenance of respiratory protection equipment as a part of the respiratory protection program. Respiratory equipment should be cleaned, stored, and maintained per the manufacturer recommendations. Cleaning is normally accomplished through mild soap and water for rubber systems. Some other systems such as paper respirators are to be disposed of after use. Their use is limited to one time, or limited use per manufacturer requirements.
Discuss Respirator equipment must be regularly cleaned and disinfected according to specified procedures (See Appendix B-2 of the standard

## Slide 319: Module 6: Maintenance and care for respiratory protection
Provide for:
  cleaning and disinfection procedures
  proper storage
  regular inspections
  repair methods
Notes: The frequency of cleaning and disinfecting or sanitizing respirators will depend in part on whether your employees share the equipment or are issued respirators for their exclusive use. Worksite conditions also dictate cleaning frequency; e.g., working in a dirty environment will require that the respirator facepiece, in particular, be cleaned more frequently. The frequency must be noted in your written respiratory protection plan.
Rubber respirators are often cleaned with warm soapy water, and air dried in a clean environment.
Paper respirators need to be replaced with each use, and/or when they become clogged during a single use.
Only a qualified person may repair the respirator in less specific training has been conducted to ensure proper installation of parts.

## Slide 320: Module 6: Maintenance and care for respiratory protection
Store respirators in a manner that protects them from:
  Dust;
  Sunlight;
  Extreme temperatures;
  Excessive moisture;
  Contamination;
  Damaging chemicals, or other destructive conditions.
Notes: Respirators should be stored in a manner that:
  Protects them from contamination, dust, sunlight, extreme temperatures, excessive moisture, damaging chemicals, or other destructive conditions.

## Slide 321: Module 6: Maintenance and care for respiratory protection
All respirator inspections must include:
  A check of respirator function;
  Tightness of connections, and the;
  Condition of the various parts (including, but not limited to the face piece, head straps, valves, connecting tubes, and cartridges, canisters, or filters.)
Notes: The instructor shall go over the proper respirator inspection for different types of respirators.
The inspection of a half face Robert tightfitting respirator – requires inspection of the rubber surface around the half face unit. The inspection of the disc at the inlets. Which should be flexible without cracks and returned back to their original condition when released. Inspection of the filtration connections threads. The strap shall be inspected to ensure that they hold in place and have no damage. Filters will be inspected as designated in the respiratory protection plan to ensure that they are clean and free of materials, and are of the right& to protect the employees from the hazards.
Paper respirators – will be inspected to ensure that they are new, have no tears or rips, and that the straps are securely connected and have no damage. Inform the students to also ensure that there is no oil, moisture, or staining of the surface of the mask. If supplied with a nose cramp, ensure that it is securely connected.
A fullface respirator – must have all of the seal area inspected for damage, rips, tears, or changes such as hardening or cracking. The glass shall be inspected for cracks. The filter connection point must be inspected for threading, and damage. The filters must be inspected as designated by your written respiratory protection program and manufacturer requirements to ensure they are clean, and will provide you appropriate protection.

## Slide 322: Module 6: Maintenance and care for respiratory protection
If a respirator does not pass inspection, you must remove the respirator from service and discard, repair, or adjust it.
Tagging out-of-service respirators is a good means for ensuring that defective respirators are not inadvertently used.
Notes: The instructor will inform the students that if a respirator does not pass inspection it must be removed from service. And tagged as out of service so it is not inadvertently used.

## Slide 323: Module 6: Respirator Exercise
Respirator identification and inspection.
Notes: The instructor shall review the different methods of inspection For each type of respirator. Then the class will be given a chance to work in small groups to inspect and or assemble as they would in the field. The groups will be given approximately 5-10 minutes per respirator to conduct the inspection.
There should be several different types of respirators for the class to review. To include but not be limited to a half-face tight fitting respirator, a paper NIOSH approved filtering dust mask, an SCBA or SAR, and a Full face respirator.

## Slide 324: Module 6: Respirator selection, use, and care and Lab - Part II:
Summary:
  Identify basic types of PPE used to reduce health hazards associated with silica exposure
  Identify importance of respiratory protection
  Identify proper use of respiratory protection
  Identify when to perform and how to perform a user seal check
  Identify how to maintain and care for respiratory protection
  Identify when it is time to replace/change a respirator
Notes: The instructor shall review the summary questions and ensure that the students do not have any questions on the inspection, storage, cleaning of respiratory protection equipment.

## Slide 325: Module 6 : Respirator selection, use, and care and Lab-Part II:
  Any Questions?
Notes: Answer student questions, if any.
Students are to take the final test and the instructor shall grade and go over the results.

## Slide 326: USF OTI Education Center Respirable Silica in the Construction Industry
Module 7
Notes: This module discusses proper housekeeping techniques and hazards associated with improperly cleanup of respirable silica dust. This section covers the proper methods of using wet, or HEPA vacuuming methods to remove the hazardous dust. Participants will have the chance to practice some of the proper methods using a safe product and the correct techniques to reduce exposure.
Advance to the next slide.

## Slide 327: Module 7
This material was produced under grant number SH-29661-SH6 from OSHA. It does not necessarily reflect the views or policies of the U.S. Department of Labor, nor does mention of trade names, commercial products, or organizations imply endorsement by the U.S. Government.
Housekeeping Techniques

## Slide 328: Module 7: Housekeeping Techniques:
Terminal Objective
  Trainees will be able to identify appropriate housekeeping techniques to reduce risk of silica dust exposure.
Enabling Objective
  Identify general housekeeping techniques that are allowed and not allowed.
  Identify when housekeeping measures are inappropriate and/or ineffective.
  Identify appropriate alternatives to wet sweeping or HEPA vacuuming.
Notes: Instructor to review the Objectives with the students.
Terminal Objective
  Trainees will be able to identify appropriate housekeeping techniques to reduce risk of silica dust exposure
Enabling Objective
  Identify general housekeeping techniques that are allowed and not allowed
  Identify when housekeeping measures are inappropriate and/or ineffective
  Identify appropriate alternatives to wet sweeping or HEPA vacuuming.
  Advance to the next slide.

## Slide 329: Module 7 : Housekeeping Techniques:
All employers covered under the new Silica Standard must restrict housekeeping practices that expose employees to respirable crystalline silica where feasible alternatives are available.
Notes: Instructor shall review the Employer Responsibilities on housekeeping.
Employers covered under the new silica standard must restrict housekeeping methods that would expose employees to crystalline silica whenever feasible alternatives are available. We will speak on several methods that can be utilized during this process.
Advance to the next slide.

## Slide 330: Module 7 : Housekeeping Techniques:
The respirable crystalline silica standard requires all construction employers covered by the standard, including those who fully and properly implement the control methods specified in Table 1, to avoid certain housekeeping practices.
Notes: Instructor shall review the Employer Responsibilities on housekeeping using Table 1.
The silica standard requires construction employers covered by the standard to avoid certain housekeeping practices.
Advance to the next slide.

## Slide 331: Module 7 : Housekeeping Techniques:
Example:
Employees are dry sweeping in an area where brick were cut with a stationary saw late in the afternoon yesterday.
Is there a possible exposure hazards?
Notes: Instructor shall review the question on housekeeping with the students and get a general answer from the group:
Employees dry sweeping in an area where brick were cut with a stationary saw late in the afternoon yesterday. Is there a possible exposure hazards?
Yes, Dry sweeping can push the silica dust into the air and become respirable.
Advance to the next slide.

## Slide 332: Module 7 : Housekeeping Techniques:
Example:
Employees are dry sweeping in an area where brick were cut with a stationary saw late in the afternoon yesterday.
Is there a possible exposure hazards?
Yes
Notes: Instructor shall review the question on housekeeping with the students and get a general answer from the group:
Employees dry sweeping in an area where brick were cut with a stationary saw late in the afternoon yesterday. Is there a possible exposure hazards?
Yes, Dry sweeping can push the silica dust into the air and become respirable.
Advance to the next slide.

## Slide 333: Module 7 : Housekeeping Techniques:
When cleaning up dust that could contribute to employee exposure to respirable crystalline silica, employers must:
Not allow dry brushing or dry sweeping, unless methods such as wet sweeping and HEPA-filtered vacuuming are not feasible;
Not allow cleaning of surfaces or clothing with compressed air, unless the compressed air is used together with a ventilation system that effectively captures the dust cloud or no other cleaning method is feasible.
Notes: Instructor shall review the housekeeping exposure:
When cleaning up any dust that could contribute to an employee's exposure to crystalline silica the employer must, not allow dry brushing or sweeping, unless using a HEPA filtered vacuum or wet sweeping is infeasible. Also not allow cleaning of surfaces or clothing with compressed air, unless the compressed air is used together with ventilation system that effectively captures the dust cloud or other cleaning method.
Advance to the next slide.

## Slide 334: Module 7 : Housekeeping Techniques:
High-efficiency particulate air (HEPA) filter means a filter that is at least 99.7% efficient in removing mono-dispersed particles of 0.3 micrometers in diameter.
HEPA filtered vacuuming is an example of a housekeeping method that minimizes employee exposure to respirable crystalline silica, and some Table 1 task require HEPA-filtered vacuuming.
Notes: Instructor shall review the using HEPA filter vacuum systems in housekeeping to prevent exposure:
High-efficiency particulate air (HEPA) filter means a filter that is at least 99.7% efficient in removing mono-dispersed particles of 0.3 micrometers in diameter.
HEPA filtered vacuuming is an example of a housekeeping method that minimizes employee exposure to respirable crystalline silica, and some table 1 task require HEPA-filtered vacuuming.
Advance to the next slide.

## Slide 335: Module 7 : Housekeeping Techniques:
Dispose of used vacuum bags in a container and keep the container sealed.
Notes: Instructor shall review the use of vacuum bags in vacuum systems on housekeeping:
Dispose of used vacuum bags in a container and keep the container sealed. When removing dust bags from vacuum systems, the employee must open the system to be able to close the bag. During this period one of 2 methods must be used, either PPE that will protect the respiratory system, or by pulling water into the system to reduce the escape of dust when the system is opened. The problem with wetting the system is that the filters will need to be changed or dried before use.
Advance to the next slide.

## Slide 336: Module 7 : Housekeeping Techniques:
When employees are removing a bag from the HEPA vacuum system, should they wear PPE?
Notes: Instructor shall review the question on housekeeping with the students and get a general answer from the group:
When employees are removing a bag from the HEPA vacuum system, should they wear PPE?
Yes, moving the bag and closing it can push the silica dust into the air and become respirable.
Advance to the next slide.

## Slide 337: Module 7 : Housekeeping Techniques:
When employees are removing a bag from the HEPA vacuum system, should they wear PPE?
Yes
Notes: Instructor shall review the question on housekeeping with the students and get a general answer from the group:
When employees are removing a bag from the HEPA vacuum system, should they wear PPE?
Yes, moving the bag and closing it can push the silica dust into the air and become respirable.
Advance to the next slide.

## Slide 338: Module 7 : Housekeeping Techniques:
Cleaning methods such as dry sweeping, dry brushing, and use of compressed air can cause respirable crystalline silica dust to get into the air and be inhaled by employees.
Therefore, the silica standard limits the use of these cleaning methods to prevent unnecessary exposures to employees.
Notes: Instructor shall review the use of dry sweeping in housekeeping:
The use of cleaning methods such as dry sweeping, dry brushing, or the use of compressed air will cause christening silica to get into the air and be inhaled by employees. It's important to not use dry-cleaning methods in lesser no other alternatives. Employees that do use dry methods must use some form of respiratory protection.
Advance to the next slide.

## Slide 339: Module 7 : Housekeeping Techniques:
Employers are required to use other cleaning methods such as wet sweeping and HEPA filtered vacuums, whenever feasible.
These methods reduce employee exposures by preventing silica-containing dust from getting into the air.
Notes: Instructor shall review the use of wet sweeping and vacuum systems in housekeeping activities:
Cleaning methods such as wet sweeping and HEPA filter vacuums should be used whenever feasible.
Advance to the next slide.

## Slide 340: Module 7 : Housekeeping Techniques:
Example:
If you are cleaning a new construction project and the granite counter top was cut in the building.
- If there are new wood floors present, what is the best cleaning method to use to clean up the dust?
HEPA Vacuum
or alternate
*pictures obtained from www.sylvane.com
Notes: Instructor shall review the question on housekeeping with the students and get a general answer from the group:
If you are cleaning in a new construction project and the granite counter top was cut in the building. If there are new wood floors, what cleaning method can you use to clean up the dust?
HEPA Vacuum or alternate
.
Advance to the next slide.

## Slide 341: Module 7 : Housekeeping Techniques:
Feasibility of Cleaning Methods In a very limited number of cases, cleaning methods such as wet sweeping or HEPA filtered vacuums may not be safe or effective.
If these methods would cause damage, or would create a hazard in the workplace, the employer is not required to use these cleaning methods.
Notes: Instructor shall review the use flexible systems on housekeeping:
In very rare cases using wet sweeping or HEPA filtered vacuum may not be safe or effective, they might cause damage or would create a hazard in the workplace. If this is the case than the employers not required to use these cleaning methods according to the standard. An example of a situation where you could not do this might be in an explosive environment with other chemicals or substances that react to water..
Advance to the next slide.

## Slide 342: Module 7 : Housekeeping Techniques:
In cases where one of those cleaning methods may not be safe or effective, employers could often use another acceptable method for cleaning.
Example: if it is not feasible to wet sweep a wood floor because water would damage the wood or cause mold growth, a HEPA-filtered vacuum could be used for cleaning.
These situations are expected to be rare, which no acceptable cleaning methods can be used.
Notes: Instructor shall review the use of housekeeping methods to prevent exposure:
However, even in cases where one of those cleaning methods may not be safe or effective, employers could often use another acceptable method for cleaning. For example, if it is not feasible to wet sweep a wood floor because water would damage the wood or cause mold growth, a HEPA-filtered vacuum could be used for cleaning.
Therefore, situations in which no acceptable cleaning methods can be used are expected to be very rare.
Advance to the next slide.

## Slide 343: Module 7 : Housekeeping Techniques:
In those rare cases where the employer needs to use cleaning methods such as:
Dry sweeping;
Dry brushing or;
Compressed air.
The employer must be able to show why cleaning methods that decrease an employee exposure are not feasible.
Notes: Instructor shall review the use of housekeeping methods to prevent exposure:
In those rare cases where the employer needs to use cleaning methods such as dry sweeping, dry brushing, or compressed air, the employer must be able to show why cleaning methods that decrease employee exposures are not feasible.
Advance to the next slide.

## Slide 344: Module 7 : Housekeeping Techniques:
When Employers Must Follow Housekeeping Practices the housekeeping requirements in the silica standard apply only where cleaning
  “could contribute to employee exposure to respirable crystalline silica”.
This phrase clarifies that employers only have to follow the housekeeping requirements of the silica standard where employees could be exposed to the very small (respirable) crystalline silica particles created by high-energy tasks such as drilling, cutting, grinding, or crushing crystalline-silica-containing materials.
Notes: Instructor shall review the use of housekeeping methods to prevent exposure:
Employers must follow the housekeeping practices within the silica standard whenever there is silica that is respirable in the area that must be cleaned. These are areas where high-energy task of taken place.
Advance to the next slide.

## Slide 345: Module 7 : Housekeeping Techniques:
Employers are not required to follow these housekeeping requirements when cleaning:
  Ordinary soil;
  Large debris;
  Non-silica containing materials (i.e. such as sawdust)
Notes: Instructor shall review the requirements for housekeeping on non-silica materials:
Employers are not required to follow these housekeeping requirements when cleaning ordinary soil, large debris, and non-silica containing materials, such as sawdust.
Advance to the next slide.

## Slide 346: Module 7 : Housekeeping Techniques:
Is silica a flammable hazardous dust?
Notes: Instructor shall review the question on housekeeping with the students and get a general answer from the group:
Is silica a flammable hazardous dust?
No, silica is not flammable.
.
Advance to the next slide.

## Slide 347: Module 7 : Housekeeping Techniques:
Is silica a flammable hazardous dust?
No
Notes: Instructor shall review the question on housekeeping with the students and get a general answer from the group:
Is silica a flammable hazardous dust?
No, silica is not flammable.
.
Advance to the next slide.

## Slide 348: Module 7 : Housekeeping Techniques:
In the rare cases where conventional wet or HEPA vacuuming methods cannot be used, employees, must be protected by appropriate PPE if there is a potential to add to the exposure:
Dry sweeping;
Blowing;
Dusting;
Or other methods that might increase exposure to the employee.
Notes: Instructor shall review the use of housekeeping methods to prevent exposure:
In the rare cases where conventional wet or HEPA Vacuuming methods cannot be used employee must be protected by appropriate PPE meeting the requirements if there is a potential to add to the exposure form the method used.
Dry sweeping
Blowing
Dusting
Or other methods or other methods that might increase exposure to the employee
Advance to the next slide.

## Slide 349: Module 7 : Housekeeping Techniques:
If there are no engineering controls to prevent exposure when cleaning dry silica dust, what is the required PPE for respiratory protection?
N95 Respirator
Notes: Instructor shall review the question on housekeeping with the students and get a general answer from the group:
If there are no engineering controls to prevent exposure when cleaning dry silica dust, what is the require PPE for respiratory protection?
A N95 respirator would be required if there are no other control measures to prevent exposure.
.
Advance to the next slide.

## Slide 350: Module 7 : Housekeeping Techniques:
The proper PPE is at a minimum a NIOSH N95 respirator is to be used once s/he has been fit tested, trained and authorized by his/her employer, and also evaluated by a medical professional.
Notes: Instructor shall review the use PPE to prevent exposure in housekeeping:
The minimum NIOSH approved respirator would be the N-95 respirator that has been fit tested on the employee after he or she has been authorized, trained and evaluated by a medical professional to wear the respirator. This follows the respiratory protection standard.
Advance to the next slide.

## Slide 351: Module 7 : Housekeeping Techniques:
Written exposure control plans describe workplace exposures and ways to reduce those exposures such as;
  Engineering controls;
  Work practices;
  Housekeeping methods, and;
  Restricting access to areas where high exposures occur.
Notes: Instructor shall review the section on the written exposure control plants on housekeeping:
The written exposure control plan must describe the workplace exposures and ways to reduce the exposure. Things like engineering controls, work practice controls, housekeeping methods, and restricted access to areas where high exposures occur must be put in place to reduce those exposures.
Advance to the next slide.

## Slide 352: Module 7 : Housekeeping Techniques:
Housekeeping methods used must limit employee exposure to respirable crystalline silica.
While employees are cleaning, dust can become airborne and expose them to silica.
Notes: Instructor shall review the use of housekeeping methods that sill prevent exposure:
Housekeeping methods used must limit employee exposure to respirable crystalline silica. While employees are cleaning, dust can become airborne and expose them to silica.
Advance to the next slide.

## Slide 353: Module 7 : Housekeeping Techniques:
This image shows dust so deep on "I" beam flanges that it exceeds the angle-of-repose and is constantly falling into the general environment.
Cleaning of a facility on a regular basis will prevent buildup of dust. Spills of silica containing materials should be promptly cleaned up. Cleaning should employ methods which do not create dust (e.g., vacuuming, wet wash-down) rather than dust generating methods (e.g., sweeping, blowing).
Notes: Instructor shall review cleaning to prevent exposure:
In this image, it shows dust so deep on "I" beam flanges that it exceeds the angle-of-repose and is constantly falling into the general environment. Cleaning of a facility on a regular basis will prevent buildup of dust. Spills of silica containing materials should be promptly cleaned up. Cleaning should employ methods which do not create dust rather than dust generating methods.
Advance to the next slide.

## Slide 354: Module 7 : Housekeeping Techniques:
When using a vacuum system:
The vacuum system must have a capture bag to contain the silica dust.
When removing the bag employees must control the exposure to Silica dust and close the bag without creating an exposure by:
  Using a wet control method, or;
  Using proper PPE.
Bags of Silica dust must be disposed of in a controlled landfill or similar method.
Notes: Instructor shall review the use of vacuuming systems in housekeeping methods to prevent exposure:
When using a HEPA vac system that contained silica dust. It is best to use a bag system to make the removal of the silica dust easiest. When the bag is removed the employee must control the exposure to silica dust and close the bag without creating a exposure, by using a wet control method or using proper PPE.
Bags a silica dust must be disposed of in a controlled landfill or similar method. Following the federal, state, local guidelines. These controlled landfills are considered sanitary landfills they are lined.
Advance to the next slide.

## Slide 355: Module 7 : Housekeeping Techniques:
Exercise
Notes: Students are to practice cleaning up small simulated areas in groups.
Advance to the next slide.

## Slide 356: Module 7 : Housekeeping Techniques:
Students are to demonstrate the proper methods for cleaning an area with simulated silica dust.
  Wet method
  Wet Sweeping
  Dry HEPA Vacuuming
  Wet HEPA Vacuuming
Notes: Students are to demonstrate the proper methods for cleaning an area with simulated silica dust.
  Wet method – Spraying the area down with water and flushing the silica dust into a drain or natural area to remove the hazard
  Wet Sweeping – Adding water to an area and sweeping it to a control area.
  Dry HEPA Vacuuming – Use a HEPA vacuum to pick up the silica dust in an area and then removing the bag safely for disposal. Note PPE or water control will be required for this activity.
  Wet HEPA Vacuuming - Use a HEPA vacuum to pick up the silica dust and water in an area and then removing the bag safely for disposal.
Instructor is to provide guidance on each method and evaluate the students on the correct use of each method.
Advance to the next slide.

## Slide 357: Module 7 : Housekeeping Techniques:
  Summary:
  Identify appropriate housekeeping techniques to reduce risk of silica dust exposure.
  Identify general housekeeping techniques that are allowed and not allowed.
  Identify when housekeeping measures are inappropriate and/or ineffective.
  Identify appropriate alternatives to wet sweeping or HEPA vacuuming.
Notes:   The instructor will review the key points in the Summary students will be able to respond to each one;
  Summary:
  Identify appropriate housekeeping techniques to reduce risk of silica dust exposure
  Identify general housekeeping techniques that are allowed and not allowed
  Identify when housekeeping measures are inappropriate and/or ineffective
  Identify appropriate alternatives to wet sweeping or HEPA vacuuming
Advance to the next slide.

## Slide 358: Module 7 : Housekeeping Techniques:
  Any Questions?
Notes: Answer student questions, if any.
Students are to take the final test and the instructor shall grade and go over the results.